## Slide 1: Design Choices for Sensor Networks
Santhosh Prabhu, Mohammad Ahmad
Advanced Distributed Systems
CS 525

## Slide 2: Sensor Nodes
Tiny, self contained computers
Sensors to collect data
Used in coordinated sensing and monitoring
Deployed in inhospitable/unsafe environments
Relatively low cost, so somewhat expendable

## Slide 3: Example Hardware
Size
  Golem Dust: 11.7 cu. mm
  MICA motes: Few inches
Everything on one chip: micro-everything
  processor, transceiver, battery, sensors, memory, bus
  MICA: 4 MHz, 40 Kbps, 4 KB SRAM / 512 KB Serial Flash, lasts 7 days at full blast on 2 x AA batteries
Slide from Indy’s talk on Feb-6

## Slide 4: Design Challenges:
Energy Efficiency
Limited Resources
Fault Tolerance

## Slide 5: Design Challenges:
Energy Efficiency
Limited Resources
Fault Tolerance
}
In:
Operating Systems (TinyOS)
Communication (Directed Diffusion)
(Today’s Topics)

## Slide 6: Operating System for Sensor Networks

## Slide 7: TinyOS
Operating system designed for embedded devices
Emerged from UC Berkeley in 2000
  Sensor research was beginning
  Developed in nesC (a new C dialect)
Currently averages 25,000 downloads a year
  Worldwide community of developers and users

## Slide 8: Overview
Key design goals of TinyOS
  Resource minimization
  Bug prevention
What lessons can be drawn from the experience of the TinyOS development?

## Slide 9: Resource minimization
TinyOS software should use as few hardware resources as possible
  Trade off runtime flexibility for smaller code and data
Computationally efficient
  Minimizing cycle counts and wake time
Require little state
  Minimize RAM
Tight code
  Minimize ROM

## Slide 10: Microcontroller specification
TI MSP430 Microcontrollers

## Slide 11: Why resource minimization is important?
Energy
  Parts with more hardware draw more power both when awake and when asleep
  ‘every bit transmitted brings a sensor node one moment closer to death’
Cost
  Becomes significant for large scale use
  A $6 cut in price for 100,000 units leads to $600,000 in savings

## Slide 12: Prevention principle
In-field debugging of sensor networks in notoriously difficult
  Unknown input
  Unreliable wireless communication
  Limited resources make traditional debugging techniques (logging) unsuitable
TinyOS should be structured to make it harder to write bugs

## Slide 13: Approach
Pushed dynamic runtime operations into static compile time ones
  Evolved language primitives and abstractions to achieve this goal
Allowed for near optimal RAM usage and dependable software systems

## Slide 14: ROM and RAM Allocation
ROM minimization
  Inlining and dead code elimination
RAM minimization
  Goal for TinyOS: Want system calls to require as little RAM as possible
  Goal for traditional OS: Want to make system calls as fast as possible

## Slide 15: Example: RAM Minimization
Timer service
  32 bit timer requires 10 bytes of state
Pre-1.0
  Initial implementation maintained a linked list of timer structures
  Required an additional 2 bytes for the pointer (20% overhead)
V-1.0
  Allocate fixed array of timer structures
  nesC introduced ‘unique’ as a way of distinguishing between the timer structures
  Problem: Overprovisioning
V-1.1
  Introduced ‘uniqueCount’ which returns the number of times unique has been called with a particular string
  Allowed for minimum allocation of resources for timer structures
  Allocate exactly how much is required

## Slide 16: Isolation
TinyOS 1.x had poor isolation between components – shared memory pools
  Example: Packet transmission
  Components share queues so its possible for a badly behaving component to starve others
  Need to consider that any operation might fail, increasing ROM and RAM use
Concluded that shared memory pools violated the prevention principle and required more resources

## Slide 17: Static Virtualization
Static Virtualization
  Each component can declare a logical instance of a service
  Each component’s interaction to an underlying shared resource is completely independent
  Enables software to use an OS service isolated from all other users
  Compile time certainty

## Slide 18: What lessons can be drawn from the experience of TinyOS development ?

## Slide 19: Initial Users
How to get the initial users
  Promote use internally (Click modular router)
  Provide grants to work on the system
NEST project
  Made using TinyOS a requirement for grants
Advantages
  Moved project beyond UC Berkeley
Disadvantages
  Focusing on growth within research community led to more focus on technical complexity

## Slide 20: Language Co-design
Advantages:
  Flexibility to handle new problems
  nesC’s language features contributed to prevention and minimization
Disadvantages
  Barrier to entry
  Making it easier to solve hard problems made it harder to solve easy ones
  Staffing
Suggested Solution
  Split design and evolution efforts

## Slide 21: Modular Structure
Components are key to TinyOS design
Advantages:
  Structured so that it is easy to modify and extend
  Easy to verify small components
Disadvantages:
  Difficult to understand system for the first time
  Tiny pieces of functionality spread across files with different levels of indirection
  Overkill!
Solution
  Restructure as things stabilize

## Slide 22: Modular Structure

## Slide 23: Conclusion
Very successful as an academic project
  Averages 25,000 downloads a year
  Significant impact outside academia
Where is missed out
  Simple sensing applications
    Do it yourself
  Platform for the ‘internet of things’
    Connect sensors to the internet
    Contiki

## Slide 24: Communication in Sensor Networks

## Slide 25: Concerns
The pervasive concerns of energy/resource usage and fault tolerance
Limited control over the topology – Nodes are usually scattered randomly
Mobility of nodes – Nodes may be moved around
Real-time response requirement

## Slide 26: The first step: Routing Algorithms
Most approaches borrowed from the MANET world
Table driven (Proactive) Protocols:
  Each node keeps a list of destinations and the corresponding routes
  Example: DSDV
On-demand (Reactive) Protocols:
  Routes established when there is data to be sent
  Example: AODV

## Slide 27: The first step: Routing Algorithms
MANET Algorithms are not the way to go
Table driven (Proactive) Protocols:
  Periodic message exchanges
  Unnecessary memory usage
On-demand (Reactive) Protocols:
  Route setup required before transmitting data
They all separate communication from application

## Slide 28: Efficient routing protocols are good, but can we do better?
Can we use in-network aggregation to minimize communication overhead?
Can we achieve better fault tolerance with minimal reconfiguration?
How can application knowledge help us design better protocols?

## Slide 29: Directed Diffusion:
Data centric data dissemination paradigm
Named data in attribute-value pair format
Operator queries transformed into interests - Data requested by sending interests
Interests are diffused toward the nodes in a specific region
Upon interest reception, nodes collect data via their sensors and return it along the reverse path
Intermediate nodes might perform data aggregation

## Slide 30: Directed Diffusion: Benefits
Multi-path delivery for robustness
Application specific path selection
Adaptive choice of transmission rates
Aggregation reduces communication overhead
Nodes can be anonymous – Only local interactions, so no global identifiers required

## Slide 31: Directed Diffusion: Interests
Specification of a data-collection task, identified by attribute-value pairs
Any query is translated into an interest
type = wheeled vehicle // type of data to be collected
Interval=20ms //how frequently data needs to be sent
duration=10s //how long to monitor
rect=[-100,100,200,400] //area where monitoring is to be done

## Slide 32: Directed Diffusion: Interest Propagation
A node initiating a task (sink) injects interests into the network
Interests propagate by
  flooding
  geographic routing
  cache-based routing
Nodes receiving a new interest caches the interest and creates a gradient entry for the interest to the sender
Specifies:
  The node to which data matching the interest should be sent
  Data rate (intervals between data messages)
  Duration (Time at which gradient expires)

## Slide 33: Directed Diffusion: Gradients
Possibly multiple gradients per interest at node (when interest received from multiple neighbors)
Deleted after timeout duration
Can be updated by new interest messages
Interest deleted if no more gradients remain
Initial Gradients – Low data rate, exploratory

## Slide 34: Directed Diffusion: Gradients

## Slide 35: Directed Diffusion: Gradients

## Slide 36: Directed Diffusion: Gradients

## Slide 37: Directed Diffusion: Data Propagation
Nodes in the specified region set up sensors
Data collected at highest data rate among all gradients
Sends event description to neighbors with for whom gradients exist
            type = wheeled vehicle
            instance = truck
            location = [125,220]
            intensity = 0.6
            confidence = 0.85
            timestamp = 01:20:40

## Slide 38: Directed Diffusion: Data Propagation
Received data checked against a cache
New data cached and forwarded
Drop duplicates (prevents loops in forwarding)
Down-conversion: Data forwarded no faster than required

## Slide 39: Directed Diffusion: Reinforcement
Collect more information along better paths
Done by raising data rate with chosen neighbors
type = wheeled vehicle type = wheeled vehicle
Interval=20ms Interval=5ms
duration=10s duration=10s
rect=[-100,100,200,400] rect=[-100,100,200,400]
Options:
  Neighbor that sent data first
  Every neighbor that sent data recently
  Neighbors that consistently send new data
Choice determines what kind of path is favored
Notes: ----- Meeting Notes (3/13/14 00:10) -----
along better paths

## Slide 40: Directed Diffusion: Negative Reinforcement
Truncate undesirable paths
Done by:
  Timeouts
  Explicit negative reinforcement (low data rate interest)
Options:
  Consistently old events
  Ranking neighbors on number of new events received
Tradeoff between energy efficiency and fault tolerance

## Slide 41: Directed Diffusion: Reinforcement
Helps in local repairs
Removes loops
X

## Slide 42: Directed Diffusion: Experiments
Comparing Directed Diffusion with the alternatives:
  Flooding data from source to sink
  Omniscient Multicast: End to end communication along shortest path
ns-2 simulation
Increasing network size (in steps of 50)
Average node density kept constant

## Slide 43: Directed Diffusion: Energy use
Diffusion compared to flooding, Omniscient Multicast
Reduced communication due to aggregation
Average Energy (Joules/Node/Received Pkt)
Network Size

## Slide 44: Directed Diffusion: Delay
No global knowledge
But paths comparable to Omniscient Multicast
Empirical path selection with local decisions works well
Flooding suffers from collisions
Delay(secs)
Network Size

## Slide 45: Directed Diffusion: Failure Tolerance
Lower energy consumption under more failures!!
Unnecessary redundancy due to conservative reinforcement
Average Energy (Joules/Node/Received Pkt)
Network Size

## Slide 46: Discussion Points
Static virtualization does away with shared memory pools. Doesn’t this lead to resource wastage?
Could traditional protocols benefit from named data? (Question from CS525 Spring 2013)
  Content Delivery Networks
Would rebuilding TinyOS be worth it?

## Slide 47: Discussion Points
Picking the right data rate – A tradeoff between energy efficiency and event detection
Congestion free network assumed
Can aggregation slow down communication?
Complete knowledge should help in minimizing bugs anyway
Does caching in diffusion conflict with the idea with the RAM usage minimization?