## Slide 1: Exploring Energy-Latency Tradeoffs for Broadcasts in Energy-Saving Sensor Networks
Author:
Matthew J. Miller
Cigdem Sengul
Indranil Gupta
Presenter:
Wenyu Ren
Notes: Accepted by icdcs 2005

## Slide 2: Wireless Sensor Networks (WSNs)
Resources
Energy
CPU
Memory
vs.
Performance
Latency
Reliability
Notes: Here starts my presentation. In terms of wireless sensor networks, there are two major issues we need to consider: Resources and Performance.
Sensor nodes are inherently resource constrained. They have limited power of battery, CPU and Memory. And energy is the most important resource for battery-powered sensors.
On the other hand, latency and reliability are the two most commonly-used performance metrics.
However, it is obvious that offering better reliability and performance to a sensor network application leads to greater usage and depletion of the resources.
So there is always a resource-performance trade-off in WSNs.
Based on the different emphasis on the two aspects, sensor applications can be generally classified into two categories.

## Slide 3: Sensor Application Type 1
Code Update Application
  Updates Generated Once Every Few Weeks
  Reducing energy consumption is important
  Latency is not a major concern
Here is Patch #27

## Slide 4: Sensor Application Type 2
Short-Term Event Detection
E.g., Intruder Alert for Temporary Overnight Camp
Latency is critical
With adequate power supplies, energy usage is not a concern
Look For An Event With These Attributes

## Slide 5: Energy-Latency Relationship
Energy
Latency
Notes: To support a wide variety of future applications, sensor networking technologies will be required to provide enough flexibility for a designer to choose the appropriate operation point on the resource-performance spectrum. So studying the relationship between energy and latency is of great value.

## Slide 6: Broadcast in Sensor Networks
Flooding: a high number of redundant packets
SPIN: incorporate negotiation
Virtual Infrastructure
Gossip
Notes: This paper focuses on the broadcast problem. Broadcast is a fundamental communication primitive in sensor networks, which is useful to applications for disseminating sensor data, instructions, and code updates.
The usual approach to broadcast is by flooding the entire network. This, however, creates a high number of redundant packets.
The deficiencies of the classic flooding approach can be avoided in different ways.
SPIN protocols incorporate meta-data negotiations to eliminate the transmission of redundant data throughout the network.
Overlaying a virtual infrastructure over the underlying network can reduce the number of nodes involved in broadcasts.
Allowing each node to forward a message with some probability can also alleviate the problems with flooding. Work in this paper is most similar to this gossip type of approach.

## Slide 7: Sleep Scheduling Mechanism
Active-sleep Cycle
Divide time into frames
  Active time: send and receive messages
  Sleep time: radio in sleep mode to save energy
Examples
  IEEE 802.11 Power Save Mode (PSM)
  S-MAC/T-MAC
Notes: Before I move on to the work of this paper, I still have another thing to introduce.
Active-sleep cycle is one of the main MAC-layer approaches to reduce energy consumption in WSNs. It lets nodes sleep periodically. This paper mainly focuses on the active-sleep cycle approach.
The basic idea of introducing an active-sleep cycle to a contention-based protocol is to divide time into frames.
Each frame is divided into an active time and a sleep time. During the active time, a node can send and receive messages.
During the sleep time, a node puts its radio in sleep mode to save energy.
Examples of this kind of approaches includes:

## Slide 8: Broadcast in IEEE 802.11 PSM
A
N1
N2
N3
ATIM window
BI
D
A
D
A
D
BI
AW
A
= ATIM Pkt
D
= Data Pkt
N2
N1
N3
Notes: Here is a broadcast example for IEEE 802.11 PSM.
All nodes in the network are synchronized to wake up periodically to listen to beacon messages. Broadcast messages are first buffered at the transmitter and announced during the period when all nodes are awake.
The announcement is made via an ad hoc traffic indication message (ATIM) inside a small interval at the beginning of the beacon interval called the ATIM window.
If a node receives a directed ATIM frame in the ATIM window, it sends an acknowledgment and stays awake for the entire beacon interval waiting for data packets to be transmitted.
Immediately after the ATIM window, a node can transmit buffered data packets to nodes that are known to be active.
Otherwise, the node can switch to the low-power state to conserve energy.

## Slide 9: Extreme 1 (PSM)
A
N1
N2
N3
BI
D
A
D
A
BI
A
= ATIM Pkt
D
= Data Pkt
N2
N1
N3
Notes: Actually, PSM can be seen as one extreme in terms of protocol design. A data packet can only be transmitted if it is announced in the previous ATIM window and a node will always sleeps if no ATIM frame is received in the previous ATIM window.
In this design, to rebroadcast the message, a node must wait for the next ATIM window to guarantee that each node in its neighborhood receives the ATIM advertising the broadcast. This certainly increases the latency of the broadcasts.

## Slide 10: Extreme 2
A
N1
N2
N3
BI
D
D
BI
A
= ATIM Pkt
D
= Data Pkt
N2
N1
N3
D
Notes: Another extreme is that a node never sleeps and will rebroadcast a packet in the current beacon interval. This design has a lower latency but much higher energy consumption.

## Slide 11: Probability-Based Broadcast Forwarding (PBBF)
Goal
    with high probability, a node receives at least one copy of each broadcast packet, while reducing the latency due to sleeping
Two parameters: p and q
  p —— the probability that a node rebroadcasts a packet in the current active time despite the fact that not all neighbors may be awake to receive the broadcast
  q —— the probability that a node remains on after the active time when it normally would sleep
Notes: To address the resource-performance trade-off, this paper presents something in the middle, called Probability-Based Broadcast Forwarding (PBBF).
Its goal is to ensure that, with high probability, a node receives at least one copy of each broadcast packet, while reducing the latency due to sleeping.
PBBF introduces two new parameters: p and q.
The first parameter, p, is the probability that a node rebroadcasts a packet in the current active time despite the fact that not all neighbors may be awake to receive the broadcast.
The second parameter, q, represents the probability that a node remains on after the active time when it normally would sleep.

## Slide 12: PBBF Example
N1
N2
N3
ID
ID
A
D
A
= ATIM Pkt
D
= Normal Broadcast
N2
N1
N3
w/ Pr=q
w/ Pr=p
w/ Pr=(1-q)
w/ Pr=q
w/ Pr=(1-p)
w/ Pr=p
ID
= Immediate Broadcast
Notes: Here is an example for PBBF.
Node 1 has a broadcast message to send after the first ATIM window. Using the p parameter, Node 1 decides to send the message immediately instead of waiting for the second window to announce it.
Therefore, only Node 3, which tossed a coin and decided to stay awake after the first ATIM window based on the q parameter, receives the message.
On reception of the message, Node 3 decides to rebroadcast via a normal broadcast and, therefore, waits for the second ATIM window to guarantee that each node in its neighborhood receives the broadcast.
Hence, Node 2 is able to receive the message this time and decides to rebroadcast it immediately.

## Slide 13: PBBF Characteristics
p = 0 and q = 0: The original sleep scheduling protocol
p = 1 and q = 1: Approximation of the always-on mode
p: latency vs. reliability
q: energy vs. reliability
Effects of p and q on energy, latency and reliability:
 | Energy | Latency | Reliability
p ↑ | --- | ↓ if q > 0 | ↓ if q < 1
q ↑ | ↑ | ↓ if p > 0 | ↑ if p > 0
Notes: The original sleep scheduling protocol is a special case of PBBF with p = 0 and q = 0. The always-on mode can be approximated by setting p = 1 and q = 1.
Through the use of two parameters, p and q, PBBF protocol provides a trade-off between energy, latency, and reliability.
While p presents a trade-off between latency and reliability, q presents a trade-off in terms of energy and reliability.
As p increases, latency decreases while the fraction of nodes not receiving a broadcast increases (unless q = 1).
As q increases, energy consumption increases, but the fraction of nodes receiving a broadcast increases (unless p = 0).

## Slide 14: Analytical Results: Reliability
Bond (edge) percolation model
  pedge: probability that an edge between two vertices is open
Phase 1
Phase 0
Notes: After presenting the PBBF protocol, the paper analyzes the protocol in terms of reliability, energy and latency.
The reliability of PBBF protocols can be analyzed using percolation models. PBBF’s reliability is characterized by a bond percolation model.
In this model, an edge between two vertices is open with the probability p edge.
A phase transition occurs when the probability of an edge between two vertices is greater than the critical value. In this phase, the probability that an infinitely large cluster exists in a graph is close to one.
Another phase transition occurs when p edge is less than the critical value. In this phase, the probability that an infinitely large cluster exists in the graph is close to zero.

## Slide 15: Analytical Results: Reliability
The probability that a broadcast is received on a link A → B is:
pedge = pq + (1-p)
pq + (1-p) > pcritical
every broadcast reaches most of the nodes in the network
Immediate
broadcast of A
B being
awake
Rebroadcast
when B is awake
Notes: In PBBF, if a node A receives the broadcast message, the probability that a given neighbor, B, of A receives a copy of the message via the link A → B is p · q + (1 − p).
The first term arises from the likelihood of A broadcasting the message immediately after reception and that B being awake at the time. The second term is simply the likelihood of a rebroadcast when B is awake.
Then, each (directed) edge in the network is open with this probability. Thus, if this probability is greater than the critical value, then every broadcast reaches most of the nodes in the network according to the percolation theory.

## Slide 16: Analytical Results: Reliability
q
p=0.25
p=0.37
p=0.5
p=0.75
Fraction of Broadcasts
Received by 99% of Nodes
Notes: Here is the PBBF’s reliability using an ideal simulator by varying q while keeping p fixed. The ideal simulator assumes an ideal MAC and physical layer with no collisions or interference.
As shown in the figure, threshold behavior is observed. For sufficiently large values of p, none of the broadcasts achieve a desired reliability when q is small.
However, at some threshold q value, the reliability metric rapidly increases to where every broadcast is received by the specified fraction of nodes.
This is similar to the critical probability behavior shown in percolation theory.

## Slide 17: Analytical Results: Energy
Notes: To analyze the energy consumption of PBBF, the paper uses E original to denote the relative energy consumption of a sleep scheduling protocol compared to a protocol with no energy-saving. It can be written as:
The increased energy consumption due to the q parameter compared to original sleep scheduling protocol is:
The simulation results verify the analytical result given in the equation.
While using PSM saves almost 3 Joules per update over using no PSM, the energy consumption of PBBF increases linearly with the q parameter, and does not depend on p at all.

## Slide 18: Analytical Results: Latency
L: the expected time between A sending the broadcast and B receiving it from A
L1: time to immediately transmit the data packet
L2: time to wake up all neighbors for the broadcast
LS,B: the latency from the source S to the node B
len(S, B): average length (in terms of hop count) of the path from S to B
Notes: The analysis of latency will also introduce some definitions.

## Slide 19: Analytical Results: Latency
Increasing p
Notes: This figure shows variation of per-hop latency versus q.
As q increases, which means broadcasts reach more nodes, higher p values achieve lower latency as nodes do not need to wait until the next beacon interval to broadcast the message.

## Slide 20: Analytical Results: Latency
q
Average 60-Hop
Flooding Hop Count
p=0.37
p=0.75
Increasing Reliability
Notes: This figure shows variation of average 60-hop flooding hop count versus q.
We can see that when the reliability is high, the average length of the path from S to B is equal to the shortest distance between S and B.
This is because the fraction of nodes receiving the broadcast is very high with high reliability, this means the message is likely to propagate along the shortest path from the source S to the node B.

## Slide 21: Analytical Results: Energy-Latency Tradeoff
Joules/Broadcast
Average Per-Hop Broadcast Latency (s)
Achievable region
for reliability
≥ 99%
Set the values of p and q so that they are just across the reliability threshold boundary and into the high reliability region
Tune these values (staying close to the boundary) until the desired energy-latency trade-off is achieved
Notes: Based on the equations of energy and latency, we can derive the direct relation between energy, EPBBF, and latency, L, like this.
The energy consumed at a node increases linearly with q and the latency is inversely related to q (and also p). Thus, the energy and latency are inversely related to each other in the PBBF protocol.
The threshold behavior of the PBBF protocols allows an application designer to first set the values of p and q so that they are just across the reliability threshold boundary and into the high reliability region, which is the shadowed region in the figure.
Secondly, it allows application designers to tune these values while staying close to the boundary until the desired energy-latency trade-off is achieved.

## Slide 22: Simulation Results
Simulated code distribution application in ns-2 network simulator
Parameter | Value | Parameter | Value
N | 50 | Tframe | 10 s
PTX | 81 mW | Tactive | 1 s
PI | 30 mW | q | 0.25
PS | 3 µW | ∆ | 10.0
λ | 0.01 packets/s | Total Packet Size | 64 bytes
L1 | ≈ 1.5 s | Data Packet Payload | 30 bytes
Notes: The authors implemented PBBF on top of IEEE 802.11 PSM and compare it with regular PSM using the ns-2 network simulator.
They implemented an application to simulate code distribution in a sensor network. One random node is chosen to be the base station which periodically sends patches for sensors to apply.

## Slide 23: Simulation Results: Energy
Energy
Joules/Broadcast
q
PBBF
Notes: This figure shows how the average energy consumed at a node changes with q. The energy is normalized for the number of updates generated,.
We can see that using PSM saves almost 2 Joules per update over using no PSM.
The figure also shows that energy increases linearly with the q value.
We also observe that q dominates p in the energy usage because the PBBF lines overlap regardless of the p value.

## Slide 24: Simulation Results: Latency
Latency
Average 5-Hop Latency
Increasing p
q
Notes: This figure shows the average latency of nodes that are five hops from the source.
We can see that PSM consistently has a high latency, whereas turning PSM off results in a much lower latency.
PBBF does worse than PSM at small values of q, but improves significantly as q and p increase.
This is because when q is small, it is more likely that a node will not receive the broadcast from the neighbor which would result in the smallest latency.
However, as q and p get larger, there is a greater chance a broadcast will be transmitted and received without waiting for the next beacon interval, which results in the decrease of latency.

## Slide 25: Simulation Results: Reliability
q
Average Fraction of
Broadcasts Received
p=0.5
Notes: This figure illustrates how the q value affects the fraction of updates a node receives.
We observe that setting p = 0.5 results in a significant degradation until q reaches about 0.5.
For p = 0.25, there is a little degradation and all the other p values result in very little loss.

## Slide 26: Conclusion
Have presented, analyzed, simulated, and measured the performance of a class of probabilistic broadcast protocols for multi-hop WSNs.
Have quantified the energy-latency trade-off required to obtain a given level of reliability using PBBF.
Have implemented the PBBF protocols in ns-2 and have studied the performance characteristics of PBBF when used for code distribution.
Experiments indicate that PBBF is an efficient broadcast mechanism in the sense that it provides an application designer the opportunity to tune the system to an appropriate operating point along the reliability resource-performance spectrum.
Notes: In this paper, the authors have presented, analyzed, simulated, and measured the performance of a class of probabilistic broadcast protocols for multi-hop WSNs.
They have quantified the energy-latency trade-off required to obtain a given level of reliability using PBBF.
This is facilitated by allowing an application designer to tune the values of parameters p and q while maintaining the value of 1 − p · (1 − q) above the threshold required to achieve very high reliability.
The authors have also implemented the PBBF protocols in ns-2 and have studied the performance characteristics of PBBF when used for code distribution.
Experiments indicate that PBBF is an efficient broadcast mechanism in the sense that it provides an application designer the opportunity to tune the system to an appropriate operating point along the reliability resource-performance spectrum.

## Slide 27: Discussion
Pros:
PBBF can be used in conjunction with any sleep scheduling protocol
Provides theoretical explanation as well as simulation results
Cons:
Perfect synchronization assumption is not valid
No real deployment of PBBF
Notes: Pros:
PBBF can be used in conjunction with any sleep scheduling protocol. For example, it can be easily integrated into IEEE 802.11 PSM. This gives PBBF great adaptability and makes it highly deployable.
This paper provides a explanation of the energy-latency trade-off in WSNs broadcasting from a theoretical aspect as well as thorough simulation results to quantify the trade-off. This is essential to delineate trade-off knobs for the application designer.
Cons:
This paper assumes perfect synchronization in the WSN when conducting the simulation. As a matter of fact, it is difficult, and in most cases impossible, to achieve perfect synchronization among cooperative transmitters especially for low-cost, small-sized transmitters, such as sensors. Synchronization is difficult because parameters of electronic components may be drifting and because making handshaking among transmitters is as infrequently as possible to save energy.
Another con of the paper is that it does not present a real deployment of the PBBF protocol and thus lack practical experiment results on real testbed. The paper will be more convincing if testbed based results are provided.

## Slide 28: Thank You