## Slide 1: IEEE Workshop Series: EAGLE Workshop

## Slide 2
Why EAGLE?
FREE for students :)
Most seamless transition from Design->Schematic->Layout->Board
Integrates easily with Autodesk software

## Slide 3
Presentation Outline
Main Presentation:
Schematic Editor
  Basic tools
PCB Layout
  Design considerations
Ordering the PCB
  What’s a Gerber file?
Additional info
Adding custom part footprints to EAGLE

## Slide 4
Schematic
Editor

## Slide 5
Schematic Editor Tools – Basic Overview
Select, Move, Flip, and Rotate
Copy, Paste, Delete, Edit, and Add
Name, Value, and Smash
Adding shapes and text
Connecting parts

## Slide 6
Some Tool Tips
Name vs. value
Show tool vs. moving

## Slide 7
Some General Tips
Inputs on left, outputs on right.
Modularize
Keep them clean and legible!
  - Avoid crossed wires at all costs
  - Label nets, parts, and sections
  - Make “tunnels” if you have to
  - Order/connect things consistently

## Slide 8
Board
Layout

## Slide 9
First Step: Set Your Design Rules!
Know what your fabricator can do
- Minimum drill size, trace width, tolerances on sizes
- Set minimum distance rule accordingly
Know how much current each signal will carry
- This can vary based on your maximum temperature rise
- Set minimum trace width accordingly

## Slide 10
Board Layout Tools – Basic Overview
Mirror
Route and un-route
Add vias
Ratsnest

## Slide 11
General Design Guides
Tolerances! (again)
  - Always design around the maximum tolerances if you can
Avoid right angles
- Mutual inductance and signal coupling are board killers
Consider how the parts will solder
- Trying to solder a small part surrounded by big parts is not fun
Add planes for ground and power, if space permits

## Slide 12
Ordering the PCB

## Slide 13
Generate Gerber Files
Common Gerber files (RS-274X)
Each one is a vector file that serves as instructions for the manufacturer
Make sure to include those drill files!
CAM Processor -> Open Job -> gerb274x.cam AND excellon.cam
Extension | Function
.gbr | Generic file
.gtl/.gbl | Top/bottom copper layers
.gto/.gbo | Top/bottom silkscreen layers
.gts/.gbs | Top/bottom soldermask layers
.drl/.txt | Drill file(s)
.oln | Board outline

## Slide 14
Custom Parts

## Slide 15
Steps of Creation
Read those datasheets!
Draw a schematic and add pins
Draw a layout and add pads
Connect the pins and pads
For step-by-step tutorial, look at learn.sparkfun.com/tutorials

## Slide 16
Questions?