## Slide 1: ECE 530 – Analysis Techniques for Large-Scale Electrical Systems
Prof. Hao Zhu
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
haozhu@illinois.edu
11/9/2015
Lecture 19: Least-Squares Method

## Slide 2: Announcements
Homework 5 due Nov 11 in class
Final exam scheduled for the afternoon of Dec. 14

## Slide 3: Least Squares
So far we have considered the solution of Ax = b in which A is a square matrix; as long as A is nonsingular there is a single solution
  That is, we have the same number of equations (m) as unknowns (n)
Many problems are overdetermined in which there more equations than unknowns (m > n)
  Overdetermined systems are usually inconsistent, in which no value of x exactly solves all the equations
Underdetermined systems have more unknowns than equations (m < n); they never have a unique solution but are usually consistent

## Slide 4: Method of Least Squares
The least squares method is a solution approach for determining an approximate solution for an overdetermined system
If the system is inconsistent, then not all of the equations can be exactly satisfied
The difference for each equation between its exact solution and the estimated solution is known as the error
Least squares seeks to minimize the sum of the squares of the errors
Weighted least squares allows differ weights for the equations

## Slide 5: Least Squares Problem
Consider , where , ,
or

## Slide 6: Least Squares Solution
We write (ai)T for the row i of A and ai is a column vector
Here, m ≥ n and the solution we are seeking is that which minimizes , where p denotes some specific vector norm
Since usually an overdetermined system has no exact solution, the best we can do is determine an x that minimizes the desired norm.

## Slide 7: Example 1: Choice of p
We discuss the choice of p in terms of a specific example
Consider the equation Ax = b with
Hence three equations and one unknown
We will consider three possible choices for p

## Slide 8: Example 1: Choice of p
(i) p = 1
(ii) p = 2
(iii) p = 

## Slide 9: The Least Squares Problem
In general, is non-differentiable for p = 1 or p = ∞
The choice of p = 2 has become well established and given the least-squares fit interpretation
We next motivate the choice of p = 2 by first considering the least–squares problem

## Slide 10: The Least Squares Problem
The problem
is tractable for 2 major reasons
(i) the function
is differentiable in x ; and

## Slide 11: The Least Squares Problem
(ii) the norm is preserved under orthogonal transformations:
with Q an arbitrary orthogonal matrix; that is, Q satisfies

## Slide 12: The Least Squares Problem
We introduce next, the basic underlying assumption:
A is of full (column) rank, i.e., the columns of A
constitute a set of linearly independent vectors
This assumption implies that the rank of A is n because n ≤ m since we are dealing with an overdetermined system
Fact: The least squares problem solution x* satisfies

## Slide 13: Proof of Fact
Since by definition the least squares solution x* minimizes at the optimum, the derivative of this function vanishes:

## Slide 14: Implications
This underlying assumption implies that
A is full column rank
Therefore, the fact that
ATA is positive definite (p.d.)
follows from considering any x ≠ 0 and evaluating
which is the definition of a p.d. matrix
We use the shorthand ATA 0 for ATA being a symmetric, positive definite matrix

## Slide 15: Implications
The underlying assumption that A is full rank and therefore ATA is p.d. implies that there exists a unique least squares solution
Note: we use the inverse in a conceptual, rather than a computational, sense
The below formulation is known as the normal equations, with the conceptual solution as its unique solution

## Slide 16: Implications
An important implication of positive definiteness is that we can factor ATA since ATA 0
The expression ATA = GTG is called the Cholesky factorization of any symmetric p.d. matrix ATA

## Slide 17: Least Squares Solution Algorithm
  Step 1: Compute the lower triangular part of ATA
  Step 2: Obtain the Cholesky Factorization
  Step 3: Compute
  Step 4: Solve for y using forward substitution in
  and for x using backward substitution in

## Slide 18: Practical Considerations
The two key problems that arise in practice with the triangularization procedure are:
  While A maybe sparse, ATA is much less sparse and consequently requires more computing and storage resources for the solution
  ATA may be numerically less well-conditioned than A
18

## Slide 19: Example 2: Loss of Sparsity
Assume the B matrix for a network is
Then BTB is
Second neighbors are now connected! But large networks are still sparse, just not as sparse

## Slide 20: Numerical Conditioning
To understand the numerical ill-conditioning issue, we need to introduce terminology
We define the norm of a matrix to be

## Slide 21: Numerical Conditioning
i.e., li is a root of the polynomial
In words, the norm of matrix B is the square root of the largest eigenvalue of BTB

## Slide 22: Numerical Conditioning
The conditioning number of a matrix B is defined as
A well–conditioned matrix has a small value of
, close to 1
The larger the value of is, the more pronounced the ill-conditioning is
The ill-conditioned nature of ATA may severely impact the accuracy of the computed solution

## Slide 23: Example 3: Ill-Conditioned ATA
We illustrate the fact that an ill-conditioned matrix ATA results in highly sensitive solutions of least-squares problems in this example with then

## Slide 24: Example 3: Ill-Conditioned ATA
We introduce a “noise” in A to be the matrix dA

## Slide 25: Example 3: Ill-Conditioned ATA
This “noise” leads to the error E in the computation
of ATA with
Let and assume that there is no “noise” in , i.e.,

## Slide 26: Example 3: Ill-Conditioned ATA
The resulting error in solving the normal equations is independent of since it is caused purely by and
Let x be the true solution of the normal equations

## Slide 27: Example 3: Ill-Conditioned ATA
Let be the solution of the system with the error arising due to , i.e., the solution of
Therefore,

## Slide 28
Therefore, the relative error is
Now, the conditioning number
and
So the product approximates the relative error
Example 3: Ill-Conditioned ATA

## Slide 29
Thus the conditioning number is a major contributor to the error in the least-squares solution
In other words, the sensitivity of the solution to any system error, be its data entry or of a numerical nature, is very dependent on
Example 3: Ill-Conditioned ATA

## Slide 30
With the previous background we proceed to the typical schemes in use for solving least squares problems, all along paying adequate attention to the numerical aspects of the solution approach
If the matrix is full, then often the best solution approach is to use a singular value decomposition (SVD), to form a matrix known as the pseudo-inverse of the matrix
  We'll cover this later after first considering the sparse problem
We first review some fundamental building blocks and then present the key results useful for the sparse matrices common in state estimation
Solving the Least-Squares Problem