Discussion Section: Week 10 (Solutions)

Problem 1:

Consider a system in which the memory has the following hole sizes in the following memory order:

1KB,  4 KB, 15 KB, 20 KB, 4 KB, 7 KB, 18 KB, 12 KB, 15 KB, 9 KB

You are given successive requests for program segments in the following order:

10 KB, 5 KB, 3 KB, 2 KB, 19 KB, 9 KB, 24 KB, 10 KB.

For each of the following algorithms, show how the holes get filled for each of the above requests. If a particular request cannot be satisfied, you can skip it (but do mention which ones cannot be satisfied):

- First fit:

10 KB: 1, 4, 5, 20, 4, 7, 18, 12, 15, 9

5 KB: 1, 4, 20, 4, 7, 18, 12, 15, 9

3 KB: 1, 1, 20, 4, 7, 18, 12, 15, 9

2 KB: 1, 1, 18, 4, 7, 18, 12, 15, 9

19 KB: Can’t fit

9 KB: 1, 1, 9, 4, 7, 18, 12, 15, 9

24 KB: Can’t fit

10 KB: 1, 1, 9, 4, 7, 8, 12, 15, 9

- Best fit:

10 KB: 1, 4, 15, 20, 4, 7, 18, 2, 15, 9

5 KB: 1, 4, 15, 20, 4, 2, 18, 2, 15, 9

3 KB: 1, 1, 15, 20, 4, 2, 18, 2, 15, 9

2 KB: 1, 1, 15, 20, 4, 18, 2, 15, 9

19 KB: 1, 1, 15, 1, 4, 18, 2, 15, 9

9 KB: 1, 1, 15, 1, 4, 18, 2, 15

24 KB: Can’t fit

10 KB: 1, 1, 5, 1, 4, 18, 2, 15

- Worst fit:

10 KB: 1, 4, 15, 10, 4, 7, 18, 12, 15, 9

5 KB: 1, 4, 15, 10, 4, 7, 13, 12, 15, 9

3 KB: 1, 4, 12, 10, 4, 7, 13, 12, 15, 9

2 KB: 1, 4, 12, 10, 4, 7, 13, 12, 13, 9

19 KB: Can’t fit

9 KB: 1, 4, 12, 10, 4, 7, 4, 12, 13, 9

24 KB: Can’t fit

10 KB: 1, 4, 12, 10, 4, 7, 4, 12, 3, 9

- Next fit:

10 KB: 1, 4, 5, 20, 4, 7, 18, 12, 15, 9

5 KB: 1, 4, 20, 4, 7, 18, 12, 15, 9

3 KB: 1, 4, 17, 4, 7, 18, 12, 15, 9

2 KB: 1, 4, 15, 4, 7, 18, 12, 15, 9

19 KB: Can’t fit

9 KB: 1, 4, 6, 4, 7, 18, 12, 15, 9

24 KB: Can’t fit

10 KB: 1, 4, 6, 4, 7, 8, 12, 15, 9

Problem 2:

For each of the following decimal virtual addresses, compute the virtual page number and offset for a 4 KB page and for and 8 KB page: 20000, 32768, 60000.

4 KB = 2^12 B
8 KB = 2^ 13 B

| Address | Page Number (4KB) | Offset (4KB) | Page Number (8KB) | Offset (8KB) |
| --- | --- | --- | --- | --- |
| 20000 | 4 | 3616 | 2 | 3616 |
| 32768 | 8 | 0 | 4 | 0 |
| 60000 | 14 | 2656 | 7 | 2656 |

Problem 3:

Consider the page table of the figure. Give the physical address corresponding to each of the following virtual addresses:

- 29: Physical address: 8K + 29 = 8221

- 4100: Physical address: 4K + (4100 – 4K) = 4100

- 8300: Physical address: 24K + (8300 – 8K) = 24684

Problem 4:

A machine has 48 bit virtual addresses and 32 bit physical addresses. Pages are 8 KB. How many entries are needed for the page table?

Page size = 8 KB = 2^13 B
Offset = 13 bits
# of virtual pages = 2^(48 – 13) = 2^35 = # of entries in page table

Problem 5:

Consider a machine such as the DEC Alpha 21064 which has 64 bit registers and manipulates 64-bit addresses. If the page size is 8KB, how many bits of virtual page number are there? If the page table used for translation from virtual to physical addresses were 8 bytes per entry, how much memory is required for the page table and is this amount of memory feasible?

Page size = 8 KB = 2^13 B
Offset = 13 bits
Bits for virtual page number = (64 – 13) = 51
# of page table entries = 2^51
Size of page table = 2^51 * 8 B =2^54 B = 2^24 GB

Problem 6:

A computer with a 32-bit address uses a two-level page table. Virtual addresses are split into 9-bit top-level page table field, an 11 bit second-level page table field, and an offset. How large are the pages and how many are there in the address space?

Offset = 32 – 9 – 11 = 12 bits
Page size = 2^12 B = 4 KB
Total number of pages possible = 2^9 * 2^11 = 2^20

Problem 7:

Fill in the following table:

| Virtual Address (bits) | Page Size | # of Page Frames | # of Virtual Pages | Offset Length (bits) | Addressable Physical Memory |
| --- | --- | --- | --- | --- | --- |
| 16 | 256 B = 2^8 | 2^2 | 2^8 | 8 | 2^10 = 1 KB |
| 32 | 1 MB = 2^20 | 2^4 | 2^12 | 20 | 2^24 = 16 MB |
| 32 | 1 KB = 2^10 | 2^8 | 2^22 | 10 | 2^18 = 256 KB |
| 64 | 16 KB = 2^14 | 2^20 | 2^50 | 14 | 2^34 = 16 GB |
| 64 | 8 MB = 2^23 | 2^16 | 2^41 | 23 | 2^39 = 512 GB |

Problem 8:

Fill in this table with the correct page evictions. Physical memory contains 4 pages.

| Page Accesses | 0 | 1 | 2 | 3 | 4 | 1 | 3 | 4 | 4 | 5 | 3 | 1 | 2 | 0 | 4 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Optimal | - | - | - | - | 0 | - | - | - | - | 4 | - | - | - | 3 | 2 | - | - |
| FIFO | - | - | - | - | 0 | - | - | - | - | 1 | - | 2 | 3 | 4 | 5 | 1 | - |
| LRU | - | - | - | - | 0 | - | - | - | - | 2 | - | - | 4 | 5 | 3 | 1 | - |
| LFU | - | - | - | - | 0 | - | - | - | - | 2 | - | - | 5 | 2 | - | 0 | - |
| MRU | - | - | - | - | 3 | - | 1 | - | - | 4 | - | 3 | - | - | 0 | - | - |