## Slide 1: Networking
CS425 / CSE424 / ECE428 — Fall 2011 — Distributed Systems
Some material derived from slides by I. Gupta, K. Nahrstedt, S. Mitra, N. Vaidya, M.T. Harandi, J. Hou

## Slide 2
The Internet (Internet Mapping Project, color coded by ISPs)
PCs,routers,
switches…
=nodes
links=
edges
Notes: Mercator map

## Slide 3: Routing
Routing algorithms
  Link state
  Distance Vector

## Slide 4: Interplay between routing and forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 5: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Remark: Graph abstraction is useful in other network contexts
Example: P2P, where N is set of peers and E is set of TCP connections

## Slide 6: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path

## Slide 7: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 8: Link State Routing
A router broadcasts a link-state-advertisement (LSA) packet after booting, as well as periodically (or upon topology change). Packet forwarded only once, TTL-restricted
Initial TTL is very high.

## Slide 9: Link State Routing
Each router must
  Discover its neighbors and learn their network addresses
    When a router is booted up, it learns who its neighbors are by sending a special Hello packet on each point-to-point link.
    The router on the other end sends back a reply.
  Measure the delay or cost to each of its neighbors
    A router sends a special Echo packet over the link that the other end sends back immediately. By measuring the round-trip time, the sending router gets a reasonable delay estimate.
  Construct a packet telling all it has just learned.
    Broadcast this packet

## Slide 10: Link State Routing
Broadcast the LSA packet to all other routers.
  Each packet contains a sequence number that is incremented for each new LSA packet sent.
  Each router keeps track of all the (source router, sequence) pairs it sees. When a new LSA packet comes in, it is checked against the pairs. If the received packet is new, it is forwarded on all the links except the one it arrived on.
  The age of each packet is included and is decremented once per time unit. When the age hits zero, the information is discarded. Initial age = very high
For routing a packet, since the source knows the entire network graph, it simply computes the shortest path (actual sequence of nodes) locally using the Dijkstra’s algorithm. It can include the path in the packet, and intermediate nodes simply follow this route to decide their next hop for the packet.

## Slide 11: Distance Vector Algorithm (1)
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv(y) }
where min is taken over all neighbors of x

## Slide 12: Bellman-Ford example (2)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
B-F equation says:

## Slide 13: Distance Vector Algorithm (3)
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost to each neighbor v: c(x,v)
Node x maintains Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 14: Distance vector algorithm (4)
Basic idea:
Each node periodically sends its own distance vector estimate to neighbors
When node a node x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converge the actual least cost dx(y)

## Slide 15: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost of msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
Each node:

## Slide 16
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u’s DV
u | 0
v | 2
w | 5
x | 1
y | ∞
z | ∞
v’s DV
u | 2
v | 0
w | 3
x | 2
y | ∞
z | ∞
w’s DV
u | 5
v | 3
w | 0
x | 3
y | 1
z | 5
x’s DV
u | 1
v | 2
w | 3
x | 0
y | 1
z | ∞
y’s DV
u | ∞
v | ∞
w | 1
x | 1
y | 0
z | 2
z’s DV
u | ∞
v | ∞
w | 5
x | ∞
y | 2
z | 0

## Slide 17
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u’s DV
u | 0
v | 2
w | 5
x | 1
y | ∞
z | ∞
v’s DV
u | 2
v | 0
w | 3
x | 2
y | ∞
z | ∞
w’s DV
u | 5
v | 3
w | 0
x | 3
y | 1
z | 5
x’s DV
u | 1
v | 2
w | 3
x | 0
y | 1
z | ∞
y’s DV
u | ∞
v | ∞
w | 1
x | 1
y | 0
z | 2
z’s DV
u | ∞
v | ∞
w | 5
x | ∞
y | 2
z | 0
u’s updated DV
u | 
v | 
w | 
x | 
y | 
z | 
2
3+5
1+2
2
5
3+2
1+3
4

## Slide 18: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
At time t0, y detects the link-cost change, updates its DV,
and informs its neighbors.
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.

## Slide 19: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes
Poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
x
z
1
4
50
y
60

## Slide 20: Count-to-infinity Problem
x
z
1
4
50
y
60
y | 4
z | 5
x’s DV
x | 4
z | 1
y’s DV
x | 5
y | 1
z’s DV
dist=60
dist=5+1

## Slide 21: Count-to-infinity Problem
x
z
1
4
50
y
60
y | 4
z | 5
x’s DV
x | 6
z | 1
y’s DV
x | 5
y | 1
z’s DV
dist=50
dist=6+1

## Slide 22: Count-to-infinity Problem
x
z
1
4
50
y
60
y | 4
z | 5
x’s DV
x | 6
z | 1
y’s DV
x | 7
y | 1
z’s DV
dist=60
dist=7+1

## Slide 23: Poisoned Reverse
x
z
1
4
50
y
60
y | 4
z | 5
x’s DV
x | 4
z | 1
y’s DV
x | 5
y | 1
z’s DV
dist=60
dist=∞+1

## Slide 24: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 25: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  routers typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 26: IP networks
Address has 2 components
  Network (high-order bits)
  Host (low-order bits)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 27: IPv4 Address Model
Class | Network ID | Host ID | # of Addresses | # of Networks
A | 0 + 7 bit | 24 bit | 224-2 | 126
B | 10 + 14 bit | 16 bit | 65,536 - 2 | 214
C | 110 + 21 bit | 8 bit | 256 - 2 | 221
D | 1110 + Multicast Address |  | IP Multicast | 
E | Future Use |  |  | 
0
Network (7 bits)
Network (14 bits)
1
1
0
1
0
Network (21 bits)
Host (24 bits)
Host (16 bits)
Host (8 bits)
Class A:
Class B:
Class C:

## Slide 28: IP networks
Class A network: 18.0.0.0 (MIT)
  www.mit.edu has address 18.7.22.83
Class B network: 128.174.0.0 (UIUC)
  www.cs.uiuc.edu has address 128.174.252.84
Class C network: 216.125.249.0 (Parkland)
  www.parkland.edu has address 216.125.249.97

## Slide 29: CIDR
3-class model too inflexible
CIDR: Classless InterDomain Routing
  Arbitrary number of bits to specify network
  Address format: a.b.c.d/x, where x is # bits in network portion
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 30: Classless Domains
Internet Archive - 207.241.224.0/20
  4K hosts
  207.241.224.0 - 207.241.239.255
AT&T - 204.127.128.0/18
  16K hosts
  204.127.128.0 - 204.127.191.255
UUNET - 63.64.0.0/10
  4M hosts
  63.64.0.0 - 63.127.255.255

## Slide 31: IP forwarding
Forwarding table has:
  Network number
  Interface
Avoid having to store 4 billion entries
  But there are still 2 million class C’s
  …and perhaps more CIDR networks

## Slide 32: Hierarchical Routing
scale: with 200 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 33: Hierarchical Networks
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 34: Subnetting
UIUC - 130.126.0.0/16
  130.126.0.0 - 130.126.255.255
CRHC - 130.126.136.0/21
  130.126.136.0 - 130.126.143.255
EWS - 130.126.160.0/21
  130.126.160.0 - 130.126.167.255

## Slide 35: Forwarding Tables
  130.126.136.0/21 if1
  130.126.160.0/21 if2
  130.126.0.0/16 if3
  0.0.0.0/0 if4
Most specific rule is used
Most hosts outside of the core have default rules
CRHC
EWS
UIUC
Internet
if1
if2
if4
if3
Notes: Forwarding tables are small, except at network core
Stop here, go back to routing.

## Slide 36: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
Gateway router
Direct link to router in another AS

## Slide 37: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Forwarding table is configured by both intra- and inter-AS routing algorithm
  Intra-AS sets entries for internal dests
  Inter-AS & Intra-As sets entries for external dests

## Slide 38: DNS: Domain Name System
People: many identifiers:
  SSN, name, UIN, etc.
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  Resource “name”, e.g., URL sal.cs.uiuc.edu – human-readable format
Q: given a resource name, how does a client find out the IP address of the service/server?
Domain Name System:
distributed database implemented in a hierarchy of many name servers
application-layer protocol that is responsible for resolving names (address/name translation)

## Slide 39: DNS Name Servers
Alternative
no server has all name-to-IP address mappings
Hierarchy of name servers
authoritative name servers:
  for a resource, stores the mapped IP address for that resource
local name servers:
  each institution/company/ISP owns a local (default) name server
  host DNS query first goes to local name server
  local name server might be caching an answer
Why not have a central DNS server?
single point of failure
traffic volume
may be far
maintenance difficult
doesn’t scale!
(WWW contains several billion pages today)

## Slide 40: DNS: Root Name Servers
contacted by local name server that can not resolve query
root name server:
  contacts authoritative name server if name mapping not known
  gets mapping
  returns mapping to local name server
~ dozen root name servers worldwide (as of ’98)

## Slide 41: Simple DNS Example
host surf.eurecom.fr wants IP address of dragon.cs.uiuc.edu
1. Contacts its local DNS server, dns.eurecom.fr
2. dns.eurecom.fr contacts root name server, if necessary
3. root name server contacts authoritative name server, dns.cs.uiuc.edu, if necessary
Answer returned by first server that is caching the mapping tuple
requesting host
surf.eurecom.fr
dragon.cs.uiuc.edu
root name server
authoritative name server
dns.cs.uiuc.edu
local name server
dns.eurecom.fr
1
2
3
4
5
6

## Slide 42: DNS Example
Root name server:
may not know the authoritative name server
may know intermediate name server: whom to contact to find authoritative name server
Hierarchy
.
.edu .com .mil …
uiuc.edu mit.edu…
requesting host
surf.eurecom.fr
dragon.cs.uiuc.edu
root name server
local name server
dns.eurecom.fr
1
2
3
4
5
6
authoritative name server
dns.cs.uiuc.edu
intermediate name server
dns.uiuc.edu
7
8

## Slide 43: DNS: Iterated Queries
recursive query:
puts burden of name resolution on servers along the way
may fail if a server does not know next server to contact
iterated query:
contacted server replies with name of server to querying server
“I don’t know this resource name, but ask this other server”
takes longer (more replies) but gives client more control
requesting host
surf.eurecom.fr
dragon.cs.uiuc.edu
root name server
local name server
dns.eurecom.fr
1
2
3
4
5
6
authoritative name server
dns.cs.uiuc.edu
intermediate name server
dns.uiuc.edu
7
8
iterated query

## Slide 44: DNS: Caching and Updating Records
Once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time
Update/notify mechanisms: insert new DNS entries
  RFC 2136
  http://www.ietf.org/html.charters/dnsind-charter.html
  Rarely update for most websites
  Until Akamai realized otherwise (their first version uses update extensively)