## Slide 1: Basic Concepts
CS 438: Spring 2014
Matthew Caesar
http://courses.engr.illinois.edu/cs438/

## Slide 2: Today
10,000 foot view of the Internet
Basic concepts
  links
  packet delays
  circuit switching
  packet (datagram) switching
Layering

## Slide 3: A 10,000 foot view of the Internet

## Slide 4: How can Two Hosts Communicate?
Encode information on modulated “Carrier signal”
  Phase, frequency, and amplitude modulation, and combinations thereof
  Ethernet: self-clocking Manchester coding ensures one transition per clock
  Technologies: copper, optical, wireless
0.7 Volts
-0.7 Volts

## Slide 5: How can many hosts communicate?
Naïve approach: full mesh
Problem:
  Obviously doesn’t scale to the 570,937,778+ hosts in the Internet

## Slide 6: How can many hosts communicate?
Better approach: Multiplex traffic with routers
Goals: make network robust to failures and attack, maintain spare capacity, reduce operational costs
  Introduces new challenges: What topology to use? How to find and look up paths? How to identify destinations?

## Slide 9: The Internet is a federated system
ISP A
user
ISP B
ISP C
user
Tied together by IP -- the “Internet Protocol” : a single common interface between users and the network and between networks
The Internet ties together different networks
  >20,000 ISP networks
Internet

## Slide 10: The Internet is a federated system
The Internet ties together different networks
  >20,000 ISP networks
A single, common interface is great for interoperability…
…but tricky for business
Why does this matter?
  ease of interoperability is the Internet’s most important goal
  practical realities of incentives, economics and real-world trust drive topology, route selection and service evolution

## Slide 11: How can routers find paths?
Robert
pinterest.com
23.2.0.0/24
81.2.0.0/24
10.1.0.0/16
4.0.0.0/8
Prefix
Hops
IF
Routing Table at B
D
1
4.0.0.0/8
Prefix
Hops
IF
Routing Table at C
D
1
4.0.0.0/8
Prefix
Hops
IF
Routing Table at A
B
2
A
B
C
D
10.1.0.1
10.1.8.7
23.2.0.1
81.2.0.1
4.5.16.2
4.18.5.1
4.9.0.1
IP address
4.0.0.0/8
Prefix
Robert’s local
DNS server
Pinterest’s authoritative
DNS server
.com authoritative
DNS sever
Hosts assigned topology-dependent addresses
Routers advertise address blocks (“prefixes”)
Routers compute “shortest” paths to prefixes
Map IP addresses to names with DNS

## Slide 12: Basic Concepts

## Slide 13: Nodes and Links
A
B

## Slide 14: Properties of Links
Bandwidth (capacity): “width” of the link
  number of bits sent (or received) per unit time (bits/sec or bps)
Latency (delay): “length” of the link
  propagation time for data to travel along the link (seconds)
Bandwidth-Delay Product (BDP): “volume” of the link
  amount of data that can be “in flight” at any time
  propagation delay × bits/time = total bits in link
bandwidth
Latency
delay x bandwidth

## Slide 15: Examples of Bandwidth-Delay
Same city over a slow link:
  BW ~100Mbps
  Latency ~0.1msec
  BDP ~10,000bits (~1.25KBytes)
Cross-country over fast link:
  BW ~10Gbps
  Latency~10msec
  BDP ~108bits (~12.5GBytes)

## Slide 16: Packet Delay Sending a 100B packet from A to B?
time=0
A
B
100 Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
Packet Delay = Transmission Delay + Propagation Delay
Packet Delay =
(Packet Size ÷ Link Bandwidth) + Link Latency

## Slide 17: Packet Delay Sending a 100B packet from A to B?
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 18: Packet Delay: The “pipe” view Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 19: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 20: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
1Mbps, 10ms (BDP=10,000)
time 
BW 
200B?

## Slide 21
Any questions?

## Slide 22: Nodes and Links
A
B

## Slide 23: What if we have more nodes?
One link for every node?
Need a scalable way to interconnect nodes

## Slide 24: What if I have more nodes?
One link for all nodes?
This is a broadcast network

## Slide 25: Solution: A switched network
Nodes share network link resources
How is this sharing implemented?
Notes: multiple conversations in parallel
resources are shared

## Slide 26: Two forms of switched networks
Circuit switching (used in the telephone network)
Packet switching (used in the Internet)
Notes: borrow mckeown’s slides (of network with image); add Berkeley and MIT.
box -- links (incoming and outgoing)
packet -- data + header.
header has an address.

## Slide 27: Circuit Switching
(1) Node A sends a reservation request
(2) Interior switches establish a connection -- i.e., “circuit”
(3) A starts sending data
(4) A sends a “teardown circuit” message
Idea: source reserves network capacity along a path
A
B
10Mb/s?
10Mb/s?
10Mb/s?
Notes: multiple conversations in parallel
resources are shared

## Slide 28: Circuit Switching: sharing a link
Time-division
  Each circuit allocated certain time slots
Frequency-division
  Each circuit allocated certain frequencies
time
frequency
time

## Slide 29: Time Division Multiplexing
Time divided into frames; frames into slots
Relative slot position inside a frame determines to which conversation data belongs
  e.g., slot 0 belongs to orange conversation
Slots are reserved (released) during circuit setup (teardown)
If a conversation does not use its circuit capacity is lost!
Frames
0
1
2
3
4
5
0
1
2
3
4
5
Slots =

## Slide 30: Timing in Circuit Switching
time

## Slide 31: Timing in Circuit Switching
time

## Slide 32: Timing in Circuit Switching
time

## Slide 33: Timing in Circuit Switching
time

## Slide 34: Timing in Circuit Switching
Circuit Establishment
time

## Slide 35: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
time

## Slide 36: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 37: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons

## Slide 38: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 39: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”

## Slide 40: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 41: Timing in Circuit Switching
Information
Circuit Establishment
Circuit Teardown
time
Data transfer
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 42: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup time is overhead

## Slide 43: Circuit switching
A
B
Circuit switching doesn’t “route around trouble”
Notes: multiple conversations in parallel
resources are shared

## Slide 44: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup time is overhead
  recovery from failure is slow

## Slide 45: Two forms of switched networks
Circuit switching (e.g., telephone network)
Packet switching (e.g., Internet)

## Slide 46: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
01000111100010101001110100011001
Internet Address
Age
Checksum to protect header
Header
Data
header
payload

## Slide 47: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
  payload is the data being carried
  header holds instructions to the network for how to handle packet (think of the header as an interface!)

## Slide 48: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers

## Slide 49: Switches forward packets
to MIT
to UW
UIUC
to NYU
Destination | Next Hop
UIUC | 4
UW | 5
MIT | 2
NYU | 3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4

## Slide 50: Timing in Packet Switching
time
payload
hdr
What about the time to process the packet at the switch?
We’ll assume it’s relatively negligible (mostly true)
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 51: Timing in Packet Switching
time
payload
hdr
Could the switch start transmitting as soon as it has processed the header?
Yes! This would be called a “cut through” switch
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 52: Timing in Packet Switching
time
payload
hdr
We will always assume a switch processes/forwards a packet after it has received it entirely. This is called “store and forward” switching
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 53: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers

## Slide 54: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
  no notion of packets belonging to a “circuit”

## Slide 55: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance. Instead packet switching leverages statistical multiplexing

## Slide 56: Statistical Multiplexing

## Slide 57: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 58: When Each Flow Gets 1/3rd of Capacity
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Frequent Overloading

## Slide 59: When flows share total capacity
Time
Time
Time
No Overloading
Statistical multiplexing relies on the assumption
that not all flows burst at the same time.
Very similar to insurance, and has same failure case

## Slide 60: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 61: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 62: Three Flows with Bursty Traffic
Data Rate 1+2+3 >> Capacity
Time
Time
Capacity
What do we do under overload?

## Slide 63: Statistical multiplexing: pipe view
time 
BW 
pkt tx time

## Slide 64: Statistical multiplexing: pipe view

## Slide 65: Statistical multiplexing: pipe view
No Overload!

## Slide 66: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 67: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 68: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 69: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 70: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 71: Statistical multiplexing: pipe view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts!

## Slide 72: Statistical multiplexing: pipe view
What about persistent overload?
Will eventually drop packets

## Slide 73: Queues introduce queuing delays
Recall, packet delay = tx delay + prop delay
With queues (stat. muxing)
  packet delay = tx delay + prop delay + queuing delay
Queuing delay caused by “packet interference”
Made worse at high load
  less “idle time” to absorb bursts
  think about traffic jams at rush hour

## Slide 74: Basic Queuing Theory Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
Service process: transmission times
  Average transmission time (function of packet size)
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”
Two different quantities

## Slide 75: Little’s Law (1961)
L = A x W
Average queue size (L) is average packet arrival rate (A) times average wait time (W)
  Surprisingly, not influenced by arrival process distribution, service distribution, service order, etc.
Used for router queue, circuit dimensioning
More complex computation: Xth percentile queue size
  Realm of queuing theory
  Depends on arrival/service processes

## Slide 76: Statistical Multiplexing is a recurrent theme in computer science
Phone network rather than dedicated lines
  Ancient history
Packet switching rather than circuits
  Today’s lecture
Cloud computing
  Shared datacenters, rather than single PCs

## Slide 77: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance. Instead packet switching leverages statistical multiplexing
  allows efficient use of resources
  but introduces queues and queuing delays

## Slide 78: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup adds delay
  recovery from failure is slow

## Slide 79: Packet switching: pros and cons
Cons
  no guaranteed performance
  header overhead per packet
  queues and queuing delays
Pros
  efficient use of bandwidth (stat. muxing)
  no overhead due to connection setup
  resilient -- can `route around trouble’

## Slide 80: Recap: you should leave this lecture with…
A sense of how the basic `plumbing’ works
  links and switches
  packet delays (tx, propagation, queuing)
  statistical multiplexing and queues
  circuit vs. packet switching
Next: back to lofty principles
  protocols and layering