## Slide 1: Pinhole Camera Model
Computational Photography
Derek Hoiem, University of Illinois
10/01/15

## Slide 2: Next classes: Single-view Geometry
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?

## Slide 3: Today’s class
Mapping between image and world coordinates
  Pinhole camera model
  Projective geometry
    Vanishing points and lines
  Projection matrix

## Slide 4: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide source: Seitz

## Slide 5: Pinhole camera
Idea 2: add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Slide source: Seitz
Notes: Q: How does this transform the image? A: It gets inverted

## Slide 6: Pinhole camera
Figure from Forsyth
f
f = focal length
c = center of the camera
c

## Slide 7: Camera obscura: the pre-camera
First idea: Mozi, China (470BC to 390BC)
First built: Alhacen, Iraq/Egypt (965 to 1039AD)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys

## Slide 8: Camera Obscura used for Tracing
Lens Based Camera Obscura, 1568

## Slide 9: First Photograph
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Oldest surviving photograph
  Took 8 hours on pewter plate
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 10: Pinhole camera
A lens focuses light onto the film
“circle of
confusion”
Slide source: Seitz

## Slide 11: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 12: Projection can be tricky…
Slide source: Seitz

## Slide 13: Projection can be tricky…
Slide source: Seitz

## Slide 14: Projective Geometry
What is lost?
Length
Which is closer?
Who is taller?

## Slide 15: Length is not preserved
Figure by David Forsyth
B’
C’
A’

## Slide 16: Projective Geometry
What is lost?
Length
Angles
Perpendicular?
Parallel?

## Slide 17: Parallel lines are not parallel in the image
Figure by David Forsyth

## Slide 18: Projective Geometry
What is preserved?
Straight lines are still straight

## Slide 19: Vanishing points and lines
Parallel lines in the world intersect in the image at a “vanishing point”
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 20: Vanishing points and lines
o
Vanishing Point
o
Vanishing Point
Vanishing Line
Notes: Go to board, sketch out various properties of vanishing points/lines
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 21: Vanishing points and lines
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Credit: Criminisi

## Slide 22: Vanishing points and lines
Photo from online Tate collection
Notes: Where are the vanishing points? Do buildings on left and buildings on right have the same vanishing line? Which way is the camera tilted?

## Slide 23: Note on estimating vanishing points
Use multiple lines for better accuracy
… but lines will not intersect at exactly the same point in practice
One solution: take mean of intersecting pairs
… bad idea!
Instead, minimize angular differences
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 24: (more vanishing points on board)

## Slide 25: Vanishing objects

## Slide 26: Camera matrix
http://www.youtube.com/watch?v=6KlJzfsAzoY
Notes: P = K [R t]

## Slide 27: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u

## Slide 28: Homogeneous coordinates
Conversion
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 29: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 30: Basic geometry in homogeneous coordinates
Line equation: ax + by + c = 0
Append 1 to pixel coordinate to get homogeneous coordinate
Line given by cross product of two points
Intersection of two lines given by cross product of the lines

## Slide 31: Another problem solved by homogeneous coordinates
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
Intersection of parallel lines
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 32
Slide Credit: Saverese
Projection matrix
x: Image Coordinates: w(u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,T

## Slide 33: Pinhole Camera Model
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
t
R

## Slide 34: Interlude: when have I used this stuff?

## Slide 35: When have I used this stuff?
Object Recognition (CVPR 2006)

## Slide 36: When have I used this stuff?
Single-view reconstruction (SIGGRAPH 2005)

## Slide 37: When have I used this stuff?
Getting spatial layout in indoor scenes (ICCV 2009)

## Slide 38: When have I used this stuff?
Inserting photographed objects into images (SIGGRAPH 2007)
Original
Created

## Slide 39: When have I used this stuff?
Inserting synthetic objects into images: http://vimeo.com/28962540

## Slide 40: When have I used this stuff?
Creating detailed and complete 3D scene models from a single view (ongoing)

## Slide 41
K
Slide Credit: Saverese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Principal point at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Notes: Work through equations for u and v on board

## Slide 42: Remove assumption: known optical center
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 43: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 44: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 45: Oriented and Translated Camera
Ow
iw
kw
jw
t
R

## Slide 46: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 47: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 48: Allow camera rotation

## Slide 49: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 50: Vanishing Point = Projection from Infinity

## Slide 51: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 52: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
  What’s the projection matrix?
Slide by Steve Seitz
Illustration from George Bebis

## Slide 53: Take-home question
Suppose we have two 3D cubes on the ground facing the viewer, one near, one far.
What would they look like in perspective?
What would they look like in weak perspective?
Photo credit: GazetteLive.co.uk

## Slide 54: Beyond Pinholes: Radial Distortion
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 55: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 56: Next classes
Tues: single-view metrology
  Measuring 3D distances from the image
Thurs: single-view 3D reconstruction