ECE 199 Exam 1 Fall 2003

Tuesday, September 30th, 2003

Name:

- Be sure your exam booklet has 11 pages.

- Write your name at the top of each page.

- This is a closed book exam.

- You are allowed one 8.5 x 11 sheet of notes.

- Absolutely no interaction between students is allowed.

- Show all of your work.

- Challenge questions are marked with a ***

- Don’t panic, and good luck!

Problem 1	20 points

Problem 2	20 points

Problem 3	20 points

Problem 4	20 points

Problem 5	20 points

Total		100 points

Problem 1 (20 points): Short Answer

Part A (12 points): How many bits are necessary to store a single number in the range 0 to 99999…

a)  (4 points) …using an unsigned representation?

b)  (4 points) …using a 2’s complement representation?

c)  (4 points) …using ASCII?

Part B (4 points): Explain one advantage of a floating-point representation over a 2’s complement representation.

Part C (4 points): Prove that the functions OR and NOT together are logically complete.

Problem 2 (20 Points): Sequential Circuits

Part A (10 points): For the diagram below, assume that Y initially contains a 0 while X contains some 2’s complement number. In a single sentence, describe what the contents of Y represent after the WriteEn signal is raised to a logical ‘1’ and lowered to ‘0’ 16 times.

Problem 2, continued:

Part B (10 points): Describe what the following sequential circuit does in a sentence. Assume that the output Q3Q2Q1Q0 is initially 0000.

Problem 3 (20 Points): Memories

Part A (4 points): A memory stores a total of 16 Mbits (1 Mbit is 220 bits) and uses 19-bit addresses. What is the addressability of this memory in bits?

Part B (4 points): Is it ever possible to have the PC, IR, MAR, and MDR all contain the same value during the FETCH cycle of the von Neumann instruction cycle? If so, explain how. If not, explain why not.

***Part C (12 points): You must design a 216 by 16-bit memory for the LC-3. However, you have only been given four 214 by 16-bit memory blocks to work with. Draw your design on the next page, using any gates or combinational logic blocks we discussed in class in addition to the 4 memory blocks.

Problem 4 (20 Points): Finite State Machines

A certain finite state machine implements a match scoring system for a game played in rounds by two players (X and Y).  Each round can result in a win for X, a win for Y, or a tie.  When a player gets ahead by three rounds (has won three more times than the other player), that player wins the match.  Answer all parts of this question based on the implementation shown below.  The parts are designed to help you through the analysis.

Problem 4, continued:

Part A (2 points): For what value(s) of the register S does player X win?  Player Y?

Part B (3 points): Explain the function of the bottom mux and the logic controlling it.

Part C (3 points): Explain the function of the OR gate and the mux that it controls.

Part D (4 points): Explain the meaning of the bits held in register S.

Part E (4 points): Fill in the table below of input values and their meanings; three of the meanings have been given already.

| V1 | V0 | meaning |
| --- | --- | --- |
|  |  | player X won a round |
|  |  | player Y won a round |
|  |  | round tied |
|  |  | (your answer to Part B) |

***Part F (4 points) How many bits of state are necessary if the game is instead played until one player has won three times?  Justify your answer.

Problem 5 (20 Points): The von Neumann Model

For this question, refer to the LC-3 version of the von Neumann Model below.  The LC-3 is about to perform an instruction FETCH.

Say the LC-3 completes the execution of two instructions (i.e., the instruction cycle is performed twice).  Clearly indicate all final values in the diagram below for the…

Part A (8 points): Register File

Part B (6 points): PC and IR

Part C (6 points): MAR and MDR

Hint: The instruction in x3010 is an LDR instruction and the instruction in x3011 is an ADD.

Scratch Paper for Calculations

# Text boxes

x3012

x3013

x3014

x3016

x3017

x3018

x3015

xF025

x1001

x1FF2

x300D

x1981

x0020

x0000

x1BBF

x6CBC

x3010

R6

R5

focus of Part A

V0

V1

focus of Part C

focus of Part B

S0

S1

S2

Y wins

X wins

000

3

3

3

3

3

0        1

3-bit register S

+

0        1

R4

R3

R2

R1

R7

R0

ALU

x3011

x3010

Memory

Register File

IR

#### MDR

MAR

PC

x1981

x3013

x0001

x0BEE

x1234

x3017

x3010

x002A

x300F

x300D

x300C

x300E

x903F

x834A

xB503

xC001

#### Address

16-bit Register X

load

load

16-bit Register Y

16

16

16

16

b

a

b

a

Cin

Cout

Cin

Sum

Sum

+

+

0

0

1

WriteEn

WriteEn

16

DataIn

16

14

DataOut

Address

WriteEn

16

DataIn

16

14

DataOut

Address

WriteEn

WriteEn

Address

DataOut

14

16

DataIn

16

16

DataIn

16

14

DataOut

Address

WriteEn