## Slide 1: More on Exponential Distribution, Hypo exponential distribution
ECE 313
Probability with Engineering Applications
Lecture 13
Professor Ravi K. Iyer
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana Champaign

## Slide 2: Today’s Topics
Uniform Distribution
Hypoexponential Distribution
  TMR - Simplex Example
Announcements
  Mini Project 2 will be due March 11 Saturday 11:59pm
  Midterm, March 15, in class, 11:00am – 12:20 ( one 8x11 sheet no calc -phones, laptops etc)
  Midterm review session, March 13, 5:30–7:00pm, Place TBD

## Slide 4: Uniform Distribution

## Slide 5: The Uniform or Rectangular Distribution
A continuous random variable X is said to have a uniform distribution over the interval (a,b) if its density is given by:
And the distribution function is given by:

## Slide 7: Exponential Example 1 (TMR system)
Consider the triple modular redundant (TMR) system (n = 3 and m = 2).
If R denotes the reliability of a component then
  for a discrete time we assume that R = constant and then:
RTMR = 3R2 - 2R3
  In the continuous time we assume that the failures of components are exponentially distributed with parameter 
    the reliability of a component can be expressed as:
R(TMR)

## Slide 8: Comparison of TMR and Simplex

## Slide 9: Example 1 (TMR system) cont.
From the plot Rtmr(t) against t as well as R(t) against t, note that:
and
Where t0 is the solution to the equation:

## Slide 10: Example 1 (TMR system) cont.
Thus if we define a “short” mission by the mission time t  t0, then it is clear that TMR type of redundancy improves reliability only for short missions.
For long missions, this type of redundancy actually degrades reliability.

## Slide 11: Example 2 (TMR/Simplex system)
TMR system has higher reliability than simplex for short missions only.
To improve upon the performance of TMR, we observe that after one of the three units have failed, both of the two remaining units must function properly for the classical TMR configuration to function properly.
Thus, after one failure, the system reduces to a series system of two components, from the reliability point of view.

## Slide 12: Example 2 (TMR/Simplex system) cont.
An improvement over this simple scheme, known as TMR/simplex
  detects a single component failure,
  discards the failed component, and
  reverts to one of the non-failing simplex components.
In other words, not only the failed component but also one of the good component is discarded.

## Slide 13: Example 2 (TMR/Simplex system) cont.
Let X, Y, Z, denote the times to failure of the three components.
Let W denote the residual time to failure of the selected surviving component.
Let X, Y, Z be mutually independent and exponentially distributed with parameter .
Then, if L denotes the time to failure of TMR/simplex, then L can be expressed as:

## Slide 14: Hypoexponential Distribution
Many processes in nature can be divided into sequential phases.
If the time the process spends in each phase is:
  Independent
  Exponentially distributed
It can be shown that the overall time is hypoexponentially distributed.
For example: i) The TMR simplex; ii) More generally, service times for input-output operations in a computer system often possess this distribution.
The distribution has r parameters, one for each distinct phase.

## Slide 15: Hypoexponential Distribution (cont.)
A two-stage hypoexponential random variable, X, with parameters 1 and 2 (1 ≠2 ), is denoted by X~HYPO(1, 2 ).

## Slide 16: The pdf of the Hypoexponential Distribution
f(t)
0
0.669
0.334
1.25
2.50
3.75
5.00
0
t

## Slide 17: The CDF of the Hypoexponential Distribution
The corresponding distribution function is:
t
F(t)
0
1.0
0.5
1.25
2.50
3.75
5.00
0

## Slide 18: The Hazard for the Hypoexponential Distribution
The hazard rate is given by:

## Slide 19: The Failure Rate of the Hypoexponential Distribution
This is an IFR distribution with the failure rate increasing from 0 up to min {1, 2}
h(t)
0
1.00
0.500
1.25
2.50
3.75
5.00
0
t

## Slide 20: Example 2 (TMR/Simplex system) cont.
We use two useful notions:
1. The lifetime distribution of a series system whose components have independent exponentially distributed lifetimes is itself exponentially distributed with parameter
2. If X´ and Y´are
  exponentially distributed with parameters 1 and 2, respectively,

## Slide 21: Example 2 (TMR/Simplex system) cont.
An improvement over this simple scheme, known as TMR/simplex

## Slide 22: Example 2 (TMR/Simplex system) cont.
Let X, Y, Z, denote the times to failure of the three components.
Let W denote the residual time to failure of the selected surviving component.
Let X, Y, Z be mutually independent and exponentially distributed with parameter .
Then, if L denotes the time to failure of TMR/simplex, then L can be expressed as:
L = min{X, Y, Z} + W

## Slide 23: Example 2 (TMR/Simplex system) cont.
Now:
  Since the exponential distribution is memoryless, the lifetime W of the surviving component is exponentially distributed with parameter .
  min {X, Y, Z} is exponentially distributed with parameter 3.
  Then L has a two-stage hypoexponential distribution with parameters 3 and .

## Slide 24: Example 2 (TMR/Simplex system) cont.
Therefore, we have:
The reliability expression of TMR/simplex is:
The TMR/simplex has a higher reliability than either a simplex or an ordinary TMR system for all t  0.

## Slide 25: Comparison of Simplex, TMR, & TMR/Simplex

## Slide 26: Erlang and Gamma Distribution
When r sequential phases have independent identical exponential distributions, the resulting density (pdf) is known as r-stage (or r-phase) Erlang:
The CDF (Cumulative distribution function is:
Also:

## Slide 27: Erlang and Gamma Distribution (cont.)
The exponential distribution is a special case of the Erlang distribution with r = 1.
A component subjected to an environment so that Nt, the number of peak stresses in the interval (0, t], is Poisson distributed with parameter  t.
The component can withstand (r -1) peak stresses and the rth occurrence of a peak stress causes a failure.
The component lifetime X is related to Nt so these two events are equivalent:

## Slide 28: Erlang and Gamma Distribution (cont.)
Thus:
F(t) = 1 - R(t) yields the previous formula:
Conclusion is that the component lifetime has an r-stage Erlang distribution.

## Slide 29: Gamma Function and Density
If r (call it ) take nonintegral values, then we get the gamma density:
where the gamma function is defined by the integral:

## Slide 30: Gamma Function and Density (cont.)
The following properties of the gamma function will be useful in our workl. Integration by parts shows that for  > 1:
In particular, if  is a positive integer, denoted by n, then:
Other useful formulas related to the gamma function are:
and

## Slide 31: Gamma Function and Density (cont.)

## Slide 32: Hyperexponential Distribution
A process with sequential phases gives rise to a hypoexponential or an Erlang distribution, depending upon whether or not the phases have identical distributions.
If a process consists of alternate phases, i. e. during any single experiment the process experiences one and only one of the many alternate phases, and
If these phases have independent exponential distributions, then
The overall distribution is hyperexponential.

## Slide 33: Hyperexponential Distribution (cont.)
The density function of a k-phase hyperexponential random variable is:
The distribution function is:
The failure rate is:
which is a decreasing failure rate from ii down to min {1, 2,…}

## Slide 34: Hyperexponential Distribution (cont.)
The hyperexponential is a special case of mixture distributions that often arise in practice:
The hyperexponential distribution exhibits more variability than the exponential, e.g. CPU service-time distribution in a computer system often expresses this.
If a product is manufactured in several parallel assembly lines and the outputs are merged, then the failure density of the overall product is likely to be hyperexponential.

## Slide 35: Hyperexponential Distribution (cont.)

## Slide 36: Example 3 (On-line Fault Detector)
Consider a model consisting of a functional unit (e.g., an adder) together with an on-line fault detector
Let T and C denote the times to failure of the unit and the detector respectively
After the unit fails, a finite time D (called the detection latency) is required to detect the failure.
Failure of the detector, however, is detected instantaneously.

## Slide 38: Example 3 (On-line Fault Detector) cont.
Let X denote the time to failure indication and Y denote the time to failure occurrence (of either the detector or the unit).
Then
X = min{T + D, C} and Y = min{T, C}.
If the detector fails before the unit, then a false alarm is said to have occurred.
If the unit fails before the detector, then the unit keeps producing erroneous output during the detection phase and thus propagates the effect of the failure.
The purpose of the detector is to reduce the detection time D.

## Slide 39: Example 3 (On-line Fault Detector) cont.
We define:
Real reliability Rr(t) = P(Y  t) and
Apparent reliability Ra(t) = P(X  t).
A powerful detector will tend to narrow the gap between Rr(t) and Ra(t).
Assume that T, D, and C are mutually independent and exponentially distributed with parameters , , and .

## Slide 40: Example 3 (On-line Fault Detector) cont.
Then Y is exponentially distributed with parameter  +  and:
T + D is hypoexponentially distributed so that:

## Slide 41: Example 3 (On-line Fault Detector) cont.
And, the apparent reliability is:

## Slide 42: Uniform Distribution

## Slide 43: The Uniform or Rectangular Distribution
A continuous random variable X is said to have a uniform distribution over the interval (a,b) if its density is given by:
And the distribution function is given by:

## Slide 44: Hypoexponential Distribution
Many processes in nature can be divided into sequential phases.
If the time the process spends in each phase is:
  Independent
  Exponentially distributed
It can be shown that the overall time is hypoexponentially distributed.
For example: The service times for input-output operations in a computer system often possess this distribution.
The distribution has r parameters, one for each distinct phase.

## Slide 45: Hypoexponential Distribution (cont.)
A two-stage hypoexponential random variable, X, with parameters 1 and 2 (1 ≠2 ), is denoted by X~HYPO(1, 2 ).

## Slide 46: The pdf of the Hypoexponential Distribution
f(t)
0
0.669
0.334
1.25
2.50
3.75
5.00
0
t

## Slide 47: The CDF of the Hypoexponential Distribution
The corresponding distribution function is:
t
F(t)
0
1.0
0.5
1.25
2.50
3.75
5.00
0

## Slide 48: The Hazard for the Hypoexponential Distribution
The hazard rate is given by:

## Slide 49: The Failure Rate of the Hypoexponential Distribution
This is an IFR distribution with the failure rate increasing from 0 up to min {1, 2}
h(t)
0
1.00
0.500
1.25
2.50
3.75
5.00
0
t

## Slide 50: Example 1 (TMR system)
Consider the triple modular redundant (TMR) system (n = 3 and m = 2).
Let assume that R denotes the reliability of a component then
  for the discrete time we assume that R = constant and then:
RTMR = 3R2 - 2R3
  for the continuous time we assume that the failure of components are exponentially distributed with parameter 
    the reliability of a component can be expressed as:
R(t) = 1 - (1 - e-t) = e-t , and consequently
RTMR(t) = 3R(t)2 - 2R(t)3
RTMR(t) = 3 e-2t - 2 e-3t

## Slide 51: Comparison of TMR and Simplex

## Slide 52: Example 1 (TMR system) cont.
From the plot Rtmr(t) against t as well as R(t) against t, note that:
and
Where t0 is the solution to the equation:
which is:

## Slide 53: Example 1 (TMR system) cont.
Thus if we define a “short” mission by the mission time t  t0, then it is clear that TMR type of redundancy improves reliability only for short missions.
For long missions, this type of redundancy actually degrades reliability.

## Slide 54: Example 2 (TMR/Simplex system)
TMR system has higher reliability than simplex for short missions only.
To improve upon the performance of TMR, we observe that after one of the three units have failed, both of the two remaining units must function properly for the classical TMR configuration to function properly.
Thus, after one failure, the system reduces to a series system of two components, from the reliability point of view.

## Slide 55: Example 2 (TMR/Simplex system) cont.
An improvement over this simple scheme, known as TMR/simplex
  detects a single component failure,
  discards the failed component, and
  reverts to one of the nonfailing simplex components.
In other words, not only the failed component but also one of the good components is discarded.

## Slide 56: Example 2 (TMR/Simplex system) cont.
Let X, Y, Z, denote the times to failure of the three components.
Let W denote the residual time to failure of the selected surviving component.
Let X, Y, Z be mutually independent and exponentially distributed with parameter .
Then, if L denotes the time to failure of TMR/simplex, then L can be expressed as:
L = min{X, Y, Z} + W

## Slide 57: Example 2 (TMR/Simplex system) cont.
We use two useful notions:
1. The lifetime distribution of a series system whose components have independent exponentially distributed lifetimes is itself exponentially distributed with parameter
2. If X´ and Y´are
  exponentially distributed with parameters 1 and 2, respectively,
  X´ and Y´ are independent , and
  1  2 then
Z = X´ + Y´
has a two-stage hypoexponential distribution with parameters 1 and 2,

## Slide 58: Example 2 (TMR/Simplex system) cont.
Now:
  Since the exponential distribution is memoryless, the lifetime W of the surviving component is exponentially distributed with parameter .
  min {X, Y, Z} is exponentially distributed with parameter 3.
  Then L has a two-stage hypoexponential distribution with parameters 3 and .

## Slide 59: Example 2 (TMR/Simplex system) cont.
Therefore, we have:
The reliability expression of TMR/simplex is:
The TMR/simplex has a higher reliability than either a simplex or an ordinary TMR system for all t  0.

## Slide 60: Comparison of Simplex, TMR, & TMR/Simplex

## Slide 61: Erlang and Gamma Distribution
When r sequential phases have independent identical exponential distributions, the resulting density (pdf) is known as r-stage (or r-phase) Erlang:
The CDF (Cumulative distribution function is:
Also:

## Slide 62: Erlang and Gamma Distribution (cont.)
The exponential distribution is a special case of the Erlang distribution with r = 1.
A component subjected to an environment so that Nt, the number of peak stresses in the interval (0, t], is Poisson distributed with parameter  t.
The component can withstand (r -1) peak stresses and the rth occurrence of a peak stress causes a failure.
The component lifetime X is related to Nt so these two events are equivalent:

## Slide 63: Erlang and Gamma Distribution (cont.)
Thus:
F(t) = 1 - R(t) yields the previous formula:
Conclusion is that the component lifetime has an r-stage Erlang distribution.

## Slide 64: Gamma Function and Density
If r (call it ) take nonintegral values, then we get the gamma density:
where the gamma function is defined by the integral:

## Slide 65: Gamma Function and Density (cont.)
The following properties of the gamma function will be useful in our workl. Integration by parts shows that for  > 1:
In particular, if  is a positive integer, denoted by n, then:
Other useful formulas related to the gamma function are:
and

## Slide 66: Gamma Function and Density (cont.)

## Slide 67: Hyperexponential Distribution
A process with sequential phases gives rise to a hypoexponential or an Erlang distribution, depending upon whether or not the phases have identical distributions.
If a process consists of alternate phases, i. e. during any single experiment the process experiences one and only one of the many alternate phases, and
If these phases have independent exponential distributions, then
The overall distribution is hyperexponential.

## Slide 68: Hyperexponential Distribution (cont.)
The density function of a k-phase hyperexponential random variable is:
The distribution function is:
The failure rate is:
which is a decreasing failure rate from ii down to min {1, 2,…}

## Slide 69: Hyperexponential Distribution (cont.)
The hyperexponential is a special case of mixture distributions that often arise in practice:
The hyperexponential distribution exhibits more variability than the exponential, e.g. CPU service-time distribution in a computer system often expresses this.
If a product is manufactured in several parallel assembly lines and the outputs are merged, then the failure density of the overall product is likely to be hyperexponential.

## Slide 70: Hyperexponential Distribution (cont.)

## Slide 71: Example 3 (On-line Fault Detector)
Consider a model consisting of a functional unit (e.g., an adder) together with an on-line fault detector
Let T and C denote the times to failure of the unit and the detector respectively
After the unit fails, a finite time D (called the detection latency) is required to detect the failure.
Failure of the detector, however, is detected instantaneously.

## Slide 73: Example 3 (On-line Fault Detector) cont.
Let X denote the time to failure indication and Y denote the time to failure occurrence (of either the detector or the unit).
Then
X = min{T + D, C} and Y = min{T, C}.
If the detector fails before the unit, then a false alarm is said to have occurred.
If the unit fails before the detector, then the unit keeps producing erroneous output during the detection phase and thus propagates the effect of the failure.
The purpose of the detector is to reduce the detection time D.

## Slide 74: Example 3 (On-line Fault Detector) cont.
We define:
Real reliability Rr(t) = P(Y  t) and
Apparent reliability Ra(t) = P(X  t).
A powerful detector will tend to narrow the gap between Rr(t) and Ra(t).
Assume that T, D, and C are mutually independent and exponentially distributed with parameters , , and .

## Slide 75: Example 3 (On-line Fault Detector) cont.
Then Y is exponentially distributed with parameter  +  and:
T + D is hypoexponentially distributed so that:

## Slide 76: Example 3 (On-line Fault Detector) cont.
And, the apparent reliability is:

## Slide 77: Summary
Four special types of phase-type exponential distributions:
Hypoexponential Distribution:
  Exponential distributions at each phase have different λ
2) Examples

## Slide 78: Phase-type Exponential Distributions
Exponential Distribution:
  Time to the event or Inter-arrivals => Poisson
  Phase-type Exponential Distributions:
  We have a process that is divided into k sequential phases, in which time that the process spends in each phase is:
    Independent
    Exponentially distributed
  The generalization of the phase-type exponential distributions is called Coxian Distribution
    Any distribution can be expressed as the sum of phase-type exponential distributions