## Slide 1: ECE 333 Green Energy Systems
Lecture 10: Photovoltaic Arrays
Dr. Karl Reinhard
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
reinhrd2@illinois.edu

## Slide 2: Announcements
Reading Chapter 5
HW 5:
  For Quiz 5
  5.2, 5.3, 5.4, 5.5, 5.7, 5.8, 5.10, 5.11
  Additional problem
  Before Midterm Exam 1
  5.6, 5.7, 5.9
Quiz 5: 22 Feb 18
Midterm Exam 1
  1 Mar 18 (Thursday – 2 weeks) During class period
  1 page of notes – blanks provided – will be turned in.

## Slide 3: Problem 4.11 (Section 4.13)
Typical Meteorological Year (TMY)
  Global Horizontal Irradiance (GHI) Direct Normal Irradiance (DNI) Diffuse Horizontal Irradiance (DHI)
  DNI – direct beam
  DHI – diffuse beam GHI – reflected beam
https://nsrdb.nrel.gov/tmy accessed 14 Feb 18
TMY datasets used in solar energy system computer simulations
Enable production estimates and performance comparisons of different system types and configurations

## Slide 4: Many Different PV cell Materials
Courtesy of the National Renewable Energy Laboratory, Golden, CO.
https://www.nrel.gov/pv/assets/images/efficiency-chart.png accessed 9 Feb 18
3 Technologies Dominate:
Monocrystalline Si
Polycrystalline Si (p-Si)
Thin Film
Notes: Notes accompanying NREL PV efficiency-chart.png
https://www.nrel.gov/pv/assets/pdfs/cell_efficiency_explanatory_notes.pdf (accessed 9 Feb 2018)
The National Renewable Energy Laboratory (NREL) maintains a plot of compiled values of highest confirmed conversion efficiencies for research cells, from 1976 to the present, for a range of photovoltaic technologies.
Devices included in this plot of the current state of the art have efficiencies that are confirmed by independent, recognized test labs (e.g., NREL, AIST, Fraunhofer) and are reported on a standardized basis. The measurements for new entries must be with respect to Standard Test or Reporting Conditions (STC) as defined by the global reference spectrum for flat-plate devices and the direct reference spectrum for concentrator devices as listed in standards IEC 60904-3 edition 2 or ASTM G173. The reference temperature is 25°C and the area is the cell total area or the area defined by an aperture.
Cell efficiency results are provided within different families of semiconductors: (1) multijunction cells, (2) single-junction gallium arsenide cells, (3) crystalline silicon cells, (4) thin- film technologies, and (5) emerging photovoltaics. Some 26 different subcategories are indicated by distinctive colored symbols.
The most recent world record for each technology is highlighted along the right edge in a flag that contains the efficiency and the symbol of the technology. The company or group that fabricated the device for each most-recent record is bolded on the plot.
The information plotted by NREL is provided in good faith, but NREL cannot accept direct responsibility for any errors or omissions. The plot is not copyrighted and may be used in presentations and publications, with a notation included that states: “This plot is courtesy of the National Renewable Energy Laboratory, Golden, CO.”

## Slide 5: PV Material Market Share
Source: http://www.ise.fraunhofer.de/en (Photovoltaics Report, July 2014)
Note that silicon continues to dominate in market share

## Slide 6: Single Cell V-I Terminal Relationship
Assume
  I0 = 510-11 A
  Isc = 5A,
  Rp = 5,
  Rs = 0.01 
At 25C what is Voc?
Cannot explicitly solve this equation, but an iterative solution can be found… choose Vd and solve using Newton's method).
  Choose Vd = 0.65, next iteration is 0.6504.
Photocurrent source
RP
Load
Rs
(minimize)
(maximize)
Equivalent Circuit
Isc

## Slide 7
To generate the terminal V-I Curve
  Pick a Vd value
  Solve for Id
  Solve of Ip
  I = Isc – Id - Ip
  V = Vd - Rs· I
Single Cell V-I Terminal Relationship (cont)

## Slide 8: Cells as Building Blocks
Solar cell Voc is ~ 0.6 V and ~ loaded cell V is ~ 0.5 V 0.5
V is low for power applications  single cell is impractical
 Wire individual cells in series – a module &
  encase module in a tough, weather-resistant package
Modules are in-turn wired into arrays

## Slide 9: Cells to Modules to Arrays
Modules
    12V module has 36 cells wired in series, each cell ~ 0.5 V
    72-cell modules are also common
Arrays – combination of modules connected in series and/or in parallel
FIGURE 5.33 Photovoltaic cells, modules, and arrays.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 10: Module w/ “Simple Cell” Model
Using the simplest cell model
For one cell (in the sun)

## Slide 11: Module with “Simple Cell” Model
For the entire module

## Slide 12: Module w/ “Parallel-Only” Cell Model
For the entire module
For one cell (in the sun)

## Slide 13: Module Example
Assume 36 identical cells in series w/
I0 = 510-11 A
Isc=5A
At 25C what is Voc?
Again, an iterative solution is needed and yields: V = 23.41
Rp= 10
Rs = 0 
FIGURE 5.34
For cells wired in series, their voltages at any given current add.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 14: Module with General Cell Model

## Slide 15: Module w/ “General Cell” Model
For the entire module
V
+
-
Writing the equations in terms of V and I

## Slide 16: Module Example Continued: V-I Curve
Generating the V-I Curve again requires picking a Vd
  Pick a value of Vd
  Solve for Id
  Solve for Ip
  I = Isc – Id – Ip
  V = n(Vd – Rs · I)

## Slide 17: Cells Wired to form Modules
Modules in series increase the voltage
Modules in parallel increase the current
FIGURE 5.35 For modules in series, at any given current the voltages add.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
FIGURE 5.36 For modules in parallel, at any given voltage the currents add.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell.

## Slide 18: Cells Wired to form Modules
Cells can also be wired in series and parallel combinations
Terminal Voltage and Currents add as linear combinations of strictly series or parallel modules.
FIGURE 5.37 The total I–V curve of an array consisting of two strings of three modules each
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell.

## Slide 19: Standard Test Conditions
Standard PV Test Conditions are 1 kW/m2 , 25C, 1.5 AMR
Cell rating is the Maximum Power Point (MPP) power
Fill factor (FF) is ratio of MPP to Voc  Isc
FIGURE 5.41 The maximum power point (MPP) corresponds to the biggest rectangle that can fit beneath the I–V curve.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 20: Impact of Temperature and Insolation
Cell output is sensitive to T and Insolation
Voc drops by ~ (panel dependent – check spec sheet)
FIGURE 5.42 I-V characteristic curves under various cell temperatures for a Kyocera KC120-1 PV module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
  S – Insolation (kW/m2)
  NOCT – Nominal Operating Cell T. (panel spec)
  Industry standard is that NOCT reported @
    20o C ambient and
    0.8 (kW/m2) and
    wind @ 1 m/s

## Slide 21: PV Module Shading
PV module output can be severely reduced (>50%) w/ small portion shaded
A single shaded cell in a long cell string limits current in all cells
  ISC depends directly upon Insolation: ↓ S  ↓ I
  Each cell in series must carry the same current (KCL !!)
In essence, a shaded PV cell is modeled as a resistor (vice a current source || w/ a diode )
Isc = zero
Reverse biased diode (off)
I flows through Rp, RS

## Slide 22: Shading Impact on Output Voltage
Voltage across n non-shaded cells
or n-1 non-shaded cells
+
_
I
I
I
I
I
I
I
I
I
I
_
VSH
+
FIGURE 5.43 n-cell module in which (a) all cells are in the sun or (b) the top cell is completely shaded.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2d Ed.

## Slide 23: Voltage Output w/ Shading – VSH
Rp >> Rs
FIGURE 5.44 Effect of shading one cell in an n-cell module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2d Ed.

## Slide 24: Voltage Output w/ Shading – Example
PV Module: 72 cells in Series
ISC = 6.0 A @ 25oC
Io = 5 x 10-11 A
Rp = 10 
Rs = 0.001 
4.38 A
2.24 A

## Slide 25: Voltage Output w/ Shading – Example (cont)
4.38 A
2.24 A
Cell Shading Impacts Power Output !!

## Slide 26: PV Module Operating Point
What Determines the PV Module’s Operating point??

## Slide 27: Shading Example 2
36 cell PV module w/ Rp = 6.6 W per cell.
In full sun, I = 2.14 A & V = 19.41 V.
Pout = 41.5 W.
If a cell is shaded & the I stays the same, what are the new output voltage and power?
With one cell shaded the output is < 25% of original! Lost power is dissipated as heat in the shaded cell.

## Slide 28: Shading Mitigation
Solution – bypass the shaded cell w/ diodes
Replace I ·(Rp+Rs ) resistive w/ ~.6 V diode voltage drop
No other effects under normal operation
FIGURE 5.50 Using bypass diodes to mitigate shading impact in a string of modules
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 29: Bypass Diode Impact on Module
FIGURE 5.50 Showing the ability of bypass diodes to mitigate shading problems in a string of modules
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 30: PV Module Operating Point
What Determines the PV Module’s Operating point??

## Slide 31: Monocrystalline Silicon (mono-si)
Also called crystalline silicon
Made out of high grade silicon ingots that are cylindrical in shape
  Their edges are cut
  Even coloring and uniform look
These panels cost more, but have higher efficiency and longer life
  Ex: SunPower E20 series w/ 20% efficiency
Image: http://solargaincommercial.com.au/sites/default/files/sunpower-solar-power-module.png

## Slide 32: Polycrystalline Silicon (p-Si) or Multi-cyrstalline Silicon (mc-Si)
Oldest of the commercial PV panels
Silicon is melted and poured into square molds
  Result is square wafers, with no side cuts
  Speckled appearance
Advantages:
  Less expensive
  less waste
Disadvantage:
  lower efficiency (13-16%)
Image: http://dev.msbs.net/Portals/0/images/PolycrystallineSolarPanel.jpg

## Slide 33: Thin-Film Solar Cells
Thin-film solar cells are created by depositing one or more layers of material onto the substrate
  Examples include amorphous silicon (a-Si), gallium arsenide (GaAs), cadmium telluride (CdTe), copper indium gallium selenide (CIS)
Advantages are that they are simple to mass produce, have a uniform appearance, and can be flexible
Disadvantages are they are not very efficient, and may degrade faster
Image: http://www.thesolarco.com/images/Why-Choose-Monocrystalline-Technology_amorphous.jpg