## Slide 1: ECE 333 Green Energy Systems
Lecture 11: Maximum Power Point Tracking, Photovoltaic Systems, & Utility Rates
Dr. Karl Reinhard
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
reinhrd2@illinois.edu

## Slide 2: Announcements
Quiz on HW 5 today
Exam 1 is on Thursday (1 Mar) in this room
  closed book
  closed notes
  Bring a standard calculator (no smart phones) & one 8.5” x 11” note sheet (front and back) (provided)
  Covers material up to PV arrays – but not including dc-dc converters

## Slide 3: Dust Degrades PV Panel Performance
Dust degrades PV system performance, degradation can exceed 15%
Dust accumulation depends on many factors
  Amount of dust in the environment
  Humidity, wind, rain,
  Panel tilt, surface finish
  Cleaning frequency
  Dust attracts dust!
Dust accumulation can be reduced by
  Manual cleaning – requires water, time consuming)
  Surface treatments
  Surface material w/ electrostatic charge to repel dust,
  Robotic cleaning systems

## Slide 4: PV and Dust: Robots Cleaning the Panels
Image: http://www.ecoppia.com/solution/ketura-sun
Robotic solar panel cleaning system

## Slide 5: PV Module Operating Point
What Determines the PV Module’s Operating point??

## Slide 6: The Need for DC-DC Converters
In general, delivering power from PV source to a load
  AC grid – Battery – DC machine
FIGURE 5.40 The I–V curve and power output for a PV module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
Load Line: V
Locus of Possible Operating Points
Operating Point
If Load is connected directly across PV terminals,
Since Rload is fixed, (VL, IL ) ≠ (VM, IM )
 Can’t Deliver Max Available Power to the Load

## Slide 7: The Need for DC-DC Converters (cont)
Need a DC-DC Conversion Circuit:
FIGURE 5.40 The I–V curve and power output for a PV module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
Load Line: V
Operating Point
Desired Characteristics:
 100% i.e. VM IM = Vo Io
Control Flexibility: As input varies,
Need dc-dc converter to fix operation at MPP

## Slide 8: dc-dc Conversion
Consider the Transformer (Lect 5)
Two Issues:
Saturates @ dc
Fixed turns ratio
dc-dc Converter Topologies:
  Buck
  Boost
  Buck-Boost
Composed of:
  Energy storage (L, C)
  Switches (FET, diode)
  Control (digital / analog)

## Slide 9: dc-dc Conversion Fundamentals
Relevance:
Dc-dc converters include both L and C
Guiding Principles:
1. Energy Storage Components

## Slide 10: dc-dc Conversion Fundamentals
2. Switching Waveform
A “switching signal” controls the dc-dc converter
Average behavior is important to understand dc-dc operation.
/T = D

## Slide 11: Buck dc-dc Converter
Assume an “ideal” diode
Operating Principle:
q(t) = 1, diode is rev biased  off
diode blocks current flow
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts

## Slide 12: Buck dc-dc Converter
If Capacitor C is large, then
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts
Use to understand circuit behavior
Switch On
Vout(t)
VL(t)
+
_
(KVL)
Switch Off
Vout(t)
VL(t)
+
_
(KVL)
+
_
Over a complete q(t) period (switch-on and switch-off cycle):

## Slide 13: Buck dc-dc Converter
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts
Applying
As D is controlled, the dc-dc converter delivers Vout < Vin
D

## Slide 14: Buck Converter Waveforms
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts
L: Effectively a dc I source (w/ ripple)
C: Effectively a dc V source (w/ ripple)
https://en.wikipedia.org/wiki/Buck_converter

## Slide 15: Boost dc-dc Converter
Assume an “ideal” diode
Guiding Principle:
q(t) = 1, diode is rev biased  off
diode blocks current flow
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts

## Slide 16: Boost dc-dc Converter
Use to understand circuit behavior
Switch On
(KVL)
Switch Off
(KVL)
Over a complete q(t) period (switch-on and switch-off cycle):
If Capacitor C is large, then

## Slide 17: Boost dc-dc Converter (cont)
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts
Applying
As D is controlled, the dc-dc converter delivers Vout > Vin
D

## Slide 18: Boost Converter Waveforms
q(t) = 0, iL requires a path (KCL)
diode is fwd biased  on / conducts
L: Effectively a dc I source (w/ ripple)
C: Effectively a dc V source (w/ ripple)
https://en.wikipedia.org/wiki/Boost_converter

## Slide 19: Other dc-dc converters
Many converter topologies have been proposed
E.g. flyback, buck-boost, etc.
Each involves
Some provide
some
Others w/o limits (flyback, boost)
ECE 464: Power Electronics
ECE 469: Power Electronics Lab

## Slide 20: Fundamental Operational Principles
Operate in 1 of 2 States:
  switch on, diode off
  switch off, diode on
Large L, C 
L: Effectively a dc I source (w/ ripple)
C: Effectively a dc V source (w/ ripple)

## Slide 21: Back to Our “Matching Problem(cont)
Use Conversion Circuit:
FIGURE 5.40 The I–V curve and power output for a PV module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
Load Line: V
Operating Point
Match load voltage and PV panel voltage to maximize power conversion

## Slide 22: (Back to) Maximum Power Point Trackers
Maximum Power Point Trackers (MPPTs) are often an integral PV system component, especially grid-connected
Key Idea -- As conditions change, Tuning system’s I-V curve operating point to stay near the “knee”
Buck-boost converter – DC to DC converter, can either “buck” (lower) or “boost” (raise) the voltage
Varying the buck-boost converter’s duty cycle enables the “tuning”
21
Load Line

## Slide 23: MPPTs – Example
A PV module has its MPP @ Vm = 17 V, Im = 6A.
What should MPPT duty cycle be if the module is delivering power to a 10 Ω resistive load?
Max power delivered by the PVs is 17V · 6A = 102W
Match Panel V to Load V: Boost PV’s 17 V to Load’s 31.9 V
Solving:

## Slide 24: Grid-Connected Systems
Can have a combiner box and a single inverter or small inverters for each panel
Individual inverters make the system modular
Inverter sends AC power to utility service panel
Power conditioning unit (PCU) may include
  MPPT
  Ground-fault circuit interrupter (GFCI)
  Circuitry to disconnect from grid if utility loses power
  Battery bank to provide back-up power
FIGURE 6.1 Simplified grid-connected PV system with net metering
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 25: Grid-Connected PV System Components
FIGURE 6.2 Principal components in a grid-connected PV system using a single inverter and a single utility meter.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 26: Individual Inverter Concept
Allows easy expansion
House distribution panel connections are simple
Lower $$ -- Less expensive DC cabling required
FIGURE 6.3 An alternative to having a single MPPT/inverter for an entire array is to provide microinverters for each module.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 27: Basic Voltage-Sourced Inverter Operation
Ideally inverter takes a dc input and produces a constant ac frequency output
  Output often doesn’t look like a sine ware
  Design goal is to minimize the harmonic content
Figure 6.7 from Elements of Power Electronics by Phil Krein
Filters can be used to eliminate harmonics

## Slide 28: Stand-Alone PV Systems
When the grid isn’t nearby, the extra cost and complexity of a stand-alone power system can be worth the benefits
System may include batteries and a backup generator
FIGURE 6.21 A “one-line” diagram of the important components in a stand-alone PV system.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 29: Stand-Alone PV - Considerations
PV System design begins with an estimate of the loads that need to be served by the PV system
Tradeoffs between more expensive, efficient appliances and size of PVs and battery system needed
Should you use more DC loads to avoid inverter inefficiencies or use more AC loads for convenience?
What fraction of the full load should the backup generator supply?
Power consumed while devices are off
In-rush current used to start major appliances

## Slide 30: Electric Utility Rates
Electric utilities long recognized as “natural monopolies”  so their rates set in public (political) process
  Also involved an “obligation to serve”
Three main types of utilities:
  Investor Owned (IOUs),
  Municipals (owned by city) or
  Coops (owned by members).
IOUs Rates are set through a process involving state regulators.
Initially bill was based on the number of light bulbs, later replaced by electric meters

## Slide 31: Electric Utility Rates, Cont.
W/ 50 states & 1000’s of providers, many rate structures. Simplest – flat rate per kWh….
Many structure possibilities:
  fixed charges,
  increasing or decreases rates based on amount used,
  seasonal and time-of-day rates,
  real-time (hourly) pricing,
  capacity charges, minimum power factor charges; different for residential, commercial, industrial
Energy may be supplied by a 3d party  Resulting in a transmission, distribution, & energy charge$.
Taxes may abound!!
Which is best? Incremental rates important when considering renewable additions

## Slide 32: Example PGE Rates (from Section 6.4.4), 2012
FIGURE 6.18 Example of a standard summer residential rate schedule for a California utility. Average consumption for this utility is in Tier 3.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 33: Eastern Illini Electric Coop Rates

## Slide 34: Eastern Illini Electric Coop Rates, 2015
Rate 1 (General Service, Single Phase)
  Base charge $40 per month
  All following charges per
  Delivery: 3.767¢/kWh first 1000 kWh, then 1.767¢/kWh
  Energy: 3.432 ¢/kWh
  Transmission: 1.433 ¢/kWh
  Generation: 3.767¢/kWh first 1000 kWh, then 2.647¢/kWh
  Total: 12.399 ¢/kWh first 1000 kWh, then 9.279 ¢/kWh
Rate 20 (Electric Heat, Single Phase)
  Same categories, base is $50 per month, similar rates in summer (4 months); winter rate >1000 is 7.346 ¢/kWh

## Slide 35: Sample Ameren Bill
https://www.ameren.com/illinois/csc/bill-sample-2

## Slide 36: Time of Usage Rates
Some utilities, including Ameren, provide the option to have electricity prices vary hourly
  Prices are set day ahead
Image: http://www.citizensutilityboard.org/pdfs/ConsumerInfo/AmerenPowerSmart.pdf
Prices: https://www2.ameren.com/RetailEnergy/RealTimePrices

## Slide 37: Commercial and Industrial Rates
Usually commercial and industrial rates also include a "demand charge" that is based on the maximum amount of power used during a time period
  Demand charge value is usually measured over some time period, such as 15 minutes
  It can also be time dependent, such as different values for summer and winter
Because of the demand charge, the rates paid by commercial and industrial users are lower

## Slide 38: CWLP Rates (Springfield, IL) (2012)
Residential, general: $4.67 monthly, $0.0988/kWh Winter, $0.114/kWh Summer
  Some seniors (62 up) get about a 10% discount
Residential, all electric: $4.67 monthly, $0.0895 Winter, $0.114 Summer
Small Business: $8.38 monthly, $0.095 Winter, $0.1034 Summer, Demand Charge $8/kW Winter, $9.68/kW Summer
Large Industrial: $577.13 monthly, $0.0722 Winter, $0.0781 Summer, Demand Charge: $11.46/kW Winter, $14.63/kW Summer
Source: http://www.cwlp.com/customer/rates/elecres.html

## Slide 39: US Average Electricity Rates (Feb 2018)
Image: https://www.eia.gov/electricity/data/browser/#/topic/7?geo=g&agg=0,1&endsec=vg accessed 21 Feb 18

## Slide 40: Net Metering for Renewables
Issue with small scale renewables is whether the generated electricity is sold back to the utility at the retail rate or the lower wholesale (avoided cost rate)
Net metering allows the customer to offset their own electric usage, and sometimes sell power back to the utility at the specified retail rate (meter runs backwards)
Requirements for net metering by IOUs are often set by the states; municipals and coops are self-governing
Potential concern about utilities providing services with costs born by the other customers

## Slide 41: Net Metering for Renewables
Typical residential situation w/ a single meter – Note: meter runs backwards when PV power produced exceeds local usage
During the day, any excess power from the array is sold to the utility; at night, power is purchased from the utility.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 42: Feed-in Tariffs
With feed-in tariffs there are two separate meters, one measuring the household consumption and a separate one measuring the PV generation
This allows the possibility that PV generation can be purchased at quite high rates
Feed-in tariffs started in Europe, but are now used some in the US (website http://www.pv-tech.org/tariff_watch/list summarizes them)
Current ones in Germany are $0.19/kWh for less than 10 kW, $0.18 for between 10 and 40 kW; on Hawaii it is $0.218/kWh for less than 20 kW