## Slide 1: Lecture 14: LPC speech synthesis and autocorrelation-based pitch tracking
ECE 417, Multimedia Signal Processing
October 10, 2019

## Slide 2: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 3: The LPC-10 speech synthesis model

## Slide 4: The LPC-10 Speech Coder: Transmitted Parameters
Each frame is 54 bits, and is used to synthesize 22.5ms of speech.
(54 bits/frame)/(0.0225 seconds/frame)=2400 bits/second
Pitch: 7 bits/frame (127 distinguishable non-zero pitch periods)
Energy: 5 bits/frame (32 levels, on a logRMS scale)
10 linear predictive coefficients (LPC): 41 bits/frame
Synchronization: 1 bit/frame

## Slide 5: The LPC-10 speech synthesis model
Vocal Tract:
Modeled by
an LPC synthesis
Filter.
Voiced Speech,
pitch period P
Unvoiced Speech
Binary Control
Switch:
Voiced (P>0) vs.
Unvoiced (P=0)
G
Gain=

## Slide 6: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 7: Autocorrelation is maximum at n=0

## Slide 8: Autocorrelation is maximum at n=0
Notice that, for n=0, this becomes just Parseval’s theorem:
But since is positive and real, any value of that is NOT positive and real will reduce the value of the integral!

## Slide 9: Example of an autocorrelation function computed from file0.wav, “Four score and seven years ago…”

## Slide 10: Autocorrelation of a periodic signal
Suppose x[n] is periodic, . Then the autocorrelation is also periodic:

## Slide 11: Autocorrelation of a periodic signal is periodic
Pitch period = 9ms = 99 samples
Pitch period = 9ms = 99 samples

## Slide 12: Autocorrelation pitch tracking
Compute the autocorrelation
Find the pitch period:
The search limits, and , are important for good performance:
  corresponds to a high woman’s pitch, about Hz
  corresponds to a low man’s pitch, about Hz

## Slide 13: The LPC-10 speech synthesis model
Vocal Tract:
Modeled by
an LPC synthesis
Filter.
Voiced Speech,
pitch period P
Unvoiced Speech
Binary Control
Switch:
Voiced (P>0) vs.
Unvoiced (P=0)
G
Gain=

## Slide 14: The voiced/unvoiced decision
voiced:
unvoiced (white noise): , which means that
So a reasonable V/UV decision is:
: say the frame is voiced.
: say the frame is unvoiced.
Setting threshold~0.25 works reasonably well.
voiced:
unvoiced:

## Slide 15: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 16: Inter-frame interpolation of pitch contours
We don’t want the pitch period to change suddenly at frame boundaries; it sounds weird.
Pitch
Period
Sample Number, n
Frame Boundary
Frame Boundary
Frame Boundary
Frame Boundary

## Slide 17: Inter-frame interpolation of pitch contours
Linear interpolation sounds much better. We can accomplish linear interpolation using a formula like
Where
is the pitch period in frame t
is how far sample n is from the beginning of frame t
S is the frame-skip.
Pitch
Period
Sample Number, n
Frame Boundary
Frame Boundary
Frame Boundary
Frame Boundary

## Slide 18: Inter-frame interpolation of energy
Linear interpolation is also useful for energy, EXCEPT: it sounds better if we interpolate log energy, not energy.

## Slide 19: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 20: The LPC-10 speech synthesis model
Vocal Tract:
Modeled by
an LPC synthesis
Filter.
Voiced Speech,
pitch period P
Unvoiced Speech
Binary Control
Switch:
Voiced vs.
Unvoiced
G
Gain=

## Slide 21: Unvoiced speech: e[n]=white noise
Use zero-mean, unit-variance Gaussian white noise
The choice, to use “unvoiced speech,” is communicated by the special code word “P=0”
By Morn - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=24084756

## Slide 22: Voiced speech: e[n]=pulse train
The basic idea:
Modification #1: in order for the RMS to equal 1.0, we need to scale each pulse by :

## Slide 23: Modification #2: the first pulse is not at n=0
Pitch period = 80 samples first pulse in frame 31 can’t occur until the 70th sample of the frame
30

## Slide 24: A mechanism for keeping track of pitch phase from one frame to the next
Start out, at the beginning of the speech, with a pitch phase equal to zero,
For every sample thereafter:
  If the sample is unvoiced (P[n]=0), don’t increment the pitch phase
  If the sample is voiced (P[n]>0), then increment the pitch phase
Every time the phase passes a multiple of , output a pitch pulse

## Slide 25: The pitch phase method: generate an excitation pulse whenever pitch phase crosses a -level
30
Sample Number, n
Phase

## Slide 26: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 27: Speech is predictable
Speech is not just white noise and pulse train. In fact, each sample is highly predictable from previous samples.
In fact, the pitch pulses are the only major exception to this predictability!

## Slide 28: Linear predictive coding (LPC)
The LPC idea:
Model the excitation as error
2. Force the coefficients to explain as much as they can, so that is as close to zero as possible.

## Slide 29: Linear predictive coding (LPC)
Setting gives

## Slide 30: Linear predictive coding (LPC)
So we have a set of linked equations, for :
We can write these 10 equations as a 10x10 matrix equation:
…which immediately gives the solution:
…where

## Slide 31: Outline
The LPC-10 speech synthesis model
Autocorrelation-based pitch tracking
Inter-frame interpolation of pitch and energy contours
The LPC-10 excitation model: white noise, pulse train
Linear predictive coding: how to find the coefficients
Linear predictive coding: how to make sure the coefficients are stable

## Slide 32: Speech -> Excitation -> Speech
Now that we know how to find the LPC coefficients, we can imagine an end-to-end LPC analysis-by-synthesis:
LPC
synthesis
Model
excitation
using pulse train and white noise
LPC
analysis

## Slide 33: The LPC Analysis Filter
The LPC Analysis Filter is an all-zeros filter (FIR = finite impulse response):
…where…
It’s often useful to write this as a polynomial where

## Slide 34: The LPC Synthesis Filter
The LPC Synthesis Filter is an all-poles filter (IIR = infinite impulse response):
…where…

## Slide 35: Speech -> Excitation -> Speech
Excitation Model

## Slide 36: The Stability Problem
The analysis filter is guaranteed to be stable, as long as the coefficients are finite. Suppose you know that , and . Then, even in the worst possible case,
The synthesis filter has no such guarantee. For example, suppose is just a delta function (), and suppose all of the except the first one, . Then
Which overflows your 16-bit sample buffer after only 110 samples. Your output will be full of NaNs, and you’ll be saying “What happened…?”

## Slide 37: How to Guarantee Stability
Fortunately, the LPC synthesis filter is causal, so it’s easy to guarantee stability. We just need to make sure that all of the poles have magnitude less than 1:
We find the poles like this:
in other words,
…which you can do using np.roots, if you define the polynomial correctly. Then you just truncate the magnitude,
…and then use np.poly to convert back from roots to polynomial.