## Slide 1
CS/ECE 438: Communication Networks
Fall 2019
6. Wireless & Mobile Networks

## Slide 2: Chapter 6 : Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3
Wireless Homes
Wireless Networks Increasingly Prevalent
UAVs
Wireless Biomedical Implants
Wireless Wearables
Wireless Vehicles
Wireless VR
Cellular Networks
Wireless Sensors
Wireless Data Centers

## Slide 4: Increasing Demand for Wireless Connectivity

## Slide 5: Increasing Demand for Wireless Connectivity

## Slide 6: Many Motivations for Wireless
Unrestricted mobility / deployability
  Unplugged from power outlet
Significantly lower cost
  No cable layout, service provision
  Low maintenance
Ease
  Direct communication with minimum infrastructure

## Slide 7: No Free Lunch
Numerous challenges
  Channel fluctuation
  Lower bandwidth
  Limited Battery power
  Disconnection due to mobility
  Security
  …

## Slide 8: Question Is …
Can’t we use the rich “wireline” knowledge ?
  In solving the wireless challenges

## Slide 9: The Answer
Wireless channel: A dispersive medium
The PHY and MAC layer completely dissimilar
The whole game changes

## Slide 10: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 11: Elements of a wireless network
network
infrastructure

## Slide 12: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 13: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 14: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 15: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 16: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 17: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 18: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 19: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 20: Wireless Link Characteristics
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)

## Slide 21: Wireless Link Characteristics
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)

## Slide 22: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR – easier to extract signal from noise (a “good thing”)
  Low SNR – hard to extract signal from noise ( a “bad thing”)
0
1
0
0
Bits:
0
1
0
0
Bits:
HIGH SNR  Low Bit Error Rate
LOW SNR  High Bit Error Rate

## Slide 23: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
BPSK: 1 bit per symbol
16 QAM: 4 bits per symbol

## Slide 24: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying

## Slide 25: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying
    QPSK: Phase Shift Keying

## Slide 26: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying
    QPSK: Quadrature Phase Shift Keying
    QAM: Quadrature Amplitude Modulation

## Slide 27: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying
    QPSK: Quadrature Phase Shift Keying
    QAM: Quadrature Amplitude Modulation

## Slide 28: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying
    QPSK: Quadrature Phase Shift Keying
    QAM: Quadrature Amplitude Modulation
    FSK: Frequency Shift Keying

## Slide 29: Wireless Link Characteristics
SNR: signal-to-noise ratio
  High SNR  Lower Bit Error  Use higher order modulation i.e. pack more bits per symbol
  Some types of modulations:
    BPSK: Binary Phase Shift Keying
    QPSK: Quadrature Phase Shift Keying
    QAM: Quadrature Amplitude Modulation
    FSK: Frequency Shift Keying
    PAM: Pulse Amplitude Modulation
    On-OFF Keying

## Slide 30: Wireless Link Characteristics
SNR versus BER tradeoffs
  given physical layer modulation:
  Higher SNR  Low BER
  given SNR: choose physical layer that meets BER requirement, giving highest throughput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, coding) rate adaptation
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 31: Wireless Link Characteristics
Given SNR, what is maximum rate that we can achieve?
  Shannon Capacity Theorem:

## Slide 32: Wireless Link Characteristics
important differences from wired link ….
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
X
Multiple Wired Links  No Interference
Multiple Wireless Links  Interference

## Slide 33: Wireless Link Characteristics
important differences from wired link ….
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
MAC Protocols necessary to avoid interference!

## Slide 34: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times

## Slide 35: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times

## Slide 36: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
First Path
Second Path
nth Path
    Multi-tap Channel
      Symbols arriving along late paths interfere with following symbols.
ISI: Inter-Symbol-Interference
ISI
Paths sum with
different phases:
Constructive/Destructive

## Slide 37: Wireless Link Characteristics
  Frequency Selective Fading:
  Example 2 paths with distance :
:
:
 24dB

## Slide 38: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
Fading

## Slide 39: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
    Inter-Symbol-Interference
    Frequency Selective Fading

## Slide 40: Wireless Link Characteristics
important differences from wired link ….
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
  Solution:
  OFDM: Orthogonal Frequency Division Multiplexing
  Idea: transmit symbols in frequency not time.

## Slide 41: Orthogonal Frequency Division Multiplexing

## Slide 42: Channel Estimation and Correction
How to estimate and correct for channel?
Send Preamble Bits

## Slide 43: Channel Estimation and Correction
Preamble Bits: Known bits

## Slide 44: Channel Estimation and Correction
What about multi-tap channel?
OFDM: Send bits in frequency domain
Channel estimation and correction can be done in frequency domain.

## Slide 45: Spread Spectrum
Problem of radio transmission: frequency dependent fading can wipe out narrow band signals for duration of the interference
Solution: spread the narrow band signal into a broad band signal using a special code
detection at
receiver
interference
spread signal
signal
spread
interference
f
f
power
power

## Slide 46: DSSS (Direct Sequence Spread Spectrum)
XOR the signal with pseudonoise (PN) sequence (chipping sequence)
Advantages
  reduces frequency selective fading
  Robust to interference
  Multi-user
Used in 3G & 802.11b
user data
chipping
sequence
resulting
signal
0
1
0
1
1
0
1
0
1
0
1
0
0
1
1
1
XOR
0
1
1
0
0
1
0
1
1
0
1
0
0
1
=
Tb
Tc

## Slide 47: FHSS (Frequency Hopping Spread Spectrum)
Discrete changes of carrier frequency
  sequence of frequency changes determined via PN sequence
Advantages
  frequency selective fading and interference limited to short period
  uses only small portion of spectrum at any time
  Secure
Used in bluetooth & military applicaitons

## Slide 48: Wireless Link Characteristics
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 49: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 50: Wireless network characteristics
Advantage of signal attenuation: Spatial Reuse
A
B
C
A’s signal
strength
space
C’s signal
strength
D

## Slide 51: Wireless network characteristics
Problem: A wants to transmit a packet to C
A
B
C
Option 1: A increases its power such that its packet reaches C
Option 2: A sends that packet to B which intern send it to C
A
B
C
A
B
C
d
d

## Slide 52: Wireless network characteristics
Problem: A wants to transmit a packet to C
A
B
C
Option 1: A increases its power such that its packet reaches C
Option 2: A sends that packet to B which intern send it to C
A
B
C
A
B
C
d
d
To double transmission range, we need: 4x more overall power!
To transmit over two hops, we need: 2x more overall power!

## Slide 53: Wireless network characteristics
Multi-hop wireless networks:
A
B
C
Increase TX power: increase transmission range by times, need more power
d
d
Multi-hop links: increase transmission range by times, need more power
Ad hoc multi-hop wireless networks!

## Slide 54: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 55: The Channel Access Problem
Multiple nodes share a channel
Pairwise communication desired
  Simultaneous communication not possible
MAC Protocols
  Suggests a scheme to schedule communication
    Maximize number of communications
    Ensure fairness among all transmitters
A
C
B

## Slide 56: The Trivial Solution
Transmit and pray
  Plenty of collisions  poor throughput at high load
A
C
B

## Slide 57: The Simple Fix
Transmit and pray
  Plenty of collisions  poor throughput at high load
Listen before you talk
  Carrier sense multiple access (CSMA)
  Defer transmission when signal on channel
A
C
B
Don’t
transmit
Can collisions still occur?

## Slide 58: CSMA collisions
Collisions can still occur:
Propagation delay non-zero between transmitters
When collision:
Entire packet transmission
time wasted
spatial layout of nodes
note:
Role of distance & propagation delay in determining collision probability

## Slide 59: CSMA/CD (Collision Detection)
Keep listening to channel
  While transmitting
If (Transmitted_Signal != Sensed_Signal)
   Sender knows it’s a Collision
   ABORT

## Slide 60: 2 Observations on CSMA/CD
Transmitter can send/listen concurrently
  If (Sensed - received = null)? Then success
The signal is identical at Tx and Rx
  Non-dispersive
The transmitter can DETECT if and
when collision occurs

## Slide 61: Unfortunately …
Both observations do not hold for wireless
Leading to …

## Slide 62: Wireless Medium Access Control
A
B
C
D
Distance
Signal
power
SINR threshold

## Slide 63: Wireless Media Disperse Energy
A
B
C
D
Distance
Signal
power
SINR threshold
A cannot send and listen in parallel
Signal not same at different locations

## Slide 64: Collision Detection Difficult
Signal reception based on SINR
  Transmitter can only hear itself
  Cannot determine signal quality at receiver

## Slide 65
A
B
C
D
Distance
Signal
power
SINR threshold
Red signal >> Blue signal
X
Red < Blue = collision

## Slide 66
A
B
C
D
Distance
Signal
power
SINR threshold
Important: C has not heard A, but can interfere at receiver B
X
C is the hidden terminal to A

## Slide 67
A
B
C
D
Distance
SINR threshold
Important: X has heard A, but should not defer transmission to Y
X
X is the exposed terminal to A
Y
Signal
power

## Slide 68
Hidden and Exposed Terminal Problems
Critical to wireless networks even today

## Slide 69: IEEE 802.11
CTS = Clear
To Send
RTS = Request
To Send
D
Y
S
M
K
RTS
CTS

## Slide 70: IEEE 802.11
D
Y
S
X
M
K
silenced
silenced
silenced
silenced
Data
ACK

## Slide 71
But is that enough?

## Slide 72: RTS/CTS
Does it solve hidden terminals ?
  Assuming carrier sensing zone = communication zone
C
F
A
B
E
D
CTS
RTS
E does not receive CTS successfully  Can later initiate transmission to D.
Hidden terminal problem remains.

## Slide 73: Hidden Terminal Problem
How about increasing carrier sense range ??
  E will defer on sensing carrier  no collision !!!
C
B
D
Data
A
E
CTS
RTS
F

## Slide 74: Hidden Terminal Problem
But what if barriers/obstructions ??
  E doesn’t hear C  Carrier sensing does not help
C
B
D
Data
A
E
F
CTS
RTS

## Slide 75: Exposed Terminal
B should be able to transmit to A
  RTS prevents this
C
A
B
E
D
CTS
RTS

## Slide 76: Exposed Terminal
B should be able to transmit to A
  Carrier sensing makes the situation worse
C
A
B
E
D
CTS
RTS

## Slide 77: Multiplexing
Multiplexing in 4 dimensions
  space (si)
  time (t)
  frequency (f)
  code (c)
s2
s3
s1
f
t
c
k2
k3
k4
k5
k6
k1
f
t
c
f
t
c

## Slide 78: Frequency multiplex
Separation of spectrum into smaller frequency bands
Channel gets band of the spectrum for the whole time
Advantages:
  no dynamic coordination needed
  works also for analog signals
Disadvantages:
  waste of bandwidth if traffic distributed unevenly
  inflexible
  guard spaces
k3
k4
k5
k6
f
t
c

## Slide 79: Time multiplex
f
t
c
k2
k3
k4
k5
k6
k1
Channel gets the whole spectrum for a certain amount of time
Advantages:
  only one carrier in the medium at any time
  throughput high even for many users
Disadvantages:
  precise synchronization necessary

## Slide 80: Time and frequency multiplex
f
A channel gets a certain frequency band for a certain amount of time (e.g. GSM)
Advantages:
  better protection against tapping
  protection against frequency selective interference
  higher data rates compared to code multiplex
Precise coordination required
t
c
k2
k3
k4
k5
k6
k1

## Slide 81: Code multiplex
Each channel has unique code
All channels use same spectrum at same time
Advantages:
  bandwidth efficient
  no coordination and synchronization
  good protection against interference
Disadvantages:
  lower user data rates
  more complex signal regeneration
Implemented using spread spectrum technology
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 82: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
Example codes: Gold Codes, Walsh Codes

## Slide 83: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 84: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 85: Code Division Multiple Access (CDMA)
Ideally, need codes to have good:
Auto-correlation properties:
Cross-correlation properties:
Need orthogonal codes:
For N users, length of code is exponential in N 
Near Far Effect Problem need power management

## Slide 86: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 87: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
direct sequence spread spectrum (DSSS) in physical layer
  all hosts use same chipping code
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antenna
  2.4-5 GHz range
  up to 200 Mbps
802.11ac: multiple antenna
  2.4-5 GHz range
  Up to 1.69 Gbps
802.11ad/ay: Millimeter wave
  2.4, 5, 60 GHz range
  Up to 7 Gbps

## Slide 88: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router

## Slide 89: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication
  will typically run DHCP to get IP address in AP’s subnet

## Slide 90: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 91: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 92: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 93: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 94: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 95: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 96
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 97
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 98
802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 99
802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 100: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 101
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wired tel. net.
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 102: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots

## Slide 103
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G (voice) network architecture
MSC
Public
telephone
network
Gateway
MSC
G

## Slide 104
3G (voice+data) network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 105
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)
3G (voice+data) network architecture

## Slide 106
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
3G versus 4G LTE network architecture
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 107
4G: differences from 3G
all IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 108: Mobile Technologies from 1G – 5G
Notes: And this is what I am going to show you next, a system that can find the right alignment in O(log n) packets.

## Slide 109: 5G: Unified Air Interface

## Slide 110
Notes: And this is what I am going to show you next, a system that can find the right alignment in O(log n) packets.

## Slide 111: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 112: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 113: Mobility: vocabulary
wide area network
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 114: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 115: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 116: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 117: Mobility: registration
wide area network
end result:
foreign agent knows about mobile
home agent knows location of mobile
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 118: Mobility via indirect routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 119: Indirect Routing: comments
mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself
triangle routing: correspondent-home-network-mobile
  inefficient when
  correspondent, mobile
  are in same network

## Slide 120: Mobility via direct routing
1
2
3
4
home
network
visited
network
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 121
Components of cellular network architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 122
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
GSM: indirect routing to mobile
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 123
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing
GSM: handoff with common MSC
handoff goal: route call via new base station (without interruption)
reasons for handoff:
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
  GSM doesn't mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old BSS

## Slide 124
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
new BSS
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released
GSM: handoff with common MSC

## Slide 125: Chapter 6: Outline
  Introduction
  Wireless Links
  Wireless MAC
  WiFi: 802.11 Wireless LANs
  Cellular Networks: 3G, LTE
  Mobility

## Slide 126: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links