## Slide 1
Sun Tracking Solar Panel
Leonardo Larios, Bryce Smith, Soumitri Vadali
ECE 445: Senior Design Laboratory
Project Team Number 35
Sponsor: Prof. Karl Reinhard
TA: Yuchen He

## Slide 2
Project proposed by Professor Reinhard to be integrated with other streetlight projects
The system provides a simple and effective design for tracking the sun
Introduction
Notes: Leo

## Slide 3
Move East to West and North to South
Tracking the sun
  Reset functionality
Battery can support the power consumption of the system
Objectives
Notes: Bryce

## Slide 4
Block Diagram
Notes: Soumitri

## Slide 5
Physical Build
Notes: Bryce – mount and motors
Soumitri – sensor placement and hole size

## Slide 6
Design
Solar Panel
Power generation
Output: 14.5V – 20V
Output: 5A – 5.5A

## Slide 7
Design
Battery Charge Controller
Regulates solar input for charging
Input: 15V - 20V from solar panel
Output: PWM with amplitude 12V - 15V to the battery
Input: 12V - 12.5V from the battery
Output: 0 - 10mV to the solar panel

## Slide 8
Design
Battery Charge Controller
Blue: Solar terminals
Light blue: Battery terminals
0V
15V
0V
15V
0V
12V
0V
Notes: Change colors back the original
Add the axis label – 0V,15V and what the color represents

## Slide 9
Lead-acid Battery
Input: regulated input from charge controller
Output: 12V – 15V
2 hour discharge rate provides 26 Ah
Design

## Slide 10
Design
Voltage Regulator
Input: 12V -15V from battery
Output: 5V to microcontroller
Output: 12V to Over-Current Circuit (OCC)
  Carry 2A of current

## Slide 11
Design
Voltage Regulator

## Slide 12
Design
Over-Current Circuit
Turns motor power off when current draw is above 2 amps
Input: 12V from the voltage regulator
Output: Input voltage to the motor drivers

## Slide 13
Design
Over-Current Circuit
0V
t
Green: Timing capacitor voltage
Blue: Output voltage
3V

## Slide 14
Design
Microcontroller
Processes information from various inputs to drive motors
Input: 5V from the voltage regulator
Input: Analog signal from the photosensors
Input: Two digital signals from the encoders
Output: 5V to motor drivers

## Slide 15
Design
Microcontroller

## Slide 16
Design
Motor Driver
Controls the rotation and movement of the motors
Input: Four 5V digital signals from the microcontroller
Input: 12V from the Over-Current Circuit
Output: 12V to the motors

## Slide 17
Design
Motor Driver

## Slide 18
Design
DC Motors
Recycled
Characterization
Movement

## Slide 19
Design
Encoders
Resolution: .175°
Accuracy: +/- 5°
Physical Angle | Code Value | Calculated Angle
6° | 26 | 4.57°
14° | 69 | 12.12°
23° | 120 | 21.09°
33° | 178 | 31.29°
47° | 254 | 44.65°
86° | 474 | 83.32°
Resolution: θ = (1/Pulses Per Revolution)*360 |  | 
Top: Channel A
Bottom: Channel B
0V
5V
0V
5V

## Slide 20
Design
Photosensors
Differentiate between varying levels of sunlight
Input: 5V from voltage regulator
Output: Analog signal to the microcontroller
Lighting Level | Reading (V)
Covered | 0.09
Ambient | 1.57
Flashlight-Arm’s length | 2.23
Flashlight-hand’s length | 3.68
Flashlight-direct | 4.76

## Slide 21
Design
Photosensors

## Slide 22
Functionality Tests
Photosensing unit prototypes
Microcontroller
  Inputs: Photosensors and Encoders
  Outputs: Motor Driver
Light tracking capabilities
Reset Functions
  Angle maximums
  Low light levels
Notes: Soumtri

## Slide 23
Finding the Light…
Notes: Leo

## Slide 24
Project Build
Prototyping
Machine Shop Communication
Building the interconnections
Battery SOP
Faculty resources
PCB’s
Operational tests
Outdoor panel tests
Notes: Bryce

## Slide 25
Energy Consumption
Load | Average Power [W] | Time/day [hours/day] | Average energy per day [Wh/day] | Capacity used per day [Ah/day]
Moving panel | 13.44 | .25 | 3.36 | .28
Idle panel | .9204 | 23.75 | 21.86 | 1.82
LED Light | 33 | 5 | 165 | 13.75
Total | 190.22 | 15.85
Notes: Leo

## Slide 26
Successes
Motor is able to move about two axes
  East to West: +/- 90 degrees
  North to South: +/- 22.5 degrees
System is able to detect sunlight and time of day
Reset to start position on given day
Rotation limits
Optimized solar charging and power consumption for 2 days
Notes: Leo

## Slide 27
Future Work
Perfecting the software algorithm
Improve Hardware
  More power efficient system
    Power electronics, DC/DC Converter
    Improved motor and encoder
  Refined PCB Design
Increased outdoor functionality
  Waterproof / Temperature / Wind
Integration and communication with other teams
Notes: Bryce

## Slide 28
Prof. Karl Reinhard
Machine Shop
  Special thanks to Greg Bennett
Power Lab Resources
  Special thanks to Kevin Colravy
TA: Yuchen He
Acknowledgments
Notes: Soumtri

## Slide 29
Any questions?
Thank you for your attention!

## Slide 30
Where we Started…

## Slide 31
Edge to Edge…

## Slide 32
Reset…