## Slide 1: Cell Phone Transmission Detector
ECE 445 Fall 2017
Team 12
Anish Bhattacharya, Shandilya Pachgade, AJ Schroeder

## Slide 2: Outline
Motivation and Objectives
General Design
Module Specifications
Successes and Challenges
Conclusion

## Slide 3: Motivation
Expedia.co
RF interference at Arecibo Observatory in Puerto Rico
    Tourists' cell phones
Detect cell phone transmissions to eliminate RFI
Low-cost device easily
operated by anyone

## Slide 4
Detect active transmission (LTE data usage, call/text send/receive) in two bands: USA cellular band (700-850MHz) and Puerto Rico cellular band (1.5-1.9GHz)
Use a display to show signal strengths for each band
Notify operator via LEDs (one per band) when a signal of significant strength is detected
Objectives

## Slide 5: Outline
Motivation and Objectives
General Design
Module Specifications
Successes and Challenges
Conclusion

## Slide 6
General Block Diagram

## Slide 7: Functional Block Diagram

## Slide 8: Outline
Motivation and Objectives
General Design
Module Specifications
Successes and Challenges
Conclusion

## Slide 9: RF Module

## Slide 10: RF Module: Requirements
Detection distance up to 1 meter
    Minimum discernible signal of –50dBm
Attenuate unwanted signals, FM radio (250MHz) and Bluetooth/WiFi (2.4GHz)
    3dB drop for higher band
    1dB drop lower band
Output DC signal
    50mV minimum

## Slide 11
RF Module: Design
Parts
Antenna: Pulse W5084K698MHz – 3.0GHz
BPF: Designed with passive components
Amplifier: Qorvo TQP3m9008, 20dBm Gain, 50MHz – 4.0GHz
Rectifier: Designed with Schottky diode
Antenna
RF Amp
Rectifier
Bandpass Filter

## Slide 12
Used typical center frequency-resonance formula for bandpass filter to find an LC value:
Values for C and L were chosen according to component availability/tolerances
Lower Bandpass Filter: Calculations

## Slide 13
Created and simulated the calculated filter in Keysight ADS to visualize output
Lower Bandpass Filter: Design Simulations

## Slide 14
Using the same process for the upper band, the LC value was calculated, L & C values chosen, and the circuit simulated in ADS:
Upper Bandpass Filter: Design Summary

## Slide 15
Detection distance of 1m?
MDS of –50dBm?
Lower band attenuation?
Upper band attenuation?
DC output of 50mV?
Up to 3m detection distance
MDS of ~-60dBm
~8dBm attenuation for FM radio, ~4.5dBm attenuation for BT/WiFi
~1.5dBm attenuation at 800Mhz
~100mV output for active signal
RF Module: Verifications

## Slide 16
RF Module: Final Product

## Slide 17: Notification Module

## Slide 18
Notification Module: Requirements
Amplify input signal by at least 3.3V/50mV = 6.67x
Switch output signal within 10mV of Vref (3.3V)
LED switches visibly when signal detected

## Slide 19
Notification Module: Design
Parts
Amplifier: TI LMC6022IM
Comparator: TI LM339
Notification Elements: 2.7V LED
Amplifier
Comparator
Notification

## Slide 20
Notification Module: Verifications
Amplify by at least 6.67x?
Switching at Vref±10mV?
Visible LED switching?
Accurate amplification up to ~50x
Switching at Vref±1mV
LED switches rapidly but visibly

## Slide 21
Notification Module: Final Product

## Slide 22: Display Module

## Slide 23
Ability to display two bands of interest
    US Bands (700-850MHz) and Puerto Rico bands (1.5-1.9GHz)
Display updates in real-time
    0.5 seconds delay
Precise signal strength information
    Represent the output of half-wave rectifier within 10mV
Display Module: Requirements

## Slide 24
Parts
10-bit ADC, MCP3004
Raspberry Pi
    Matplotlib (library)
    SpiDev (library)
5" HDMI LCD, 800×480
Display Module: Design
ADC
Raspberry Pi

## Slide 25
Displays two bands?
Real-time plotting?
Accurate readings?
Yes
Samples every 0.1 seconds
10-bit precision with 3.3V reference voltage (≈3.3mV)
Display Module: Verifications

## Slide 26
Display Module: Final Product

## Slide 27: Power Supply Module

## Slide 28
Need a 3.3V source
    ±10mV tolerance, able to support 500mA
Need a 5V source
    ±200mV tolerance, able to support 2A
Power Supply Module: Requirements

## Slide 29
Parts
120VAC – 12VDC Wall Adapter: Wonderoto W-T5000
Voltage Regulators: TI LM1117 family
Power Supply Module: Design
DC Jack
5V Regulator
3.3V Regulator

## Slide 30
3.3V (±10mV) supplied?
5V (±200mV) supplied?
3.3V probed on PCB
5.04V probed on PCB
Power Supply Module: Verifications

## Slide 31
Demo

## Slide 32: Outline
Motivation and Objectives
General Design
Module Specifications
Successes and Challenges
Conclusion

## Slide 33
RF Module phone test
Notable Successes
Strong signal peak
Active transmission

## Slide 34
Rectified signal from phone transmission
Notable Successes

## Slide 35
High-frequency Schottky diode
    BAT63
LCD had a "white screen of death"
    Had to adjust system configuration parameters
Non-constant connection LED rapid switching
    Design decision
Challenges

## Slide 36: Outline
Motivation and Objectives
General Design
Module Specifications
Successes and Challenges
Conclusion

## Slide 37
Control LED with Raspberry Pi software trigger instead of DC Amplifier and Comparator circuit
Cascade RF Amplifier circuits for farther range
Make device portable
Further Work

## Slide 38
Adhere to IEEE Code of Ethics
    Ensure no harm will be caused by components (shocks from 120VAC-12VDC converter, burns from voltage regulators) [IEEE Code of Ethics Section 1]
    "Improve the understanding of technology" [Section 5] via our educational display
Abide by FCC regulations
    Ensure no arbitrary transmission via our antenna
Ethical Considerations

## Slide 39: Acknowledgements and Special Thanks
Yamuna Phal
Benjamin Eng
Zipeng (Bird) Wang
Elias Wilken-Resman
Professor Can Bayram
Professor Karl Reinhardt

## Slide 40: Thank you!
Questions?