## Slide 1: Solar RC Boat 49
Team #5: Nisa Chuchawat, Robert Whalen, Zhendong (Mike) Yang

## Slide 2: Introduction
Innovate RC Boat
  Battery life: 10-15 minutes of playtime for 1.5-2 hours of charge
  Operating range: 20-100 meters
    No indication if boat goes out of range

## Slide 3: Objectives
Use solar energy to power boat
  Extend battery life
Add signal strength detection and indication
https://www.walmart.com/ip/New-Bright-23-Fountain-R-C-FF-Boat/31528113

## Slide 4
Figure 1: Top Level Block Diagram

## Slide 5: Motor Requirements
Voltage (V) | Current (A) | Power (W)
3 | 0.69 | 2.07
3.5 | 0.84 | 2.94
4 | 1.00 | 4
4.5 | 1.15 | 5.175
5 | 1.34 | 6.7
5.5 | 1.50 | 8.25
6 | 1.71 | 10.26
7 | 2.10 | 14.7
Motor voltage sources:
  6V regulated solar voltage
  9.6V internal boat battery
Motor runs with 8.7 to 12.5 W
Table I: I-V Characteristics of Boat Motor

## Slide 6: Motor Controller
Original boat hardware
Waits for RC user input
Connects power to motor
Figure 2: Motor controller output waveform with 9.5V power supply

## Slide 7: Solar Panels
Five mini encapsulated solar cells
  5V, 2.5W
Voltage range: 14.35-25V
Power range: 8.7-12.5W
Figure 3: I-V Characteristic for Single Allpowers Solar Panel for Maximum Insolation

## Slide 8: Buck Converter Design
Solar voltage input: ~14-25V
Buck converter output: 6V
Figure 4: Power (W) vs. Load Resistance for single solar cell

## Slide 9: Buck Converter Schematic
Figure 5: Buck Converter Schematic

## Slide 10: Microcontroller
ATmega328p
Controls SPDT relay
Monitor XBee communication
Figure 6: Microcontroller schematic

## Slide 11: SPDT Relay
Normally connected:
  6V regulated solar voltage
Energized input:
  9.6V internal boat battery
Output to motor controller
Figure 7: Relay switching module

## Slide 12: Signal Strength Detection
Logarithmic amplifier - AD8307
Vout = Vslope(Pin – Po)
  Vslope = 25V/dB
  Po = -84 dBm
  Vout ~ 0.9 to 2V
Figure 8: Frequency spectrum output using RC

## Slide 13: Signal Strength Detection
XBee
  Radio communication module - 2.4GHz
RSSI
  Threshold: -99dBm
  Indicate with LED
Figure 9: RC XBee module

## Slide 14: Testing XBee
Distance (m) | RSSI | Power (dBm)
0 | 0x44 | -68
3.25 | 0x56 | -86
7.05 | 0x63 | -99
11.65 | 0x77 | -119
Table II: XBee data
Figure 10: XCTU Console

## Slide 15: Testing Solar Cells
Solar lamps mimic sun
Arduino Uno controls switching
Figure 11: Illuminated solar cells
Figure 12: Solar cell test setup

## Slide 16: Module Integration
Buck converter, relay, and XBee modules
Figure 13: Fully integrated modules

## Slide 17: Boat Integration
Enclosure for PCBs
5 mounted solar panels
Extra floatation
Figure 14: Boat fully integrated with design

## Slide 18
Figure 15: Full demo video

## Slide 19: Future Improvements
Solar cells with greater current capacity
Single PCB to go inside boat
Smaller PCB and display for RC
Proper waterproof enclosure
Increase RSSI sensitivity
Better floatation

## Slide 20: Thank you!
Yamuna Phal
Professor Xiaogang (Oliver) Chen
Professor Arne Fliflet
Professor Arijit Banerjee
Professor Michael Oelze
Figure 16: ECE 445 Team #5