## Slide 1: RF Range detection and alert system team 26
Rebecca Cole, aaron sowers, sameeth gosike
TA: Channing philbrick
Notes: Aaron

## Slide 2: Introduction and Objective
Goal: Detect and Alert the user of the RC Car’s range and relative location
Implementation:
  Bluetooth Communication
  GPS Modules
  RSSI (Received Signal Strength Indication) Chip
  OLED (Organic Light Emitting Diodes) Display
Notes: Becky

## Slide 3: Design: Block Diagram
Main Features:
  Power Supply
  RF Power Detection
  Directional Sensing
  Control Unit
  Alert System
Notes: Aaron
- Needs new block diagram

## Slide 4: Top Level R&V
Notes: Aaron
Becky – Change so it says Y/N instead of colors; Change Achieved to Integrated

## Slide 5: Power Supply
Regulates 9.2V Battery down to 3.3V Supply
Goal: = 3.3V +/- 5%
Notes: Becky

## Slide 6: Power Supply: Verification
Verification:
  Utilized Power Supply to Sweep from 5-10V to verify the 3.3V output

## Slide 7: RF Power Detection
RF detection circuit for 27 MHz signal
RSSI Chip - Scales input power logarithmically
Utilizes Bandpass Filter
Notes: Aaron
Order of bullet points
Mention Bandpass Filter application

## Slide 8: RF Power Verification
Simulation results for 27 MHz bandpass filter
Notes: Aaron
- Mention 3 dB

## Slide 9: Control Unit
Took inputs from RF Power Detection, GPS and Bluetooth Modules to communicate range and GPS coordinates to Alert System
Verification:
  Implemented RF Power Detection and passed values over the Bluetooth to display on Alert System
Notes: Becky

## Slide 10: Microcontroller
Designed for ATmega328P
  Prototyping utilized Arduino Uno and RedBoard
Capable of handling the desired peripherals
  SPI
  I2C
  Analog Inputs

## Slide 11: Bluetooth Module
Utilized SparkFun Bluetooth Mate Gold
  RN-41 Class 1 Bluetooth Chip
Bluetooth Module Features:
  Range greater than that of the car
  Able to communicate with 2 digital pins or SPI communication
Notes: Becky
- Bullet point order

## Slide 12: Control Unit: Code
Notes: Becky

## Slide 13: Alert System
Display relative location and direction fed from the GPS and RSSI units
Utilizes Adafruit OLED Display and Arduino microcontroller
Verification:
  Modified print rate on OLED display through code delays to implement a reasonable refresh rate
Notes: Becky

## Slide 14: Alert system: Code
Notes: Becky

## Slide 15: Directional Sensing
Responsible for providing relative location between user and car
Implemented with Adafruits Ultimate GPS module built around MTK3339 chip
Verification
  Updates data at rate of 10 Hz
  Provided NMEA sentences with both longitudinal and latitudinal coordinates
  Accurate within only about 50m of true location

## Slide 16: Directional Sensing: code

## Slide 17: Full Board Circuit Schematic
Notes: Aaron:
Highlight its flexibility within the chip – for the OLED display/RSSI is only on one side of the chip but can be implemented on both
- Trim it down / Move so it is better organized

## Slide 18: Challenges: Power Supply and Control Unit
Power Supply:
  Verification for the Battery was not well established
  Implementing a proper load difficult
  Correct Resistors were difficult to find
Control Unit:
  Bluetooth and GPS both needed SPI communication
  Bluetooth passed only characters between serial terminal
Notes: Becky

## Slide 19: Challenges: Alert System And RF Detection
Alert System:
  OLED Library size
  Display Refresh Rate
RF Detection System:
  Antenna length
  Weak Transmitter Power
Notes: Becky and Aaron

## Slide 20: Challenges: Directional sensing
GPS Module
  Location data GPS provided was accurate only up to about a hundredth of a minute
  Difficult to capture true location points of user and car
  This made calculating relative location between the user and car inaccurate since car being used had a reliable range of about 15 feet

## Slide 21: Challenges: Integration
Low memory issues from the size of the libraries caused hesitation during integration
Some PCB board layout issues due implementation changes
Notes: Aaron

## Slide 22: Conclusion
Achievements:
  RSSI successfully integrated with the Bluetooth and OLED Display
  GPS Module integration difficulty
Further Plans:
  Integrate GPS Module
  Integrate onto new PCB and RC Car
Notes: Becky

## Slide 23: Questions?