## Slide 1: App controlled solar powered street lamp
Project Group #2
Kevin Dahm, Justin Lindstrom, Brendan Weibel

## Slide 2: Introduction

## Slide 3: Project Introduction
Rural areas often do not have infrastructure to use traditional power sources
Lighting driveways and streets are important for safety of homeowners
Solar power creates portability and longevity of a street lamp
Controlling a light from the comfort of your home is important for a user’s experience

## Slide 4: Objective

## Slide 5: Objectives
The street lamp will create a brightness of at least 3000 lumens over a wide area
Due to long night conditions, lamp must be able to function for a minimum of 8 hours
Battery charge must be remotely checked
LED must be able to be controlled remotely
  Dimming
  Turning on/off

## Slide 6: Design Overview

## Slide 7: Design – block diagram

## Slide 8: Design – pcb

## Slide 9: Requirements

## Slide 10: Requirements – power
Requirement | Verification
Regulates a voltage input of 12V to 23V to a safe charging voltage of 13.14V to 14.5V Input 17.5 +/- 10%; Output 14.3V +/- 10% | Generate 3V input. Monitor output voltage and save data. Slowly step up input to 23V while measuring. Maintain 23V for an hour to see temperature changes. Verify it stayed in desired range. Connect Battery charger to fully discharged SLA battery. Measure voltage and current at battery terminals. Ensure all charging stages are met.

## Slide 11: Requirements – control
Requirement | Verification
Must be able to view the battery charge and turn off/on the light from a mobile application | Once user opens the app, user can see a value of percent charge of the lamp as well as a visual representation of that percentage. The user also sees a large switch on the screen which has on and off buttons in order to turn the lamp on and off.
Must be able to communicate with a cell phone over Wi-Fi from a range of 250 feet | Configure ESP32 to connect to Wi-Fi Place lamp 250 feet away Connect to Wi-Fi on Phone Communicate with lamp by changing brightness on the phone
Must be able to change the brightness of the lamp | Turn on the lamp at low brightness Slowly increase brightness on the application Probe output on oscilloscope to see change in PWM

## Slide 12: Requirements – lighting
Requirement | Verification
Must sufficiently illuminate dark area while using 33W | Use Voltmeter to find the current and voltage drop through the device while it’s on. Ensure it is drawing 33W of power over 12V. Turn off other lights and ensure it provides adequate lighting to the surrounding area
Must be able to visibly change brightness of the lamp | Vary output voltage into lamp from power source View change in brightness

## Slide 13: Power module

## Slide 14: Solar panel
Renogy 100 Watt 12 Volt Monocrystalline Solar chosen
Power requirements determined LED would be on 100% for 4 hours, and 50% for 4 hours each day (220 Wh per day)
Urbana, IL average sunlight would result in this panel receiving 365.5 Wh per day

## Slide 15: Battery Charger – Summary
Will regulate the power coming in from the solar panel to provide the necessary voltage that our battery will accept
BQ24450 integrated charge controller for lead-acid batteries
  Voltage and Current regulation using this chip
  Temperature-compensated reference necessary
2 Charging Modes
  Boost Mode
  Float Mode

## Slide 16: Battery charger – Circuit

## Slide 17: Battery charger – Calculations

## Slide 18: Battery
12 V
SunXtender PVX-340T
 | Absorption Voltage at 25° C | Float Voltage at 25° C
Volts Per Cell | 2.37 – 2.40 V | 2.20 – 2.23 V
For 12V System | 14.2 – 14.4 V | 13.2 – 13.4 V

## Slide 19: Battery charger – Results
Boost to Float Transition Point
Chart: Charging Current vs. Terminal Volage
| 12.4 | 12.6 | 12.8 | 13.0 | 13.2 | 13.4 | 13.6 | 13.8 | 14.0 | 14.02 | 14.04 | 14.06 | 14.08 | 14.1 | 14.12 | 14.14 | 14.16 | 14.18
 | 3.02 | 3.02 | 3.02 | 3.02 | 3.02 | 3.01 | 3.01 | 3 | 2.94 | 2.9 | 2.87 | 2.68 | 2.55 | 2.47 | 2.21 | 1.89 | 1.53 | 1.04

## Slide 20: Control Module

## Slide 21: microcontroller
ESP32 can work as a standalone Wi-Fi and Bluetooth device
ESP32 achieves ultra-low power consumption through its own proprietary software
EspressIf has built an Arduino Development Platform

## Slide 22: Android application - UI
Single Screen Design
Three Functionalities
  Battery Life Check
  Explicit On/Off
  Brightness Scaling

## Slide 23: Android application - Logic
Yes
No
off
Yes
No

## Slide 24: Wi-Fi connection
Uses ESP32 to create a local web server on device within the user’s home Wi-Fi network
Utilizes WiFi.h class and uses a hard-coded ssid and password
Continuously checks if server is available to continue running server
Sends simple response for accesses

## Slide 25: Lighting module

## Slide 26: Led Design Decisions
Use 12 volt, 3000 lumen bulb
To allow control, need use of microcontroller
Microcontroller voltage too small, need “relay”
Provide dimming functionality through PWM
Use MOSFET as relay to allow for fast switching of PWM

## Slide 27: Dimming Design

## Slide 28: Dimming Implementation

## Slide 29: PWM Output – 20% Brightness

## Slide 30: PWM Output – 80% Brightness

## Slide 31: Dimming Verification
Chart: Power Consumed by LED vs Set Brightness
| 0.0 | 25.0 | 50.0 | 75.0 | 100.0 | 125.0 | 150.0 | 175.0 | 200.0 | 225.0 | 250.0 | 255.0
 | 0 | 1.2 | 2.7 | 6.4 | 11.01 | 14.53 | 18.03 | 20.61 | 23.23 | 25.93 | 28.52 | 28.92

## Slide 32: Successes and Challenges

## Slide 33: Successful Final Design

## Slide 34: successes
All of our requirements were met by our demo
Control Module
  Strong connection between phone and lamp system
Lighting Module
  Full dimming capabilities
  Extremely bright light
Power Module
  Clearly saw regulating voltage and current into the battery
  Differences between float and boost modes

## Slide 35: challenges
We were unable to test our system with the correct solar panel
  We used a power supply to simulate output voltage from solar panel
  Unable to determine where system would operate on the IV-curve
Battery state of charge has a high probability of error because we used a mathematical model to find the value
An additional PCB iteration would have created a design that would be easier to work with as we have “hacked” our way to a functioning circuit by using additional components

## Slide 36: Further work

## Slide 37: Maximum Power Point Tracking
Adding MPPT with impedance matching will allow device to be fully functional with solar panel and maximize efficiency.

## Slide 38: Voltage Regulator
Add a 12v to 5v voltage regulator from the battery to the microcontroller.
  Prevent the need for secondary power source

## Slide 39: State of Charge
State of charge measurements with less margin of error.
  Finding the most accurate method for calculating the state of charge would improve user satisfaction and overall quality of device.

## Slide 40: Conclusion

## Slide 41: Safety And Ethics
Due to the potential hazards of charging and discharging a Lead-acid battery, the IEEE’s Code of Ethics codes #1 and #9 were adhered to in the strictest way possible.
Furthermore, Dealing with a light that is approximately 3000 lumens needed to be considered so that consumers of this product would not damage their eyes.

## Slide 42: Final Thoughts
Successfully charged 12v AGM battery in laboratory setting.
Effectively controlled LED with mobile application using wireless communication.
Maintained small size to aid in the portability of commercialized product.

## Slide 43: Questions?