## Slide 1: Music-Visualization and Motion-Controlled LED Cube
ECE 445 Spring 2018 Team 34
Hieu Huynh
Islam Kadri
Zihan Yan
TA: Zhen Qin

## Slide 2: Team Members:
1. Hieu Huynh – Electrical Engineering
  Software Engineering – General
2. Islam Kadri – Computer Engineering
  Software Engineering – General
3. Zihan Yan –Electrical Engineering
  Digital Circuits and Hardware Design

## Slide 3: Problem Statement
Music visualization devices are usually expensive to build, fix, and buy and are generally limited to pre-programmed displays or only use a sound’s frequency input to affect the visualization. For example, Kinetic Rain, a bronze droplet and steel wire based kinetic art piece, in Singapore’s Changi Airport, cycled over 16 pre-programmed shapes and cost several million dollars to build. Additionally, these devices don’t allow for user interaction which can take away from the entertainment value of the device.

## Slide 4: Proposed Solution
Building a device that allows music visualization and user interactivity by using an 8x8x8 RGB LED grid would take advantage of LED technology’s efficient and aesthetically pleasing properties, as well as be economically efficient. Using the amplitude and direction of arrival, in addition to the frequency, the device will be able to display better looking visuals. Furthermore, by implementing a 3D Snake game, the user will have a medium to interact with the device and increase its entertainment value. This will be done using sensors to track the user’s hand movements.

## Slide 5: High Level Requirements
1. Device correctly extracts the information from the sound in an accurate manner.
2. The LED cube can reflect the frequency, amplitude, and direction of arrival of the sound.
3. Device can correctly pick up the user’s hand motion and properly control the Snake based on that information.

## Slide 6: Block Diagram

## Slide 7: Physical Design
Bird Eye View
Side Views

## Slide 8: Schematic: LED Module
Shift Registers
LEDs

## Slide 9: Requirements: Microphone Module
1. Components:
  4 Electret Microphones
  1 Digital MEMS Microphone
2. Requirements
  Microphones must have frequency response from 50Hz to 20kHz
  Microphones must have high SNR and high sensitivity
  Electret Microphones’ output must be amplified to be in range 0-5V
  Output of Digital Microphone must have I2S format

## Slide 10: Schematic, Requirements: Microphone Module
Electret Microphones and Amplifier Circuit
Digital MEMS Microphone
Digital MEMS Microphone
Frequency Response: 50Hz-20kHz
SNR: 64dBA
Sensitivity: -26dB +/-1dB
Output Format: I2S
Electret Microphone:
Frequency Response: 20Hz-20kHz
SNR: 60dBA
Sensitivity: -44dB
Amplifier Circuit:
Gain: 20x

## Slide 11: Proof of Concept: Microphone Module
Electret Microphone and Amplifier Circuit

## Slide 12: Requirements, Schematic: Proximity Sensor Module
Components
  3 Ultrasonic Sensors (HC-SR04)
2. Requirements
  Ensure that sensors can detect the position of hand when hand is moving and motionless in range of 3cm to 1m.

## Slide 13: Schematic: Power Module
Total Power Consumption: 16W.
Uses DC 5V 8A 40W AC To DC Power Adapter
http://www.gadgetronicx.com/guide-build-3-3v-power-supply-circuit/

## Slide 14: Requirements: Control Unit
Requirements:
  1. Correctly controls the color of LEDs and updates LED cube with rate of 100Hz
  2. Correctly computes the frequency spectrum of sound with frequency resolution of at most 160Hz
  3. Correctly extracts the amplitude of input sound
  4. Correctly estimates the direction of arrival of sound
  5. Estimate movement of user’s hand in 6 directions
  6. Use user’s hand movement to drive Snake game

## Slide 15: Requirements: Control Unit
  Requirement 1: Correctly controls the colors of LEDs and updates LEDs cube with rate 100Hz
1. To control LEDs’ colors: Use Bit Angle Modulation (BAM) Method
  Use 4-bit BAM  16x16x16 = 4096 colors
2. To update LEDs cube with rate 100Hz:
  Arduino shifts out 200 bits to update each layer of LEDs every 1.25ms
     Update 1 layer with rate 1000/1.25 = 800Hz
     Update LEDs cube with rate 800/8 = 100Hz

## Slide 16: Requirements: Control Unit
Requirement 2: computes the frequency spectrum of sound with frequency resolution of at most 160Hz
To compute frequency Spectrum: Use 256-point FFT.
    256-point FFT provides Fs/256 = 40000/256 = 156.25Hz frequency resolution
    Have 40k samples/sec
     Need to compute 256-point FFT 157 times/sec
     Compute 256-point FFT every 6ms

## Slide 17: Requirements: Control Unit
  Requirement 3: Correctly extract the amplitude of input sound
    Compute the exponential moving average using following formula:
with  = 0.125
Why?
Influence of past sample decreases exponentially fast  Fast update
Maintain stability when there is sudden spikes in amplitude

## Slide 18: Requirements: Control Unit
  Requirement 4: Correctly estimates the direction of arrival of sound
  To estimate the direction of arrival of the sound:
  Compute 4 exponential moving averages of signals received from 4 electret microphones using the following formula:
  For every second, find which microphone has the highest average amplitude by comparing 4 average values
  Determine the direction of arrival
with  = 0.125

## Slide 19: Requirements: Control Unit
  Requirement 5: Estimates movement of user’s hand in 6 directions

## Slide 20
Flowchart: Ultrasonic Proximity Sensor

## Slide 21: Proof of Concept: Proximity Sensor Module

## Slide 22: Requirements: Control Unit
  Requirement 6: Use user’s hand movement to drive Snake game

## Slide 23
Flowchart: Snake Game