## Slide 1
ECE 445 | Fast, Low-Cost Swarm Robots
By Michael Bartmess, Peter Cork, and Paul Ernst

## Slide 2
Swarm Robots | Overview
Project was to design and build a fleet of robots
Each robot can:
  Can move quickly and independently
  Have their current position calculated
  Will converge on a destination position
Purpose:
  Visualizing transitions and shapes
  Platform to test route planning algorithms
  Evaluate using machine vision in real time for control purposes
Final Robot Design

## Slide 3
Swarm Robots | Demonstration

## Slide 4
Swarm Robots | Control Loop
Capture Image of Field
Compute Position and Orientation
Compute Motor Commands and Send
Move Robots

## Slide 5
Swarm Robots | Hardware
Two main systems:
  Vision System
  Robot System
Robot Main Logic Board, Top and Bottom View

## Slide 6
Project | Hardware: Vision System Block Diagram
Laptop
Control System
Vision Software
WiFi Connection
USB
Webcam
USB
Router
To Robots
802.11n
120V AC
120V AC
5V

## Slide 7
Swarm Robots | Hardware: Vision System Requirements + Verification
Requirement: | Verification:
Be 1080p to provide high enough resolution | Pass, 1920x1080 image
Able to stream at least 10fps | Pass, capable of 30fps
Requirement: | Verification:
Fast enough to analyze a frame in under 100ms | Pass, can analyze at 15fps
Requirement: | Verification:
Transmit and receive a 2.4 GHz signal | Pass
Transmit 8 packets of 16kB in under 100ms | Pass, though our packets were significantly smaller
Connect to 8 devices at one time | Pass
Webcam:
Laptop:
Router:

## Slide 8
Swarm Robots | Hardware: Robot System Block Diagram
ESP8266 SoC
WiFi Connection
Antenna
Processor
Flash
To Router
UART
Programming Pins
GPIO
Power Block
5V Power
Battery Charger
3.3v LDO Regulator
Li-Ion 4.2v Battery
5V
4.2V
4.2V
3.3V
Motor Block
Motor Controller IC
4.2V
PWM
Left Motor
Right Motor

## Slide 9
Swarm Robots | Hardware: SoC Block
Used ESP12-S SMT Module
Switches for Reset and Program
General purpose Red LED
GPIO 4, 5, 12, and 13 for Motor Controller

## Slide 10
Swarm Robots | Hardware: SoC Block Requirements and Verification
Requirement: | Verification:
Be fast enough to respond to compute and respond to loop corrections in under 100ms. | Pass, but not relevant in final implementation
Be able to connect to a 2.4GHz signal. | Pass
Can transmit 2 PWM signals simultaneously. | Pass, capable of driving the two motors independently
Runs reliably between 2.95v and 3.4v | Pass, No measurable change in packet loss at 15ft
Consumes less than 200mA while transmitting | Pass, transmission draws 90mA when sending and receiving packets at 100Hz

## Slide 11
Swarm Robots | Hardware: Power Block
5v provided when plugged in
Charges battery at 100mA (ish)
LED for charging feedback
LDO produces 3.3v output

## Slide 12
Swarm Robots | Hardware: Power Block Requirements and Verification
Requirement: | Verification:
Charging Circuit: Able to charge the battery in less than 1 hour. | Mixed, correct circuit charges in 4 hours, swapping resistor 1 and 2 causes charging in 40 minutes
Voltage Regulator: Able to maintain a voltage output between 2.95V and 3.4V over an input range of 3.5V to 4.2V | Pass, voltage ranges between 3.27V and 3.29V
Voltage Regulator: Able to provide 500mA of steady state current | Pass, No degradation while drawing 500mA
Battery: Able to provide 500 mA for 30 mins | Pass, stayed in operation for over 30 minutes
Battery: Output voltage stays between 3.5 and 4.2V | Pass, min voltage seen was 3.7V, max was 4.18V

## Slide 13
Swarm Robots | Hardware: Motor Block
Uses DRV8833 as controller
Current limits to 1A draw per motor (Eq. 1)
Digital PWM signals amplified
Bidirectional control for each motor

## Slide 14
Swarm Robots | Hardware: Motor Block Requirements and Verification
Requirement: | Verification:
DC Motor: Draw less than 150mA with no load at 4V | Fail, Draws 190 mA, but since the power profile of the SoC was 100mA under what we expected this was a non-issue
Motor Controller: Operate from 3.7 to 4.2V | Pass, some mild speed changes
Motor Controller: Be able to run a DC motor bidirectionally | Pass

## Slide 15
Swarm Robots | Hardware: Layout
2 layer
6 mil signal traces
10 mil power traces
All SMT components
0805 footprint for passives
Antenna keep-out area
Top Layer:
  SoC
  Motor Controller
  Charge and Status LEDs
  Battery Connector
Bottom Layer:
  Push Buttons
  Most Passives
  Voltage Regulator and Charger IC
Top Layer
Bottom Layer

## Slide 16
Swarm Robots | Hardware: Physical Design
3D printed chassis
3 discrete parts per chassis
Footprint of 29.7cm2
Battery located on bottom
Motors connect to right angle male 0.1" headers
Top used for vision target

## Slide 17
Swarm Robots | Software
Camera configuration
Computer Vision:
  Feature Recognition
  Position Extraction
Formation design
Control loop
Network connection
Robot Firmware

## Slide 18
Swarm Robots | Software: Feature Recognition
Using Open CV library in Python
Uses ORB algorithm to find features:
  Fast, free algorithm for corner detection
  Has difficulty near edge of image
  Has difficult when many corners near each other
Software steps:
  Convert image to black and white
  Process with ORB
  Group similar/duplicate corners
  Match corners to form rectangles
  Pass to position extraction block
Feature Recognition Stages

## Slide 19
Swarm Robots | Software: Position Extraction
Extracts the position, orientation, and ID
Software Steps:
  Using rectangles found from last step
  Sample colors of quadrants to form ID
    Uses YIQ color space for greater separation
  Use long color bar to calculate orientation
  Use center of rectangle for position
Position Extraction Stages

## Slide 20
Swarm Robots | Software: Formation Design
Allows for "matched" endpoints
  Each robot has a specific destination
  "Unmatched" endpoints possible, though not implemented
Series of matched endpoints allow for more complicated transitions
  Similar to a marching band
Software Steps:
  Load in the saved endpoint file
  Set endpoints for robots
  Wait for robots to move to endpoint
  Adjust to final orientation
  Wait 0.5 seconds to verify convergence

## Slide 21
Swarm Robots | Software: Control Loop
Uses position data and endpoint
Required to account for motor non-idealities
Computes motor power for each robot
Software Steps:
  Compute distance between robot and endpoint
  Calculate angle to travel to endpoint
  Send pure rotation commands until pointing towards endpoint
  Move forward
  On approach, use cool-down and time-to-run
    Time to run sets timeout on command
    Cooldown prevents accepting a new command
"Second Degree" PWM

## Slide 22
Swarm Robots | Software: Network Connection
Uses UDP packets over 802.11n
Maintains a dedicated connection to each robot
Robots send packets back
  Status of robot
  Debug information
Computer sends robot packets every 66ms
  Power for the motors
  Run time
  "Cooldown" time
Packet to Computer from Robot |  |  | 
"S" | "T" | "A" | "T"
Version | Cooldown | Reserved | 
Total Sent Packets |  | Time to run | 
Total Received Packets |  | Robot ID 0 | Robot ID 1
Robot ID 2 | 0xFF | Reserved | 
Packet to Robot from Computer |  |  | 
"C" | "T" | "R" | "L"
Version | Cooldown | Rotational Command | 
Straight command |  | Time to run | 
Flags |  | Robot ID 0 | Robot ID 1
Robot ID 2 | 0xFF | Reserved | 

## Slide 23
Swarm Robots | Software: Robot Firmware
Connects to router
10ms control loop
  Reads packet
  Sets motor speed via PWM
  If packet contains a cool down, block incoming packets
Over-the-air updates
  Automatic updates if robots running old version
  Allowed for removing dedicated USB-to-UART chip
Programmed in C

## Slide 24
Soldering PCBs
  31 components per board
  496 components soldered in total
Assembling Robot
  Shortening and resoldering the motor and battery wires
  Press-fit motors into housing
  Wheels are screwed onto motors
  Top slides on
Swarm Robots | Assembly

## Slide 25
Swarm Robots | Failure Analysis
3 Primary Failure Modes:
  Ohmic short across push buttons
  Poor solder joints on motor controller IC
  Charger IC not working
82% of robots failed at some point
56% of robots were restored to working condition
Mitigations:
  Different push buttons, and more liberal use of flux remover
  Better soldering technique
  Proper layout review to catch silkscreen mismatch

## Slide 26
Swarm Robots | Looking Forward
Hardware:
  Reduce footprint
  Add failure mitigations
  Add off switch
  Use real connector for charging/programming
  Use better motors
  Setup for faster charging
  Add battery voltage view
Software:
  Improve vision detection run time
  Collision detection
  Automatic ID of robots
  Unmatched endpoint setup
  Velocity control

## Slide 27
Questions?