## Slide 1
Maximum Power Point Tracker for a Wind Turbine
Team #11
By: Alec Biesterfeld, Tyler Rasmussen, Ben Scrementi
TA: Evan Widloski

## Slide 2
Maximum power tracking system for the WindTura 750 turbine
Suitable for home-scale wind power systems
Introduction
2

## Slide 3
Track maximum power at various wind speeds using a digital controller to adjust the load presented to a turbine
Dissipate up to 750W to a resistive load
Low-cost and accessible solution (<$200)
Objectives

## Slide 4
Adjust load presented to the system via power converters
At smaller loads, turbine spins slower
At higher loads, turbine spins faster
Optimal speed controlled by the duty cycle of the converter
What is Maximum Power Point Tracking (MPPT)?
4

## Slide 5
System Overview

## Slide 6
To Turbine
To Load
To Wall Outlet
To Sensors on Turbine
6

## Slide 7
3 Phase, Full-Wave Rectifier
Function:
  Receive input from a three-phase PMA
  Supply a DC voltage to the DC/DC subsystem
AC/DC Converter Subsystem

## Slide 8
AC/DC Schematic

## Slide 9
Functions:
  Process sensor input
  Calculate system parameters
  Algorithmically determine the optimal duty cycle
  Output system parameters to the display
Components:
  Sensor units
  Microcontroller
  System Display
Controller Subsystem

## Slide 10
Control System Board Schematic

## Slide 11
Software Control Algorithm

## Slide 12
Display Screens:
System Display

## Slide 13
Anemometer
  Provide analog output voltage to ATMEGA328p ADC
  Use provided LUT to convert voltage to wind speed (m/s)
Anemometer (Wind Sensor)

## Slide 14
Hall Effect Sensor
  Digital output high upon pass of a magnet
  Used to calculate rotational speed
Hall Effect (RPM) Sensor
LOW
HIGH
T1
T2

## Slide 15
Voltage Sensor
  10 kΩ and 3.3 kΩ for voltage divider
  Convert output voltage to 5 V logic
Current Sensor
  Four 15 Ω, 0.5W resistors for final demonstration
  ACS758 used for higher currents
Control System Sensor Units

## Slide 16
Atmega328p, 28 DIP package
Programmed using an Arduino bootloader and Arduino IDE
Microcontroller
Pin Number | Pin Name | Design Function
4 | PD2 | LCD Display
5 | PD3 | LCD Display
6 | PD4 | LCD Display
11 | PD5 | LCD Display
12 | PD6 | LCD Display
13 | PD7 | RPM Sensor
14 | PB0 | LCD Display
15 | PB1 | DC/DC PWM Signal
16 | PB2 | LED warning light
23 | ADC0 | Voltage Sensor
24 | ADC1 | Current Sensor
28 | ADC5 | Wind Sensor
16

## Slide 17
Purpose
  Adjust the load presented to the turbine by changing its duty ratio
Components
  Gate driver IC
  Boost Converter
DC/DC Converter

## Slide 18
Should be able to operate at up to 800W
Should have an output voltage ripple of ±3% of the output voltage at 100W, ±10% at 800W
Should be at least 80% efficient at up to 800W, 90% efficient at up to 100W
DC/DC Converter Requirements

## Slide 19
Originally used a SEPIC converter in order to be able to adjust the voltage out of the turbine up or down
  Lower efficiency
  Didn’t work well at low switching frequencies
  Thermal issues
Switched to a boost converter
  Higher efficiency
  Still able to adjust the turbine’s speed up or down
Topology Selection

## Slide 20
LTSPICE Boost Simulation
20

## Slide 21
= 24mV = .2% of minimum output voltage
LTSPICE Boost Simulation
21

## Slide 22
DC/DC Converter Schematic

## Slide 23
Gate Resistor Selection
VOUT
VOUT
VGATE
VGATE
RG=110 Ω
2V Voltage Spike
η = 88.7% at 75W
RG=220 Ω
1V Voltage Spike
η = 86.6% at 70W

## Slide 24
Boost Converter Results
RLOAD | 7Ω
Duty Ratio | 29%
VIN | 19.63V
PIN | 98.1W
VOUT | 25.1V
POUT | 90.1W
Efficiency | 91.8%
Required Efficiency | 90%
VOUT Spikes | 3.5V
Required Ripple | < 0.75V
24

## Slide 25
Boost Converter Results
RLOAD | 8.33Ω
Duty Ratio | 33.5%
VIN | 38.2V
PIN | 337.6W
VOUT | 50.94V
POUT | 309.4W
Efficiency | 91.63%
Required Efficiency | 85%
VOUT Spikes | 14V
Required Ripple | < 2.5V
25

## Slide 26
Dynamometer Testing
26
https://photos.app.goo.gl/L5j9qSB3Cxwuy1kz5
Notes: https://photos.app.goo.gl/L5j9qSB3Cxwuy1kz5

## Slide 27
For a 14 Ω load and 5.5 Nm of torque from the dynamometer, data was collected at different duty ratios
Testing limited by dynamometer’s current limit
Dynamometer Testing
Duty Ratio | 20% | 25% | 35%
RPM | 434 | 380 | 268
PIN | 216.0W | 181.8W | 122.4W
VOUT | 50.8 | 47.2 | 37.5
POUT | 187.7W | 156.9W | 101.4W
Efficiency | 86.9% | 86.3% | 82.84%
Required Efficiency | 80% | 80% | 80%

## Slide 28
Used an industrial fan to simulate wind
Connected to 100 Ω load and power meter
Max output ~ 350mW
Fan Testing
28

## Slide 29
Fan Testing Results
Peak at 48%
Peak at 36%

## Slide 30
Fan Testing Results
High Fan Speed
Low Fan Speed
Stabilizes between 36-44%
Stabilizes between 40-48%

## Slide 31
Fan Testing Results
Peak at 48%
Peak at 36%
Converged around 42%
Converged around 43.5%

## Slide 32
Boost Converter Simulation

## Slide 33
Block Diagram of System

## Slide 34
Step input had an amplitude of 1 and a 1 second step size
The step input was meant to represent mechanical input from turbine
Step Response without Boost Converter

## Slide 35
Project Costs
Goal: Less than $200
35

## Slide 36
Effective maximum power point tracking demonstrated in a laboratory setting
Power electronics proven to be able to operate above 300 W
Successful interface with the WindTura 750 turbine system
Conclusions

## Slide 37
Improved testing conditions (wind tunnel, outside in relatively high winds)
Tune the response time of the power tracking system
Integration of a battery in order to create a complete off-grid power solution
Future Work

## Slide 38
Evan Widloski
Prof. Haran
Kevin Colravy
Prof. Raginsky
Prof. Banerjee
Acknowledgements
38

## Slide 39
Questions?
Thanks for listening!