## Slide 1
Parking Reservation System
Team 59
Vivek Calambur, Manjesh Mogallapalli, Ojus Deshmukh

## Slide 2
Introduction
Presented By: Vivek Calambur

## Slide 3
Parking spots not well implemented in busy areas
  Hard to find
  Highly limited spots
  No guarantee of availability
  Payment can be a hassle
Problem Statement

## Slide 4
Internet connected parking meters
  Each meter detects and displays spot availability
  Spot availability displayed on mobile app
  Mobile app allows users to make reservations
The Solution

## Slide 5
Hardware (meter):
  Sends sensor (RFID, Ultrasonic) data to backend
  Displays spot status on LCD
Backend:
  Handles RFID verification and reservation logic
  Sets LCD color
App:
  Displays spot availability
  Allows users to make reservations
System Overview

## Slide 6
Hardware
Presented By: Ojus Deshmukh

## Slide 7
Power Supply
Components
Sensors
Controllers
Pseudocode
PCB Design
Hardware Overview

## Slide 9
Power Supply Subsystem

## Slide 10
Parking Meter Subsystem

## Slide 11
Circuit Diagram

## Slide 12
Device Characteristics
Component | Voltage | Current
Microcontroller(ATMega 328-P) | 5V | 7-15 mA
Ultrasonic Sensor(HC-SR04) | 5V | 15 mA
RFID Reader(ID-12LA) | 5V | 15 mA
WiFi Module(ESP8266-01) | 3.3V(Supplied using 3.3V regulator) | 67-500 mA
LCD Screen + RGB Backlight(NHD-0216K3Z) | 5+1.9, 2.9, 2.9 V | 15 + 15, 20, 20 mA

## Slide 13
Previously used
Cheap
Easy to use with existing libraries
ATMega 328-P Microcontroller

## Slide 14
Tx/Rx pins simulated using SoftwareSerial library
Built-in antenna
Labeled as 12 cm read range
Actually close to 5 cm
ID-12LA RFID Reader

## Slide 15
16x2 character LCD
I2C communication using Wire I2C library
RGB backlight
NHD-0216K3Z LCD Screen

## Slide 16
400 cm detection range
Up to 15 measurements/second
Low-cost, easy to implement
HC-SR04 Ultrasonic Sensor

## Slide 17
3.3 V power
ESP-Firebase library
Built-in antenna
Low cost, easy to implement
WiFi Module ESP8266-01

## Slide 18
Take 10 measurements over 3 seconds
Ultrasonic sensor often reports false readings
Spot is only marked open/closed if all 10 measurements agree
Ultrasonic Algorithm

## Slide 19
When RFID tag is in range, serial communication becomes available
Parse out start-of-transmission characters and newline/carriage return to get RFID data
RFID Communication

## Slide 20
Start I2C Communication
Define I2C Device Address
Send data prefix, followed by data
End I2C Communication
LCD Communication

## Slide 21
Main PCB (Design)

## Slide 22
Main PCB (Board)

## Slide 23
Front PCB (Design)

## Slide 24
Front PCB (Board)

## Slide 25
Backend
Presented By: Vivek Calambur

## Slide 26
FirebaseArduino library for ESP8266
Firebase RTDB as primary database
Google Cloud Functions
Python 3 with Pyrebase library
Backend Technology

## Slide 27
Backend Data Flow

## Slide 28
ESP8266 has four main functions:
  Receive sensor data
  Send sensor data to Firebase
  Listen for Firebase changes
  Send updated LCD info
ESP8266 Communication

## Slide 29
Communication to microcontroller through serial
  Connected to TX/RX pins
  Used start and end characters
Communication to Firebase through library
  FirebaseArduino library
  Used event listeners extensively
ESP8266 Communication (cont.)

## Slide 30
Hosted on Google Cloud Functions
Function called on reservation creation
  Triggered by HTTP POST request
Ensure that reservation has available spot
Spots assigned in most efficient manner
Spot Assignment Algorithm

## Slide 31
Spot Assignment Algorithm (cont.)

## Slide 32
Cases:
  User has insufficient balance (FAIL)
  All spots are taken during timeslot (FAIL)
  Spot available for reservation (SUCCESS)
On success, push to Firebase
On failure, display error message on app
Spot Assignment Algorithm (cont.)

## Slide 33
Hosted on Google Cloud Functions
Needed for two reasons:
  Enforce correct user for reservations
  Payment
Function called on user parking in spot
RFID Verification

## Slide 34
RFID Verification (cont.)

## Slide 35
Hosted on Google Cloud Functions
Necessary for two reasons:
  Enforce on reservation overstay
  Cleanse unused reservations
Triggered on a cron job (every minute)
Reservation Enforcement

## Slide 36
Mobile App
Presented By: Manjesh Mogallapalli

## Slide 37
Users create account
Monitor Spot Availability
Make Reservations
View Reservations with Spot Number
Mobile App Overview

## Slide 38
Mobile App Flowchart

## Slide 39
Create Account/User Profile

## Slide 40
Open Spots

## Slide 41
Make/View Reservations

## Slide 42
Conclusion
Presented By: Manjesh Mogallapalli

## Slide 43
Achievements:
  Users can view parking spot status in real-time
  Users can make reservations
  System can verify reservations via RFID
  System can enforce reservations/payment
Weaknesses:
  Ultrasonic reliability
Project Analysis

## Slide 44
Ultrasonic timeout
FirebaseArduino certificate issue
PUT vs. PATCH on Firebase
Wi-Fi chip pin configuration
New to mobile dev
Minor PCB mistakes
Challenges

## Slide 45
Explore alternatives to Ultrasonic Sensor
Refine software
Modify physical design
Future Improvements

## Slide 46
Kyle Michal
Soumithri Bala
Professor Arne Fliflet
Credits