## Slide 1: Power Demand Response System
Team 21
Antonio Martinez & William Widjaja
ECE445 Senior Design
Notes: Tony: Hellos, we created this project. I was in charge of Hardware
William: I am William, I was in charge of software

## Slide 2: The Problem
High demand for electricity creates stress on the grid
The increase in popularity of renewable resources lowers reliability of power generation
Together these issues result in low capacity factors of power plants, making them less efficient
Which increases costs.
The Objective and High Level Requirements
Create powerline communications between the supply and demand by transmitting bits at a reasonable speed
Use this communication to schedule power usage of homes
Make these schedules dynamic
Ultimately decrease the costs
Notes: William: So why did we choose this? In short, because there is a problem. 1) High demand during peak hours causes stress on the grid. 2) Increase in renewables. 3) And together, this causes more power to be generated than can be used, lowering capacity factors and raising the cost of overall electricity, since customers need to pay for energy that is ultimately wasted as heat if it can’t be stored.
Tony: our objective is to have the power plant dictate the power usage of each home through scheduling. Proper scheduling should in theory decrease peak loads, reducing stress, and increasing efficiency, which in turn decreases costs. On the slides, our three high level requirements match with objectives 1-3. That is to establish powerline communication, properly receive and execute the schedules, and to establish dynamic scheduling.

## Slide 3: Unscheduled Loads
The Old Way
Notes: So first, we should talk the use of a schedule. Let’s say it’s summer and everyone’s coming home from work around the same time, 5pm. Once everyone’s home, their AC kicks on, requiring lots of power and creating peak loads as seen on the slides.

## Slide 4: Scheduled Loads
The New Way
Notes: Now suppose we schedule this instead. House 1’s AC kicks on before the person’s home so their house is chilled before hand. Then House 2 AC kicks on afterwards to the same affect and so on. The way these loads sum create an overall constant and lower peak load.

## Slide 5: High Level Overview
The utility company dictates the schedules
Notes: William: So how do we do this? The schedule itself is controlled from the electric utility company. The customers opt into allowing for this control. The incentive being cheaper overall electricity bills for the customers. The power company sends a control signal onto the grid, which is received by slave relays which connect between the residential appliances and the stepped down grid. These relays then control when power is supplied to the devices

## Slide 6: Original Block Level Diagram
Our Initial Idea for the Project
Notes: Originally:
-We wanted the master node to directly connect to the wall. We would then need to do AC to DC conversion and add isolation transformers to protect the master and slave nodes. However, as we progressed through the semester and began simulating blocks of the circuit, we realized the focus should shift away from power conversion and more towards the power line communication to transmit and receive a schedule across the grid.

## Slide 7: Current Block Level Diagram
Necessary Changes
Notes: This lead us to a more specific and attainable design. Here, we simplified how power was supplied because our project is proof of concept.
This is a proof of concept wherein the grid does not need to be a high voltage line to properly demonstrate our high level requirements.
We also learned there’s more to powerline communication than modulation and demodulation, so our current block level diagram includes injection and extraction from the virtual grid.
Tony: Describe 3 blocks

## Slide 8: Modulation for Power Line Injection
Notes: Tony: A bit signal is modulated or multiplied with a higher frequency carrier signal to get the shape shown in the third figure. This new modulated signal retains the same data as the bit signal, but with high frequency components for every digital one. As the name implies, data is being carried by the high frequency signal when traveling across the grid.

## Slide 9: Demodulation: Digitization
Notes: Once the modulated signal is injected to and extracted from the powerline, demodulation must occur to so that our signal can become digitized and readable for our Slave microcontroller. Powerline injection requires our signal to go through capacitors which makes the signal positive and negative. Rectification is necessary to eliminate the negative. Then, a low-pass filter eliminates the high frequency carrier we no longer need. At this point we have the envelope of the modulated signal, it’s digitized. The comparator is part of the Slave microcontroller and confirms the signal is digital and ready to read.

## Slide 10: EagleCAD Schematics
Demodulator Circuit
Modulator Circuit
Notes: Real quickly, these are our eagle cad Schematics. Top right is the modulator circuit and bottom left is the demodulator circuit

## Slide 11: Entire Schematic
Notes: The whole schematic shows that we designed one PCB to act as either master or slave

## Slide 12: Complete Project Build
Demonstration of microcontroller controlled relay switching two LEDs representing appliances
Above is the final product that we used for our demo.
Notes: Our final product has the MASTER pcb module on the left connecting to the slave on the right over the powerline (virtual grid). The small breadboard above them holds the controlled appliances. The single LED is lit constantly, showing our modulated signal over the powerline does not affect unscheduled appliances. The right image is a gif of a relay working on scheduled appliances

## Slide 13: Master Node
1: Microcontroller 1: Generates the bit signal and the PWM high frequency carrier
2. Modulator Circuit: combines these signals through the use of BJTs
3. Powerline Injection Circuit: The operational amplifier gives the modulated signal some gain before the signal passes through a capacitor, onto the power line.
Notes: Now, a closer look at the Master Node shows 3 modules. 1, Microcontroller 1 generates signals for modulation. 2, the modulator circuit executes modulation, and 3, powerline injection prepares the signal to travel across the virtual grid.

## Slide 14: Slave Node
4: Data Extraction: Another capacitor is used to only retrieve the AC component of the virtual grid, our modulated signal. It’s then amplified to make up for losses
5. Demodulator Circuit: We use a half-wave rectifier (diode) and low-pass filter to convert our signal to entirely positive, then rid of the high frequency carrier.
6. Microcontroller 2 (MC2): Another OpAmp is used to compensate signal amplitude loss during rectifying and filtering. The digital signal can now be read by MC2, which controls the relay
7. Relay: Switches supplied power to appliances
Notes: Inspecting the Slave Node in the same way, we see 4 more modules. Number 4, Data extraction is used to retrieve the modulated signal from the virtual grid. 5, the demodulator circuit rectifies and filters the signal to output its envelope. 6 is Microcontroller 2. It uses the now digital data to control the relay. And 7 is the relay which switches power to desired appliances.

## Slide 15: Scoped Modulation
Illustrative Verification
Top left, is the MC1 generated bit signal running at a desired 150Hz
On the left, is the MC1 generated high frequency carrier signal running at 40kHz
Above is our modulated signal, the final output of the Master node
Notes: Here are some verifications of our master node functioning. These images were gathered with an oscilloscope. As you can see MC1 correctly generates a bit signal and high-frequency carrier, while the modulation circuitry successfully modulates.

## Slide 16: Scoped Demodulation
Illustrative Verification
Top left is the extracted modulated signal from the virtual grid. A closer look is the green signal on the image to the right.
Bottom left is our half-wave rectifier output
Above is the comparison of three signals. From bottom up we have the original bit signal, the extracted modulated signal, and the envelope signal after filtering
Notes: We also scoped the Slave node. The input to the slave node can be seed on the top left. Bottom left shows the rectifier making the prior signal strictly positive, and the final image on the top right is a comparison of the original bit signal, the extracted modulation signal, and the envelope.

## Slide 17: Overall Comparison
Before and After
UART requires the baud rates of transmitter and receiver to be within 10% of each other. Currently, they are off by 24%. This explains why our message was not properly received and thus why our relay did not function on our PCB.
In yellow is the final result from our demodulator. It’s amplified so its max value is well above the digital threshold of 2.1V. The frequency of the demodulated signal is off such that the length of digital 1 is 0.8ms longer than the original bit signal’s 1.
In green is the demodulated signal before amplification
In blue is the original bit signal
Notes: This last oscilloscope image is a similar comparison. The tall yellow signal is our final signal as its sent to MC2. In our demonstration, our failure to control the relay is likely due to our received signal being too long compared to the sent signal. UART requires a minimum of 10% error to successfully transmit and receive data. Here, we’re off my 24%.

## Slide 18: Appliance Control
Video Verification
The Relay Switches
A relay controlled by the slave microcontroller does activate when pulsed through a transistor.
Serial Asynchronous Communication
After a signal is sent, the receiver MC waits until a special start character is detected. It then controls the relay and changes its own global variables based on the received data to store a schedule.
Notes: William

## Slide 19: Multiple Schedule Control
Video Verification
Demonstrated here is a single microcontroller dictating the schedules of two slave nodes (one is an Arduino board and one is another microcontroller). I2C is a protocol that would enable one master MC to control multiple follower nodes.
Multiple Slave Nodes
Notes: Wiliam

## Slide 20: Future Consideration
Secure the data
Add public key cryptography to secure the data once it is on the line
Better rectifier
Implement a full wave rectifier instead of a half wave.
Improve the gain
Use an op amp with larger gain. Current one only allows 6 V/V rail to rail
Relay
Use a lower rated voltage relay so it can be flipped directly with a lower supply voltage
Areas where we can improve the project
Notes: Our biggest issue is getting the final signal to closely match it’s original bit signal. We can improve upon our project by implementing a better rectifier, and higher gain opamps. We ran intro trouble because we didn’t get the ideal parts in time.

## Slide 21
.
Ethics Considered
Disclosures
Disclose complete limitations of system and testing results honestly. Share all possible conflicts of interests to end user customers and power companies
Data Vulnerability
Currently, the scheduling data can be intercepted. Even with cryptography, good op-security across all levels is needed.
Power Dependent People
We will not market this product to people who depend on power and cannot work their schedules around times without it
Fire and Shock Hazard
Components worn or destroyed from weather damage could cause unintentional shorts.
Notes: William

## Slide 22
Thanks for listening to this presentation!

## Slide 23
We hope to bring this technology to a whole city in the future
Any Questions?
Thanks So Much ECE @ Illinois!