## Slide 1
Prerak Sanghvi | Neil Stimpson | Vassily Petrov

## Slide 2: Motivation
To make a safer, intuitive bicycle brake system
Objectives
Combine multiple sensors and motors
Implement an algorithm for optimum braking
Incorporate active battery monitoring
Integrate into a compact assembly

## Slide 4
Master Housing Unit
Hand Force Sensor
Optical Sensor
Optical Sensor

## Slide 5
Battery
Front Wheel Servo
Back Wheel Servo
Load Cell
Master PCB
To Optical Sensor

## Slide 6: Master PCB

## Slide 8: Power Module
Texas Instruments TPS563240 Buck converters (pair)
MOSFET controlled power switch

## Slide 10
Microcontroller
Silicon Labs EFM32 ARM Cortex M0+ Microcontroller @ 24MHz
Integrates all on-board and external sensors

## Slide 11
Uses Serial Com

## Slide 12
Load Cell Amplifier and ADC
Avia HX711 Load Cell Sensor
Used to measure the force on brake lever

## Slide 13
USES I2C Communication

## Slide 14
Servo Monitors
Texas Instruments INA260 Power Monitors
Feedback from force applied by servos

## Slide 15
Uses PWM signals

## Slide 16: Optical Encoder

## Slide 17: Optical Encoder

## Slide 18
Optical Encoder Behavior
Wheel Speed increase
Raw input
Filtered output

## Slide 19
Results
Sensor data sent out through serial interface
Can be displayed in real time using our Python app

## Slide 20
Results
Comparison of GPS speed to wheel sensor speed
Overall accurate, but has lots of noise

## Slide 21: Challenges
Multiple 3D print iterations
PCB modifications
Accelerometer mounting
Non – linearity of the braking system

## Slide 22
Future Work
Implementing accelerometer
Optical ring precision improvement
Cruise control functionality
Endless possibilities!
Safety Considerations
Mechanical emergency brake

## Slide 23
Special Thanks
For providing free samples of ICs
Glen Hedin, ECE Machine Shop – For their work on the Mechanical assembly and enclosure
Chris Horn – For his guidance throughout the project