## Slide 1
AUTOMATED WILDLIFE WATCHER
Electrical & Computer Engineering
Group #61
Edwin Lu, Xu Gao, Kelvin Chen
May 3, 2023

## Slide 2
Introduction
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 3
Project Introduction
Despite growing interest in wildlife ecology, the actual data collection process is very tedious
Lots of investment in time and manpower
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Objective: Automated Wildlife Watcher
We envision a wildlife camera that can keep a certain area of interest not only for a sustained period of time but also can track and follow any wildlife and zoom in for a more clear image or video of their behavior.
[1]
[2]
[3],[4]
Notes: Kelvin

## Slide 4
IMAGE / GRAPHIC
High level requirements
Camera can detect object entering its the 15m X 15m field of vision, 15m away or 1m X 1m field of vision, 3m away
Two servo motors can move in coordination and track object moving across 3m/s
Before the start of each tracking, two servo motors will return to their default positions
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kelvin

## Slide 5
FUNCTIONAL TEST RESULT
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Successful motion detection
Successful servo tracking
Successful retest after threshold lack of movement
Not enough testing for different lighting conditions and background
Object recognition selects any object with a larger enough difference with background

## Slide 6
Design overview
Block Diagram | Subsystems
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 7
IMAGE / GRAPHIC
Four Submodules
Power submodule
Gimbal submodule
Microcontroller submodule
Camera submodule
GRAINGER ENGINEERING
Block Diagram — Initial design
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 8
Three Submodules
Gimbal submodule
Computation submodule
Camera submodule
GRAINGER ENGINEERING
Block Diagram — Final design
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 9
Initial
Separate power submodule
Unclear camera control module
Raspberry Pi as main microcontroller
Final
Independent microcontrollers
Simplified gimbal modules
Practical camera module
GRAINGER ENGINEERING
Block Diagram — Comparison
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 10
Block
IMAGE / GRAPHIC
Camera - Arducam
Arducam - 1080p USB camera
Capturing videos
  Directly connected to Raspberry Pi
Motion detecting and tracking algorithm on Raspberry Pi
GRAINGER ENGINEERING
Camera Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kelvin

## Slide 11
New Block diagram
GRAINGER ENGINEERING
Raspberry Pi Code Flowchart
ELECTRICAL & COMPUTER ENGINEERING
Notes: Edwin

## Slide 12
Gimbal
QuBona - Tripod
Deegoo-FPV - servo brackets
Flechawk - servo motors
2 Servo motors
  Independent horizontal and vertical movement
Communication through PCB
  Pulse Wave Modulation
Many thanks to the ECE Machine Shop
GRAINGER ENGINEERING
Gimbal Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kelvin

## Slide 13
GRAINGER ENGINEERING
Arduino (ATMega328p) Code Flowchart
ELECTRICAL & COMPUTER ENGINEERING
Gimbal Control
Receive Coordinates from Raspberry Pi
Calculate ΔServo_x and ΔServo_y
Limit with Max movement
Smooth to move 1° at a time
Write Data to Servos
Notes: Edwin

## Slide 14
New Block diagram
GRAINGER ENGINEERING
State Machine
ELECTRICAL & COMPUTER ENGINEERING
Notes: Edwin

## Slide 15
Initial Design
Components in our initial pcb:
ATmega328P-U
SPI 5-pin headers
Servo motors 3-pin headers
Challenges
Could not program the ATmega328P-U
Communication between the microcontroller and Raspberry Pi was not successful
GRAINGER ENGINEERING
Microcontroller Subsystem — PCB
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 16
Why it’s not working?
Programming
Programmed ATmega328P using Arduino
Failed to program ATmega328P with its internal clock.
  A crystal oscillator is needed on the PCB
Connection to Raspberry Pi
Missing ground pin for SPI protocol
software problem
GRAINGER ENGINEERING
Microcontroller Subsystem — PCB
ELECTRICAL & COMPUTER ENGINEERING
Notes: Edwin
Xu

## Slide 17
Temporary Solution
Replace microcontroller by Arduino Uno
  main part of PCB was replaced by Arduino Uno
Change communication protocol
  Use UART protocol for communication between Arduino and Raspberry Pi
Connect Arduino Uno with breadboard
  A simple voltage divider circuit built on breadboard
  transfer 5V to 3.3V
  protect RX pin on Raspberry Pi
GRAINGER ENGINEERING
Microcontroller Subsystem — PCB
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 18
Revised Design
Added AVR-ISP-6 to program ATmega328P by USBasp
Added voltage regulator on PCB
Used UART protocol for connection to Raspberry Pi
GRAINGER ENGINEERING
Microcontroller Subsystem — PCB
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 19
Requirements & Verification
When the gimbal needs to move, the microcontroller must communicate with the gimbal system
Arduino Uno (ATmega328P) sent pwm signals to servo motors
When the recorded video needs to be saved, the microcontroller must give instruction to store data
The recorded videos were saved in the SD card of Raspberry Pi
When the camera needs to turn on/off, the microcontroller must communicate with the camera system
The camera will turn off with a delay after the user stops the program
GRAINGER ENGINEERING
Microcontroller Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Xu

## Slide 20
Result Analysis
Successes | Challenges
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 21
Successes
Motion detection and Tracking (for short time)
Independent servo motor controls
Functional cross-module communication
Challenges
Slow tracking speed
Tracking algorithm not fully functional for faster movement
PCB not functional
Delay exists in executing user’s command
GRAINGER ENGINEERING
Results
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kelvin

## Slide 22
Conclusion
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 23
Project Idea
Much more ambitious than expected
Unclear expectations and high level requirements
Acquired Skills
PCB design
Program ATmega328P microcontroller
Implement Motion Detection
Implement Object tracking
Build connection between microcontrollers by communication protocols
Learned how to control and integrate subsystems
GRAINGER ENGINEERING
Conclusion
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kelvin

## Slide 24
Next steps
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 25
Algorithm
More robust tracking algorithm to adjust for moving camera and detecting moving objects
Train a CNN model to recognize the moving objects as animals or not
Camera
Zoom functionality
Outdoor protection (weather proofing)
Power
Independent power/battery power supply
User Experience
Remote control (setup Raspberry Pi remote desktop by xrdp)
More user-friendly interface
GRAINGER ENGINEERING
Future Considerations
ELECTRICAL & COMPUTER ENGINEERING
Notes: More robust tracking algorithm to adjust for moving camera and detecting moving objects – Kalman filters(?)
Xu

## Slide 26
Any questions?
Thanks for coming!
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 27
Image used:
[1] “Bumble Bee Watch,” Bumble Bee Watch. Accessed: May 3, 2023. [Online]
Available: https://www.bumblebeewatch.org/
[2] “Global pollinator declines: trends, impacts and drivers,” Potts, et al.. Accessed: May 3, 2023. [Online]
Available: https://www.sciencedirect.com/science/article/pii/S0169534710000364?casa_token=VkoL2GQpBAYAAAAA:6QjCYwheQAlUfP7e3tpTQI9oKIXG-IhlGIJoAH0rpA9pQ5fjM3dQYv3kTbhfYlXCPWP8W-FYrkk
[3] PNGITEM. Garden Flowers png images. Accessed: Feb 9, 2023. [Online Image]
Available: https://www.pngwing.com/en/search?q=garden+Flowers
[4] CLIPARTIX. Hummingbird Clipart. Accessed: Feb 9, 2023. [Online Image]
Available: https://clipartix.com/hummingbird-clipart-image-31490/
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING