# SLAM on Smartphones

ECE 445

Design Review

YIXIAO LIN

FENGYUANSHAN XU

TA: Mustafa Mukadam

September 20, 2013

1. Introduction......................................................................................................3

1.1 Statement of Purpose................................................................................. 3

- Objectives........................................................................................................4

2.1 Goals...........................................................................................................4

2.2 Functions.....................................................................................................4

2.3 Benefitss......................................................................................................4

2.4 Features.......................................................................................................4

- Design..............................................................................................................5

3.1 Block Diagram............................................................................................5

3.2 Block Description.....................................................................................11

- Performance Requirement and Verification...................................................16

4.1 Requirement & Verification......................................................................16

4.2 Tolerence Analysis....................................................................................19

- Cost Analysis.................................................................................................20

5.1 Labor Cost.................................................................................................20

5.2 Unit Cost...................................................................................................20

5.3 Total Cost..................................................................................................20

5.4 Schedule....................................................................................................21

6. Ethics and Safety.............................................................................................23

7. Reference........................................................................................................24

8. Appendix.........................................................................................................25

1. INTRODUCTION

### 1.1 Statement of purpose

When it comes to distributed robotic systems, great limitations exist for higher level programming. A positioning system would allow coordinate based behavior. Thereafter, it reduces the complexity of higher level robotic programming. We want to build a positioning system that detects the environment around itself and creates a map. The map information can be easily used by other robotic developers in any indoor environment.

## 2 Objectives

### 2.1 Goals:

·Reduce the complexity of the indoor robotic positioning problem

·Compatible map data transfer to android smart phones as well as computers

### 2.2 Functions:

·Sensor platform with accurate angle control

·Continuously collects the distance data in an automatic way

·Noise filtering of the sensor raw data and process data

·Transfer processed map data to an Android phone

·Generate map of surrounding environment

### 2.3 Benefits:

·Simple devices fit in any kind of indoor environment without additional set up requirements

·Easy to apply to any other robotic platforms

### 2.4 Features:

·Extremely portable device

·Simple to set up and use for any robotic platform

·Generate map information of the indoor environment

3. DESIGN

### 3.1 Block Diagram

As shown on figure 1 below, this is our top level system diagram.

Figure 1. Top Level System Layout

The figure 2 is the block diagram for each top level system block.

Figure 2. Block Diagram

To be more specific:

Figure 3. Specific Block Diagram

Each procedure in this system:

Figure 4. Top Level Program Flow

The flow chart for test ultrasonic sensor precision:

Figure 5. Precision Test Program Flow

The flaw chart for map generation will be:

Figure 6. Arduino Program Flow

The flow chart for the Android program is:

Figure 6. Android Program Flow

### 3.2 Block Descriptions

Summary:

As shown in the top level system layout, our design is consisted of three parts. Data collection unit will collect the data which is the distance between the robot and the surrounding obstacles. The data will flow into the data process and communication unit. A map of surrounding environment will be generated. A path for exploring the room will be generated for the robot as well. Then the newly planned path will drive the motor for robot to move and drive the motor of the sensor to collect distance data in another direction.

3.2.1 Ultrasonic sensor

| Ultrasonic sensor |
| --- |
| Input | 5V DC voltage |
| Output | Input TTL lever signal and the range in proportion |
| Specifications | 2mA working current | 15 degree of effectual angle |
|  | Range from 2cm to 5m | 40Hz working frequency |

We are using an Ultrasonic Range Detection Sensor SainSmart HC-SR04. This is used for detecting the range between the robot and the obstacles nearby. This sensor can send an ultrasound pulse at a frequency of 40KHz. It then waits for receive the echo back pulse and calculates the time taken in microseconds. With 5V DC working voltage and 15mA working current, this sensor has sentry distance from 2cm – 500cm and accuracy up to 0.3cm. The output of this sensor is an analog signal. We can determine the distance between current position and the obstacle according to the voltage level. The output voltage will be passed to Arduino Board for processing. The sensor is driven by a servo motor to collect the data from all directions.

3.2.2  Arduino UNO Microcontroller

| Arduino UNO Microcontroller |
| --- |
| Input | 1)9V DC power supply Analog signal from ultrasonic sensor |
| Output | Digital signal to Android phone through usb port Digital siganl to motor shield |
| Specifications | Recommend operate voltage: 7-12V | 14 digital I/O pins; 6 analog input pins |
|  | 16MHz clock | 40mA per I/O Pins |

We choose Arduino UNO to be our data processor. It will control the servo motor and generate a map of surrounding obstacles. We are going to write a program for this board to process the output voltage from the sensor. Therefore, Arduino board can determine how far an obstacle is away from the robot at the direction. Then based on current map information, Arduino board will control the servo motor to rotate by an angle to get the distance data in another direction to complete the map. The control signal will be sent to the servo motor controller. There is an USB interface on this Arduino UNO board, which enables the communication between the Arduino and Android platform. The map created by the Arduino board will be passed to the Android phone through the USB port.

3.2.3 Moter Shield

| Motor shield |
| --- |
| Input | 1)5V DC power supply 2)Analog signal from 3)Externel power supply for servo motor |
| Output | Analog signal to servo motor to control the speed and direction of motor |
| Specification | External voltage within 5-12V | 8 I/O Pins, 4 Pins for each channel |

Motor shield is designed to drive inductive loads, in our case, the servo motor. A separate power supply will be providing the power for the motor. Motor shield serves as a bridge between our arduino UNO microcontroller and the servo motor

3.2.4  Servo Motor

| Servo Moter |
| --- |
| Input | 1)5V DC power supply 2)analog signal from microcontroller |
| Output | Degree wise motor movement |
| Specification | Operating voltage 4.8V to 6V |

We choose servo motor over stepper motor for the reason that servo motor allows for precise control of angular position and velocity. We can determine at which angle our sensor is currently at. This motor will be assembled on top of our robot. The digital servo motor controller directs operation of the servo motor by sending velocity command signals to the amplifier, which drives the servo motor.

3.2.5  Android:

We are using Samsung Nexus S Android smartphones to control iRobot Create platforms. The phone is placed on top of iRobot Create. It sends commands to the robots using Bluetooth communication. We will develop program in java to control the robot exploring behavior.

We will also use the compass sensor in the phone to determine the orientation of the robot.

3.2.6  iRobot Create:

This platform will be controlled by Android phone through a Bluetooth module. It will move according to the phone’s command. The platform has two wheels; it can go straight, turn left/right. The platform also have 2 bump sensors, 2 cliff sensors, 2 wheel drop sensors and a wall sensor. The motors for the robot is also encoded. The distance and angle odometry will be used to estimate the current location of the robot.

3.2.7  Power supply:

The power supply will be used for the controller, the sensor and the servo motor. The power supply will consist of a 9V battery and an adapter.

| Units | Battery Type |
| --- | --- |
| Arduino/Ultrasonic sensor/LED | 9V battery |
| Motor Shield | 5V battery (4*1.25V rechargeable battery) |
| iRobot | 18V Li battery |
| Android | 1500mAh Li battery |

## 4 Performance Requirements and Verification

### 4.1 Requirements & Verifications

| Requirements | Verification |
| --- | --- |
| Ultrasonic Sensor 1) Ultra-sonic sensor feedback accurate, with false tolerance up to 0.01 meter in the range of 5 cm to 500 cm | 1) ·Obtain 10 data points in the surrounding environment using a ruler ·Obtain the same position data from ultrasonic sensor and compare the difference |
| Servo Motor 1) Servo motor able to drive the sensor from 0 to 180 degree 2) angle accuracy of 1 degree 3) Enough torque to spin with ultrasonic sensor on top of it | 1) ·Initialize the servo motor position to 0, test 20 random positions. 2) ·Measure the servo motor position in degrees using a clinometer. 3) ·Compare the servo motor position and the ideal position. |
| Motor Shield 1) External power supply 5V±1% DC Voltage 2) Each of the output signal pin working well | 1) ·Since Motor shield require 4.8-6V DC voltage, we need to use a voltagemeter to ensure that the power supply is within this range. 2) ·Motor shield can transfer the signal from Arduino board to servo motor correctly. Write a simple program for driving the motor and use a voltage meter to measure if the desired signal appears at the output pins. |
| Arduino map generation Generate a map based on the current sensor readings in 30 seconds after receiving the sensor data. | 1) ·After generating a new map, a test LED lights up. ·After servo motor finish moving from 0 to 180 degree, the time LED lights up should be less than 30 seconds. |
| Arduino Power 1) Power supply 9V±5% DC voltage 2) Arudino is receiving right amount of voltage | 1) ·Using a voltage probe or a oscilloscope to test the power source first. 2) ·If requirement above fulfilled, connect the power source to the Arduino board and measure the voltage of V_in port |
| Arduino USB Port 1) USB port is making a good connection 2) USB port can transfer data correctly | 1) ·Multimeter at USB connector to make sure good connection 2) ·Connect the Arduino board to PC through USB port. Write a simple program and load it to the board. See if the board loaded with the desired program |
| Arduino to Android 1)Real time map data transfer from phone in 5 seconds 2)The signal passed to Android phone stays in the range of 5.00 ± 0.25 V | 1) ·Generate a new map on Arduino and pass it to Android ·Measure the data transfer time 2) ·Use a multimeter to measure the voltage signal from the Arduino |
| iRobot Distance information generated properly by iRobot Angle information generated properly by iRobot | 1) ·Rotate both left and right wheels by 5 Rounds ·Read distance generated by iRobot ·Compare distance reading with 10*π*Wheelradius 2) ·Rotate left motor by x rounds, right motor by y rounds ·Read angle generated by iRobot ·Compare angle reading with (4*360*π(x-y)*Wheelradius)/d d is the distance between two wheels |
| Android Phone 1) Internal IMU can provide correct data of current orientation 2) Angle accuracy of 1 degree 3) Bluetooth with iRobots connects without and disconnection in 30 minutes period | & 2) ·Initialize the phone position to 0, test 20 random positions ·Measure the phone position in degress using a clinometer ·Compare the phone position and the reading from IMU |
| Obstacle specification 1) Height 2) Well shaped 3) Coarse surface | 1) ·Each obstacle is at least140mm in height to be sensible by ultrasonic sensor. 2) ·Check the shape of each obstacle and make sure that only cuboid shaped obstacle in the room 3) ·None of the obstacles have smooth transducer surface |
| Room specification 1) flat groud 2) within 10m*10m in size 3) no strong magnetic field | 1) ·No small obstacles on group that will influence the motion of robot 2) ·Room does not exceed 10m*10m in area 3) ·No strong magnetic field in the room that may influence the performance of IMU |

### 4.2 Tolerance Analysis

Since the mapping heavily depends on distance data, the tolerance analysis will be based on the accuracy of our ultra-sonic sensor. To ensure the accuracy of sensor measurement, we will compare the sensor estimated distance with real distance. The room diameter should not be larger than 10 meter. Any point that is further away than 5 meters from the sensor would not be guaranteed to meet the 0.01 meter accuracy specification.

## 5. Cost Analysis

### 5.1 Labor cost

| Name | Hourly Rate | Total Hours | Total |
| --- | --- | --- | --- |
| FENGYUANSHAN XU | $40.00 | 180 | $18,000 |
| YIXIAO LIN | $40.00 | 180 | $18,000 |
| Total | $80.00 | 360 | $36,000 |

### 5.2 Unit Cost

| Item Name | Quantity | Cost($) | Ordering Status |
| --- | --- | --- | --- |
| Ultrasonic Sensor | 1 | 7.00 | Arrived |
| Arduino UNO | 1 | 10.00 | Arrived |
| Servo Motor | 1 | 15.00 | Arrived |
| Motor Shield | 1 | 30.00 | Arrived |
| Base | 1 | 30.00 | Ordered |
| 9V Battery | 1 | 5.00 | Arrived |
| 1.25V rechargeable battery | 4 | 18.00 | Arrived |
| Total |  | 115.00 |  |

### 5.3 Total Cost

| Section | Total |
| --- | --- |
| Labor | $36000 |
| Parts | $124 |
| Total | $36124 |

### 5.4 Schedule

| Week | Task | Responsibility |
| --- | --- | --- |
| 9/16 | Finalize the proposal | Yixiao Lin |
|  | Read papers on servo motor and in door slam using ultrasonic sensor | Fengyuanshan Xu |
| 9/23 | Research Arduino to Android communication, order ultrasonic sensor and required arduino board. | Yixiao Lin |
|  | Design Review, order servo motor, study Arduino code for controlling servo motor. | Fengyuanshan Xu |
| 9/30 | Test servo motor performance. | Yixiao Lin |
|  | Handle servo motor and inertial measurement unit. Assemble servo motor with ultrasonic sensor | Fengyuanshan Xu |
| 10/7 | Work on program for data processing | Yixiao Lin |
|  | Test ultrasonic sensor on servo motor | Fengyuanshan Xu |
| 10/14 | Finish code for map generation | Yixiao Lin |
|  | Test ultrasonic sensor with IMU | Fengyuanshan Xu |
| 10/21 | Simulate the program on Arduino | Yixiao Lin |
|  | Connect sensor, motor and IMU to Arduino and test the data processing program | Fengyuanshan Xu |
| 10/28 | Grab papers on communication between Android and Arduino | Yixiao Lin |
|  | Work on code pass data from Arduino to Android | Fengyuanshan Xu |
| 11/4 | Test path planning program on Android phone | Yixiao Lin |
|  | Work on program for map generation | Fengyuanshan Xu |
| 11/11 | Combine all parts together | Yixiao Lin |
|  | Finish program for map generation | Fengyuanshan Xu |
| 11/18 | Complete the project by fixing remaining issues | Yixiao Lin |
|  | Final test to devices and functionalities | Fengyuanshan Xu |
| 11/25 | Tolerance analysis | Yixiao Lin |
|  | Verification of specifications | Fengyuanshan Xu |
| 12/2 | Demo and presentation | Yixiao Lin |
|  | Demo and presentation | Fengyuanshan Xu |
| 12/9 | Final paper | Yixiao Lin |
|  | Final paper | Fengyuanshan Xu |

## 6 - Ethics and Safety

### 6.1 Ethics

The SLAM on smartphone is a product that will be able to do all of the details listed in the benefits and features. In order to realistically make this platform marketable, it will have to comply with the IEEE Code of Ethics. Of the ten that IEEE has listed, the code below is the one that applies to this project:

- to accept responsibility in making decisions consistent with the safety, health, and welfare of the public, and to disclose promptly factors that might endanger the public or the environment

- to be honest and realistic in stating claims or estimates based on available data

Since our project heavily relies on sensor data to estimate, we will be honest about our claims and estimations

### 6.2 Safety

To make our product practical, we will need to be able to guarantee a safe working environment. The power supplies are low voltage (maximum voltage is 18V DC). This is a safe voltage for human beings. But since we are using battery, we have to make sure that battery acid does not leak. We will also follow all the safety regulations and instructions in the senior design lab.

7 References

[1] United States. IEEE. 7.8. IEEE Code of Ethics. Washington DC, 2013. Web.

[2] Arduino UNO R3 Schematics, 2013. Web

http://arduino.cc/en/Main/arduinoBoardUno

[3] Arduino R3 Motor Shield Schematics, 2013, Web

http://arduino.cc/en/Main/ArduinoMotorShieldR3

[4] Ultrasonic Ranging Module HC - SR04, 2013, Web

http://elecfreaks.com/store/download/HC-SR04.pdf

[5] iRobot open interface, 2013, Web

http://www.irobot.com/filelibrary/pdfs/hrd/create/Create%20Open%20Interface_v2.pdf

8 Appendix

Motor Shield datasheet

Arduino UNO datasheet