Engineers of Catan

Design Review

ECE 445

Hannah Hasken - Adam Blackburn

TA: Ryan Corey

Prof: P. Scott Carney

Project 8

February 27, 2013

Contents

1.0 Introduction	4

1.1 Statement of Purpose	4

1.2 Goals	4

1.3 Benefits	4

1.4 Functions	4

1.5 Features	4

2.0 Design	5

2.1 Block Diagram	5

2.2 Block Descriptions	6

2.2.1 Master Module	6

2.2.2 Board Tiles	7

2.2.3 Dice Module	9

2.2.4 User-display Module	9

2.2.5 Game Pieces	10

2.2.6 Robber	10

3.0 Requirements and Verification	11

3.1.1 Master Module	11

3.1.2 Board Tile	12

3.1.3 Dice Module	13

3.1.4 User-display Module	14

3.1.5 Game Pieces	14

3.1.6 Robber	14

3.2 Tolerance Analysis	15

3.3 Preliminary Testing	15

3.3.1 LED Brightness Testing	15

3.3.2 I2C Bus Testing	15

3.3.3 Game Piece Design	15

3.4 Flowcharts	16

3.4.1 Board Tile Flowchart	16

3.4.2 Overall Flowchart	17

3.5 Simulation	18

3.5.1 Game Piece Resistor Values	18

4.0 Cost and Schedule	19

4.1 Cost Analysis	19

4.1.1 Labor	19

4.1.2 Parts	20

4.1.3 Grand Total	20

4.2 Schedule	21

5.0 Discussion of Ethical Considerations	22

# 1.0 Introduction

## 1.1 Statement of Purpose

We chose to create an electronic version of the board game, “Settlers of Catan”. This board allows players to move through the game faster and to make sure that there are no missed resources during distribution. It also speeds up the initial game setup process.

We selected this project because there is nothing similar available, and it presents some unique challenges with regards to piece detection and board design, due to the game's unique reconfigurable layout and pieces. We also felt that we could produce a functional, easy-to-use, and nice-looking final device that would be a worthwhile goal.

## 1.2 Goals

- Develop a modular board system that can be easily expanded and assembled

- Recreate very similar gameplay to the actual board game

- Have an easy-to-use interface for players that doesn’t require additional learning

## 1.3 Benefits

- Resources automatically totaled for players at the beginning of each turn

- Automatically generate the board configuration.

- Built-in random-number dice.

- Makes resource distribution easier for players

- Speeds game play

## 1.4 Functions

- Bright LEDs to display board layout and 7-segment displays to indicate number on each tile

- Automatic randomized board layout for each game

- Identify individual pieces (type and owner)

- Easy to read resource information for each player

## 1.5 Features

- Automatic board layout

- Easy-to-use resource counting feature

- Intuitive gameplay

- Contains all pieces for a 4 person game

# 2.0 Design

## 2.1 Block Diagram

Game piece

Robber

Board tile

Dice module

User-display module

Master module

Power supply

## 2.2 Block Descriptions

### 2.2.1 Master Module

The master module will contain the game logic and will be responsible for controlling the board tiles, dice module, and user-display modules. The master module will be connected to the other modules via an I2C bus.

### 2.2.2 Board Tiles

In the traditional Settlers of Catan, the board is made up of several (19) tiles that are laid out and used to construct a unique board for each game. Each tile also gets a token with a number from 2 to 12. Our version will have those tiles assembled, but the logic in each cell will allow the layout of the board to be randomly generated. This will allow the same gameplay as the traditional version. Each tile will include an RGB LED to change the color, two piece sensors, a Hall Effect sensor for detection of the robber, and a 7-segment display to show its number.

In the board game, the tiles are hexagons. The board tiles PCBs will be rectangles for easier assembly, but the plastic cover on the game will give the illusion of hexagon tiles.

The board tile PCBs will be connected to each other via the CONPREV and CONNEXT headers. This will allow only one connection to the master module but will allow access to the entire string of board tiles. This will minimize the connections between parts and simplify assembly since each of the board tile modules only have to be connected to the new and previous modules in the series. This modular design would also allow re-use of our design to make boards of different shapes or larger boards by simply adding more board tile PCBs and updating the master module.

The tiles will be identical and connected via an I2C bus to allow individual addressing and two-way communication with only two wires.

Piece sensor header and voltage dividers

Hall Effect sensor header

I2C connection from previous/to next

Capacitors for MCU VCC

RESET pullup

Capacitor to stabilize Hall Effect analog pin

RGB LED and resistors

7-segment display and resistors

Header for programmer connection

MSP430G2553 MCU

The board tiles will be controlled by the master module via the I2C bus.

### 2.2.3 Dice Module

The dice module will consist of two digital "dice" and a button to “roll” them. The numbers will be generated by a random number generator and displayed via LEDs. The module will then send the numbers to the master module via the bus. This will simulate rolling the dice for each turn.

### 2.2.4 User-display Module

The user display module will display the number of resources collected after each dice roll, while taking into account the position of the robber. These will be displayed using 7-segment displays. The master module will update the displays via the I2C bus. This will allow players to easily decide which resources to collect after each dice roll.

The same circuit used for the dice will be used for the user-display module, sans button, simply repeated 10 times. The grouping for the 7-segment displays is illustrated below.

### 2.2.5 Game Pieces

The standard game pieces will consist of different valued resistors inside of pieces. This will allow the board tiles to identify the type of piece, as well as which player the piece belongs to by measuring the voltage drop in a voltage divider. This will allow automatic totaling of the points for easy resource distribution. The pieces will allow a simple, intuitive gameplay similar to the normal game.

### 2.2.6 Robber

The robber will be a plastic game piece with a powerful magnet on the base, which will activate the Hall Effect sensor in each board cell in order to allow the board to sense the piece location. This will allow the robber to be used in the same way as the normal game.

The board cell will contain a magnet to pull the robber to the correct location so that the detection is reliable.

Plastic game piece

Strong magnet

# 3.0 Requirements and Verification

### 3.1.1 Master Module

| Requirements | Verification |
| --- | --- |
| Receive data at master module via I2C Send data from master module via I2C Module must provide an internal voltage of 3.3V ± 0.1V for use by the microcontroller. Pull-up resistors must provide 3.3V ± 0.1V to the I2C bus when all connected inputs are in high-impedance mode. Switches must provide 3.3V ± 0.1V at the input of the microcontroller. LEDs must function when provided grounded via the microcontroller. | Connect the CONNEXT header to the CONPREV header on the board tile or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the master module or test program sends data to the board tile. Connect the CONNEXT header to the CONPREV header on the board tile or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the master module or test program sends data to the board tile. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONNEXT header and attach the ground to the GND pin in the CONNEXT header. Use a multimeter to verify that the MSP430 VCC pin has 3.3V ± 0.1V. Using a multimeter, verify that the voltage on the I2C bus is 3.3V ± 0.1V when the microcontroller inputs are in high-impedance mode. Using a multimeter in continuity mode without connecting the board tile to power, attach one lead to the 3V3 trace and the other to the input pin on the microcontroller. Press the button. When pressed, there should be very low resistance (<5Ω) Connect a 5.0 ± 0.1V power source to the 5V pin in the CONNEXT header and ground to the GND pin in the CONNEXT header. Using a microcontroller test program, verify that the LEDs illuminate when the pin is in output mode and is grounded. |

### 3.1.2 Board Tile

| Requirements | Verification |
| --- | --- |
| Receive data at board tile via I2C Send data from board tile via I2C Voltages at pins in the CONPREV header must show up at the same pin in the CONNEXT header RGB LED in tile must be visible in a brightly-lit room 7 segment display must be visible in a brightly-lit room. Must detect standard game pieces when connected Hall Effect sensor must detect magnet magnetic field through 1/4” plastic. Tile must provide an internal voltage of 3.3V ± 0.1V for use by the microcontroller. | Connect the CONPREV header to the header on the master module or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the master module or test program sends data to the board tile. Connect the CONPREV header to the header on the master module or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the master module or test program sends data to the board tile. Attach a 5.0 ± 0.1V source to the VCC pin in the CONPREV header and verify that the same pin in the CONPREV header shows a 5.0± 0.1V voltage. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONPREV header and attach the ground to the GND pin in the CONPREV header. Load the LED brightness test program onto the microcontroller via the PROGRAM header. Verify that the LED can be seen when covered by ¼” white plastic in a brightly-lit room. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONPREV header and attach the ground to the GND pin in the CONPREV header. Load the 7-segment test program. Verify that the 7-segment display counts through all numbers from 0 to 10 and is visible when uncovered in a brightly-lit room. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONPREV header and attach the ground to the GND pin in the CONPREV header. Attach a game piece containing a 1000 ohm resistor to the connector. Verify that the voltage at the ANALOGX junction is 1.65 V ± 0.05V. In addition, use a multimeter to ensure that the correct voltage appears at the analog input pin on the microcontroller. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONPREV header and attach the ground to the GND pin in the CONPREV header. Place robber piece on board tile near Hall Effect sensor. Verify with a multimeter that the voltage output from the Hall Effect sensor changes when the robber piece is placed near the sensor. In addition, use test code on the microcontroller to verify that the voltage read on the analog input pin changes when the robber is placed or removed. Connect a 5.0 ± 0.1V power source to the 5V pin in the CONPREV header and attach the ground to the GND pin in the CONPREV header. Use a multimeter to verify that the MSP430 VCC pin has 3.3V ± 0.1V. |

### 3.1.3 Dice Module

| Requirements | Verification |
| --- | --- |
| Pin wiring in hardware matches pin designations in software Must send information (about generated numbers) serially | Ensure the power is on See if all numbers display properly on the 7-segment display. Check wires and leads with multimeter. Connect the CONPREV header to the header on the master module or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the test program sends data. |

### 3.1.4 User-display Module

| Requirements | Verification |
| --- | --- |
| Must receive information (about earned resources) via I2C Pin wiring in hardware matches pin designations in software | Connect the CONPREV header to the header on the master module or a test microcontroller with a test program. Attach the power cable to the master module. Using a logic analyzer attached to the I2C bus, verify that the I2C signals are correct when the test program sends data. Ensure the power is on See if all numbers display properly on the 7-segment display. Check wires and leads with multimeter. |

### 3.1.5 Game Pieces

| Requirements | Verification |
| --- | --- |
| Must be durable enough to withstand many plug/unplug cycles Must fit snugly in the board Resistance must appear at the jack terminals | Plug/unplug the piece 100 times. Ensure no visible damage or wear is apparent. Ensure that pieces fit firmly and flush with the surface and don’t move when the board is shaken Using a multimeter, measure the resistance at the terminal on the 3.5mm jack and ensure that it matches the resistance of the resistor placed inside the piece. |

### 3.1.6 Robber

| Requirements | Verification |
| --- | --- |
| Magnet must be powerful enough to cause a noticeable voltage change in the Hall Effect sensors when place ¼” above the sensor | Connect the output from the Hall Effect sensor to a multimeter and measure the voltage change when the magnet is placed above the sensor on ¼” plastic. Ensure that it is at least 0.15V difference when the piece is placed versus when it is not. |

## 3.2 Tolerance Analysis

The component that most affects the performance of the project is the I2C bus. If the capacitance of the bus is too high, it will not work, and none of the components will be able to function. This can be corrected with an I2C buffer IC, but it is preferable not to use a buffer if not required.

In order to function, the bus must have a capacitance of less than 400pF, according to the specification. We will measure the bus capacitance when the unit is assembled to determine if it meets the specification.

We will run the test with a function generator and oscilloscope to determine the input capacitance. We will also add additional capacitance to the bus and test the response of the controller.

## 3.3 Preliminary Testing

### 3.3.1 LED Brightness Testing

A sample RGB LED with a 20mA current was bright enough to be seen through plastic under normal lighting. Ultra-bright LEDs will be fine for this application.

A sample 7-segment display was too small and not bright enough to easily be seen through plastic. A larger, brighter 7-segment display will need to be used in the final product.

### 3.3.2 I2C Bus Testing

Testing with the MSP430 using the I2C bus has been performed, and it functions as expected. We will test again with final PCB designs before making all necessary PCBs.

### 3.3.3 Game Piece Design

Several plastic game pieces were printed using a 3D printer, and they are durable enough to be used in the final design. They can be sized appropriately to fit the necessary hardware.

## 3.4 Flowcharts

### 3.4.1 Board Tile Flowchart

Start

Setup

Sleep

Compare Address

Parse Command

Execute Command

Check Analog Values

I2C Interrupt

Address doesn’t match

Address match

ADC Check Timer Interrupt

Done

### 3.4.2 Overall Flowchart

Start

Create and send board layout to board tiles

Sleep

Receive current piece placement from tiles

Calculate resource usage

Send resource usage information to display modules

Dice roll

Send initial configuration to display modules

## 3.5 Simulation

### 3.5.1 Game Piece Resistor Values

In order to determine which values would make appropriate choices for the game piece resistors.

Using the following parameters,

| ADC | 10 | bits |
| --- | --- | --- |
| # Pieces | 8 |  |
| Divider resistor | 1000 | ohms |
| VCC | 3.3 | V |

The following simulation values were obtained:

| Piece resistance | Divider voltage | ADC Output | ADC Delta | Acceptable? |
| --- | --- | --- | --- | --- |
| 0 | 0.000 | 0 | - | - |
| 100 | 0.300 | 93 | 93 | ok |
| 270 | 0.702 | 218 | 125 | ok |
| 510 | 1.115 | 346 | 128 | ok |
| 750 | 1.414 | 439 | 93 | ok |
| 1100 | 1.729 | 536 | 98 | ok |
| 1600 | 2.031 | 630 | 94 | ok |
| 2400 | 2.329 | 723 | 93 | ok |
| 3900 | 2.627 | 815 | 92 | ok |

This uses an ADC delta of 75 as being the threshold between acceptable and not acceptable. However, all ADC deltas are at least 92, so distinguishing between the values should be no problem, even with noise. The detection circuit will be pulled down to ground when no piece is connected.

# 4.0 Cost and Schedule

## 4.1 Cost Analysis

### 4.1.1 Labor

| Name | Hourly Wages | Hours Invested | Labor Total (x2.5) |
| --- | --- | --- | --- |
| Hannah | $40 | 120 | $12000 |
| Adam | $40 | 120 | $12000 |
| Labor Total |  | 240 | $24000 |

### 4.1.2 Parts

| Part | Part Number | Status | Unit Cost | Quantity | Total |
| --- | --- | --- | --- | --- | --- |
| RGB LED |  | Not selected | $ 0.45 | 19 | $ 8.55 |
| Microcontroller | MSP430G2553 | Selected, have samples | $ 1.33 | 30 | $ 39.90 |
| 7-Segment Display | COM-08546 | Selected, have parts | $ 0.86 | 41 | $ 35.26 |
| Hall Effect Sensor | 785-SS42R | Selected, have sample | $ 1.64 | 19 | $ 31.16 |
| Linear Regulator | LM3940 | Selected | $ 1.12 | 2 | $ 2.24 |
| RCL, etc. |  | In lab/part shop |  |  | $ 40.00 |
| Jack plug (male) | 3.5 mm plug | Selected, have sample |  |  | $ 20.00 |
| Panel jack (female) | 3.5 mm jack | Not selected |  |  | $ 20.00 |
| Acrylic Sheet | 8505K15 | Selected, have sample | $ 72.13 | 1 | $ 72.13 |
| Board Frame |  |  | $ 100.00 | 1 | $ 100.00 |
| Power Supply | 6VDC 3AMP | Not selected | $ 7.16 | 1 | $ 7.16 |
| PCB |  |  |  | 36 | $ 200.00 |
| Game Pieces | 3D Printed | Selected, have samples |  | 52 | $ 50.00 |
| Part Total |  |  |  |  | $ 626.40 |

### 4.1.3 Grand Total

| Section | Total |
| --- | --- |
| Labor Total | $24000.00 |
| Part Total | $626.40 |
| Grand Total | $24626.40 |

## 4.2 Schedule

| Week | Hannah | Adam |
| --- | --- | --- |
| Feb 11 | Learn Eagle and rough design for dice PCB | Learn Eagle and rough design for master PCB |
| Feb 18 | Rough design for user display PCB and complete Design Review paper Code dice microcontroller Sign up for DR | Rough design for board frame and cover and complete Design Review paper Code master microcontroller |
| Feb 25 | Prototype game pieces and robbers Code user display microcontrollers Review/send for milling master module PCB and board frame/cover | Rough design for game tile PCB Debug master code Review/send for milling dice and user display PCB |
| Mar 4 | Solder/debug dice PCB Solder user display PCB | Finalize game tile PCB and send first for printing Finalize board frame and board cover designs and send for creation |
| Mar 11 | Debug user display Update PCB designs Individual progress report | Debug/update PCB designs Individual progress report |
| Mar 18 | Spring break | Spring break |
| Mar 25 | Solder/debug PCBs | Solder/debug game tile PCB Update game tile PCB design |
| Apr 1 | Finalize user display, dice, master PCBs Order final PCBs | Solder/debug game tile PCB Order rest of game tile PCBs |
| Apr 8 | Assemble and debug | Assemble and debug |
| Apr 15 | Sign up for demo Assemble and debug | Start presentation Assemble and debug |
| Apr 22 | Demo | Demo |
| Apr 29 | Presentation, Final Paper, and Checkout | Presentation, Final Paper, and Checkout |

# 5.0 Discussion of Ethical Considerations

We will uphold IEEE code of Ethics and Academic Honesty. We will make sure our game is safe for mature audiences to use; however, the relatively small board pieces could be a choking hazard for young children. The official game is advised for ages 10 and up. Since we do not plan on selling our board for profit, we avoid running into Intellectual Property regulations.

Safety: We don’t foresee any major safety concerns for our project. The proper precautions for wiring and soldering will be used.