## Slide 1
Virtual Cycling Reality (VCR)
Bryant Johnson, Chongxin Luo, Gregory Knox
Group 47
April 28, 2016
Notes: ECE Main Slide

## Slide 2: Introduction
Virtual Cycling reality is an innovative and enjoyable way to experience bike riding in the comfort of your own home.
User input is captured using sensors on the bike and relayed to the simulation running on your smartphone.
Responsive feedback is given to the user in the form of varying resistance levels and fan speeds.

## Slide 3: Objectives
Wanted to Incorporate:
Provide smooth virtual world for the user to experience
Track user head movement precisely
Accurately sense cycling speed and turning, with low latency user feedback

## Slide 4: Block Diagram

## Slide 5: AC Fan Overview
Triac phase fired control
Pulse delay determines the speed of the fan
Delay based on AC zero crossing signal
Mappings Delays
  5000μs slow
  4000μs medium
  3000μs fast

## Slide 6: Zero Crossing Circuit
Zero crossing circuit detects all zero crossings and provides pulse width of at least 0.05 ms.
Results show 0.616 ms actual pulse width.
Microcontroller interrupt ensures every pulse is acted upon

## Slide 7: Conclusions
Smooth and immersive VR experience achieved.
Precisely tracking the head movement with smartphone accelerometer.
Accurately measure bike speed and handlebar positions for simulation input.
Future Work:
  Exchange Arduino with microcontrollers has more timer interrupts.
  Additional tuning for user input in software side.
  Additional environment building for more realistic experience.
  Adding physical movable bike support for additional physical feedback.

## Slide 8: THANK YOU!
THANK YOU!