## Slide 1: ECE 445 Spring 2016 Group 22
Smart Drone Delivery Improvement
By Sachin Weerasooriya, Rahul Joshi, and
Raymond Hoagland

## Slide 2
Introduction
Drone technology constantly advancing
Wide variety of possible uses
Notes: Sachin

## Slide 3
Amazon’s Delivery Method
Notes: Sachin

## Slide 4
Problems With Model
Current delivery methods have option for signature confirmation
Drone delivery problems:
  No package confirmation
  Theft
  Inadvertent damage
  Delivery to wrong address
Notes: Sachin

## Slide 5
Solution
Unique landing pad per user
Phone App for package confirmation
Threat detection system while drone on ground
Notes: Sachin

## Slide 6
Block Diagram
Notes: Sachin

## Slide 7
R+V For Computer Algorithms
Total .25fps processing speed
Color decryption with 80% accuracy
Drone lands at center(+-2.5ft from middle)
User confirmation sent/received within 1 minute
App works on Android Lollipop
Notes: Joshi

## Slide 8
Computer Vision Design Choices
Camera: Logitech C920
  Commonly used in other drone projects
  Experimentally better
Single Board Computer: ODROID-C1+
  5V2A Supply
  1.5 GHz Quad Core CPUs
  1 GB DDR3 SDRAM
  40 GPIO Pins and 2 ADCs
Notes: Joshi

## Slide 9
Landing Pad Encoding
SHA-1 encoding
Base 4 color scheme
Additional color for padding
Nested contour borders
Notes: Joshi

## Slide 10
Original Idea: Base 16
SHA-1 returns hex bytes
16 Base colors
Colors indistinguishable in HSV
Highly susceptible to confusion
Notes: Joshi

## Slide 11
Why Not Base 2?
Corner Identifier to find center
Overlap due to limited options
Smaller blocks (scaling)
Notes: Joshi

## Slide 12
Why Not QR?
More complicated to scale
Height of Decoding
Notes: Joshi

## Slide 13
Image Capture
Gaussian Blur
Exposure (60%)
Brightness (20%)
512x512 px
Notes: Joshi

## Slide 14
Landing Pad Locator
Average Purple Pixels
Dead Zone 200x200px
HSV detection used
Notes: Joshi

## Slide 15
Image Reconstruction
Nested Contour Area
Rotation to angle
Purple Outline
Original Image
Reconstructed Image
Notes: Raymond

## Slide 16
Image Normalization
Reference Color
CLAHE (Lab-Space)
RGB Normalization
Original Image
RGB + CLAHE
Notes: Raymond

## Slide 17
Image Decoding
HSV Filtering
Pixel Location Match
Ties Favors Expected
Original Image
Recovered Green Sections
Notes: Raymond

## Slide 18
Image Decoding
Direct Similarity
Misses left black
Considers all possible rotations
Susceptible to Rotation Inaccuracy
Original Image
Final Reconstructed Image
Notes: Raymond

## Slide 19
Drone Choice
Drone: 3DR IRIS+ Multicopter
  Pixhawk Controller
  Payload 400 grams
Notes: Sachin

## Slide 20
MAVProxy
Python wrapper (MAVLink protocol) for ODroid
Take off and fly in cross-shaped pattern
Land drone
  Landing pad not found
  Landing pad successfully decoded (> .60 match)
Take off if threat detected (arm every 4 seconds)
Notes: Raymond

## Slide 21
User Application and Server
Android app to request confirmation
GCM Protocol Implementation
Server on odroid
Notes: Joshi

## Slide 22
Sensor Choices
Must avoid threats within 15 feet
PIR & Microwave Motion Sensor
  Small
  Low weight
  Easy to mount
  Low current draw
  Different means of motion detection
Doppler Sensor
PIR Sensor
Notes: Sachin

## Slide 23
PIR Sensors
PIR – Passive Infrared Sensor
Two IR sensitive strips
Device detects IR differential
Digital Output
https://learn.adafruit.com/pir-passive-infrared-proximity-motion-sensor/how-pirs-work

## Slide 24
Microwave Motion (Doppler) Sensor
Transceiver emits 10.525 GHz signal
Analyzes reflected signal
  Reflected signal of moving object will have Doppler Shift
http://www.limpkin.fr/public/HB100/HB100_Microwave_Sensor_Application_Note.pdf

## Slide 25
http://www.limpkin.fr/public/HB100/HB100_Microwave_Sensor_Application_Note.pdf
App Sheet Schematic

## Slide 26
Circuit Design Modifications
Design RC filters

## Slide 27
Amplified Doppler Output

## Slide 28
Interpreting Results
Doppler data fed into ADC
  10 bit resolution, 8KS/S data rate
All PIR sensors read into C1+ via GPIO pins
Multi-thread program monitors each side of drone
Both sensors high in same second is a threat

## Slide 29
System Integration
5 core sub-processes
  I/O Pipes
  Non-blocking read (threaded enqueue)
2 additional threads
  Initiate after landing
  Land again after confirmation
Notes: Raymond

## Slide 30
Delays + Complications
Drone Delivery
DF-13 Connector
SITL support
MAVProxy Documentation
Handling glare
Notes: Joshi

## Slide 31
Further Work
Base 2 Encoding + Auto-correlation
Additional Redundancies (Hamming)
Get the drone flying!
Better glare removal
Verify landing pad exists
Safety Measures
Notes: Joshi