## Slide 1: Variable Voltage Battery Pack
Group 26: Jeffrey Zhu, Mason Randle, Javier Santiago Lara
ECE 445 Final Presentation: Spring 2017

## Slide 2: Our Problem To Solve
Most larger portable power sources are static
Don’t provide active information to the user
People increasingly rely on and consume more electric power

## Slide 3: Objectives
Make a power pack capable of variable AC and DC output
Allow the user to select the output voltage with a control knob
Include voltage and current monitoring
Display information to the user

## Slide 4: Finished Product

## Slide 5: High Level Block Diagram

## Slide 6: Power Stages
DC/DC
Inverter
Transformer
1:4
For High AC:
120 W
12 V
10 A
For Low DC:
40 W
12 V
3.33 A
DC Output:
40 W
40 V
1 A
For High AC:
120 W
40 V
3 A
For High AC:
120 W
30 V rms
4 A rms
For High AC:
120 W
120 V rms
1 A rms

## Slide 7: Review of Original Design
Flyback DC/DC converter with 2 secondary windings
  Low voltage winding for DC output
  High voltage winding to inverter input
Changes made
  Flyback replaced by buck-boost
  Added output transformer to inverter
Reasons for changes
  Difficult to find suitable flyback transformer
  Multiple DC/DC outputs redundant
  Reduction in component voltage stress

## Slide 8: Input Power Module: Battery Charger
Purchased Component
Safety
  Protection
  3 Stage Charging
  Increases Lifespan of Batteries
PHOTO

## Slide 9: Input Power Module: Batteries
Purchased Components
2x 12V 10Ah Lead Acid Batteries
Voltage varies 11.7 - 12.5 V
PHOTO

## Slide 10: Input Power Module: Microcontroller Power Converter
Purchased Component
12 to 5 V DC/DC Power Converter
Did not require feedback
Voltage variation within proper range
PHOTO

## Slide 11: Output Power Module: Buck-Boost Converter
Designed Component
DC/DC Converter
Input: 12V
Output: 5-40V
DC Output of 1 A
Switching frequency: 98kHz
PHOTO

## Slide 12: Buck-Boost: Topography and Operation
Minimum duty cycle: Vo,min = 5, Vin = 12 -> 5/12= D/(1-D) -> Dmin = .29
Maximum duty cycle: Vo,max = 45, Vin = 12 -> 45/12 = D/(1-D) -> Dmax = .79
Images courtesy of learnabout-electronics.org

## Slide 13: Buck-Boost: Circuit Schematic

## Slide 14: Buck-Boost: Control Scheme
C2000 interprets control knob setting through an ADC pin
C2000 generates 98kHz PWM with duty cycle proportional to ADC input
For safety: duty cycle capped at 82%

## Slide 15: Buck-Boost: Voltage Conversion
Ideal Voltage Conversion Graph (Vin = 12V)
Measured Voltage Conversion (50 Ω Load)

## Slide 16: Buck-Boost: More Results
Voltage ripple was successfully kept under 5% with large inductors and output capacitance
Gate Driver Waveform was usually clean (more on this later)

## Slide 17: Buck-Boost: Efficiency Results
Test Conditions:
12V input
1 A output
Results:
80-90% efficiency

## Slide 18: Buck-Boost: Performance

## Slide 19: Output Power Module: Inverter & Transformer
Full Bridge Inverter
Input: 5-40V from buck-boost
Output: 4-30V AC RMS
Frequency: 60Hz
Purchased Component: Transformer
4:1 Turns Ratio
Steps up AC Voltage on Output

## Slide 20: Inverter: Circuit Schematic

## Slide 21: Inverter: Harmonic Elimination
Switching timing technique which can remove specific harmonic components
Used to remove the third (largest) harmonic by setting delta to 30 degrees
Reduces THD considerably
Image courtesy of researchgate.net

## Slide 22: Inverter: Circuit Topography
Image Courtesy of Electronics-Tutorial.net

## Slide 23: Inverter: Control Scheme
Reduce the output THD through 3rd harmonic elimination
~2us of programmed deadtime between high and low switches, for safety
Voltage in yellow, current in green
Yellow and blue, 180 degrees shifted
Yellow and red, 120 degrees shifted

## Slide 24: AC Voltage Output: Experimental Results
Output AC voltage dependent on output DC voltage
Tested output range of 13 to 120 Vrms

## Slide 25: AC Output: User Input Verification

## Slide 26: Control Module: Measurement Circuit
2 Voltage Measurement
  Battery voltage
  Buck-boost output
3 Current Measurements
  Battery current
  DC output current
  AC output current
LCD display

## Slide 27: Measurement Circuit Hardware
Voltage Measuring
  Resistive divider down to 0-5V
  Op-amp buffer for battery voltage
  Inverting op-amp for buck-boost voltage
Current Measuring
  ACS hall effect sensor, used for both AC and DC currents
Arduino
  Voltages and currents interpreted by Arduino program
LCD
  Displays voltage and current values to user

## Slide 28: Measurement Circuit Software
Voltage sensing Algorithm
Measure ADC input
Scale ADC value according to resistive divider
DC sensing Algorithm
Measure ADC voltage output of ACS chip
Multiply by scale factor for current
Add offset
AC sensing Algorithm
Measure Vpp from ACS
Calculate Vrms
Convert to Irms using scale factor and offset

## Slide 29: Final Results: Meeting Power Requirements
Buck-Boost | Met? | Inverter | Met? | AC Output | Met?
5-40 V | Yes | Remove 3rd Harmonic | Yes | 120 V RMS | Yes
1 A | Yes | 30 V RMS | Yes | 1 A RMS | No
75% Eff | Yes |  |  |  | 
5% Ripple | Yes |  |  |  | 

## Slide 30: Final Results: Meeting Other Requirements
The input power module successfully met all its requirements to charge, supply battery power, and power microcontrollers
The C2000 successfully controlled both converters
Arduino measurement circuit code created and was able to control display
Measurement circuit functionality and LCD screen were not implemented in the final project successfully

## Slide 31: Design Challenges: Bootstrap Gate driver
Why bootstrap gate driving is necessary
  Inverter and buck-boost have high side gates (source not directly grounded)
  C2000 cannot source sufficient power to drive a power MOSFET
ICs exist to fulfill this need
  Add external bootstrap and bypass capacitors
  Can be used to drive low and high side gates simultaneously
Image courtesy of Electronics Weekly

## Slide 32: Design Challenges: Bootstrap Gate Driver
Problems with original IC choice: UCC27211D
  Low tolerance to transient negative source voltage spikes
  PCB did not include protection measures
  Destroyed 10 ICs in course of testing
  Improper grounding for buck-boost gate driver
New gate driver selected: IRS21867S
  Resilient to negative transient voltage spikes
  Incorporated clamping diode and limiting resistors
  New gate driver necessitated deviation from original PCB traces
  Demonstrated survivability and functionality

## Slide 33: Design Challenges: Measurement Circuit
LCD display
  Successfully tested LCD drive
  LCD failed during final tests. No replacement available

## Slide 34: Design Challenges: High Power Testing
At high duty cycle and high amps signal noises became larger
Gate driver output waveform began to “skip” which caused audible ringing and voltage drop
Issue was partially resolved with clamping diodes and lower gate driver power voltage

## Slide 35: Future Work
Purchase new LCD screen and incorporate measurement circuit into final design
Fix Buck-Boost voltage drop problem to increase output power of project

## Slide 36: Thank You! Questions?