## Slide 1
Collective Child Tracking System
Mark Hafter, Omar Joya, Ellery Tomaszkiewicz (Group 39)
ECE 445 Spring 2017
Notes: Ellery

## Slide 2
Meet the Group
Ellery Tomaszkiewicz
Senior, Electrical Eng.
Power Systems
Mark Hafter
Senior, Computer Eng.
Networking
Omar Joya
Senior, Electrical Eng.
RF and DSP
Notes: Ellery

## Slide 3
Objective
The CCTS reduces stress on adult supervisors of children’s groups by facilitating the relative and geolocation of multiple children at the same time, in a diverse range of environments.
Notes: Ellery

## Slide 4
Introduction
The Collective Child Tracking System is made up of:
1
2
3
A child device that can be worn or carried and contains SMS and geolocation capabilities
An adult device that can keep track of up to 30 devices within a certain radius
A smartphone application that interfaces the connection among the 30 devices
Notes: Ellery

## Slide 5
System Overview
Within 150m line-of-sight, child and parent devices communicate with periodic handshakes
SAFE
FALLBACK
When the child device reaches out-of-range, the adult receives notification of his/her last known location
RESTORE
The adult supervisor receives notification of any child device that returns within range
Child Device
Adult Device
Smartphone/UI
Notes: Ellery

## Slide 6
System Overview
SMS/GSM
Bluetooth
Sub GHz
Notes: Omar

## Slide 7
Block Diagram
1
2
3
Microcontroller
Sub-GHz Transceiver
GSM Module
4
5
Smart Phone App / UI
Power System
PRIMARY COMPONENTS
(see Appendix for detailed R&V)
Notes: Omar

## Slide 8
Subsystems and Requirements

## Slide 9
Microcontroller
Features and Requirements
ADULT DEVICE
Software SPI support
16 MHz clock exceeds needs for 30+ child devices
CHILD DEVICE
Modified library support for GSM communication
Designed for low-power consumption
TxRx
BLE
TxRx
GSM
(see Appendix for software flow graphs)
Notes: Omar

## Slide 10
Microcontroller
Circuit Configuration: Child Device
Notes: Omar

## Slide 11
MASTER | SLAVE 1 | SLAVE 2 | SLAVE 3 | SLAVE 4 | MASTER | SLAVE 1 | SLAVE 2 | SLAVE 3 | SLAVE 4
t=0
t=n
ƒ MHz:
TDMA Frame
…
Microcontroller
TDMA: Sharing the Channel
Notes: Mark

## Slide 12
ADULT | CHILD 1 | CHILD 2 | . . . | CHILD 30 | ADULT | CHILD 1 | CHILD 2 | . . . | CHILD 30
t=0
t=5 s
920 MHz:
TDMA Frame
…
Microcontroller
TDMA: Sharing the Channel
Notes: Mark

## Slide 13
Sub-GHz Transceiver
Operating frequency of 902 MHz for greater range within the ISM frequency band
1
3
2
FEATURES
PCB trace antenna, omnidirectional
Synchronized clock to 16MHz with MCU
Serial (SPI) input and output to MCU
Child-Adult Communication
1
2
3
Notes: Omar

## Slide 14
Friis transmission equation: Making a conservative estimate on communication range.
SPECIFICATIONS
Reception sensitivity
Output power
Antenna gain
Operating frequency
Sub-GHz Transceiver
Calculation of Range
Notes: Omar

## Slide 15
Sub-GHz Transceiver
Range Results
Adult
Child
Transceiver testing exceeded our expectations
Indoors: ~70 meters
Outdoors: ~150 meters
Notes: Omar

## Slide 16
GSM Module
Overview
FEATURES
Phone-on-chip
GSM Network connection
Cellular tower monitoring
Notes: Mark

## Slide 17
GSM Module
Fallback: Geolocation When Out of Range
SAFE
FALLBACK
Child Device
Adult Device
Notes: Mark

## Slide 18
GSM Module
Fallback: Geolocation When Out of Range
FALLBACK
Child Device
Adult Device
Notes: Mark

## Slide 19
GSM Module
Fallback: Geolocation When Out of Range
Child Device
FALLBACK
Notes: Mark

## Slide 20
GSM Module
Fallback: Geolocation When Out of Range
Adult Device
FALLBACK
Notes: Mark

## Slide 21
Power System
500mAh Lithium Polymer Mini Rechargeable Battery
FEATURES
1
2
3
3.7V to 4.2 V output voltage
40mm x 25mm x 4.9mm
Total Battery Life:
Battery
This equation uses current draw without peaks, with peaks, the total battery life would be around 10.5 to 11 hours

## Slide 22
Power System
5V input Micro-B USB connector to Battery (3.75V-6V VDD MCP73831 LIPO Charger)
FEATURES
1
2
3
Red LED (charging) and Green LED (done charging)
500mA charge current with jumper soldered
Charging is performed in three stages
- Pre-conditioning
- Fast Charge
- Trickle Charge
Battery Charger
Notes: First a preconditioning charge, then a constant-current fast charge, and finally a constant voltage trickle charge to keep the battery topped-up

## Slide 23
Power System
3-terminal Adjustable Regulator from 1.25V to 37V (LM317)
Components connected to the voltage regulator (Vout = 2.8V)
Sub-GHz Transceiver
Bluetooth LE
Voltage Regulator
Equation used to find Vout

## Slide 24
Smart Phone Application
GSM Data Input
{
radioType: gsm
considerIP: false
cellTowers: [
{
cellID:
locationAreaCode:
mobileCountryCode:
mobileNetworkCode:
}
{
cellID:
locationAreaCode:
mobileCountryCode:
mobileNetworkCode:
}
]
}
REQUEST
JSON
RAW CELL DATA
Notes: Omar

## Slide 25
JSON
MAP COORDINATES
Smart Phone Application
GSM Data Input
Notes: Omar

## Slide 26
Smart Phone Application
App Features
FEATURES
Automatic connection to BLE module (UART)
Tracking 30 children with 5 s updates
Geographic location and radius during fallback
1
2
3
1
2
3
Notes: Omar

## Slide 27
Safety and Ethics
1
2
3
Lithium-Polymer Battery Risks
Assurance of Protection
Finite-energy battery
Removal of device
Privacy Risks
Capturing location of children in real time
Children vs. adult privacy rights

## Slide 28
Conclusions

## Slide 29
Test Methods
SERIAL MONITOR
OSCILLOSCOPE
COMMON SENSE
Check that devices are functioning and integrated
Track power consumption
Check that devices are communicating useful data
Debug for hours…
Check for silly mistakes
Avoid hazards

## Slide 30
Setbacks in Design
PCB design needed reiteration and was not sustainable in design process

## Slide 31
Setbacks in Design
Operating voltage was too low for voltage regulator to function as we wanted
Battery Voltage: 4.1 V
Operating Voltage: 5.0 V

## Slide 32
Setbacks in Design
Redesign of pinouts for simultaneous hardware and software SPI
Disposal of faulty LiPo battery
Hours of circuit-debugging for trivial reasons
Loss of child device from short-circuiting

## Slide 33
Did We Fulfill Our Goal?
High Level Requirements
System must determine if a specific child device is within 50 meters range of adult device at intervals of ten seconds or less
Child devices must transmit via SMS the current cellular telemetry data from the GSM modem
Child devices must function for at least five hours
The child devices must be wearable

## Slide 34
Conclusions and Future Work
1
2
3
Prototype to avoid waste
Improvement: make it dynamic
Form factor and user needs

## Slide 35
Thank You
Questions?

## Slide 36
Appendix

## Slide 37
Adult Device Flow Graph

## Slide 38
Child Device Flow Graph