## Slide 1
Wi-Fi Enabled Motorized Windows For Automatic Climate Control
Group 34: Trevor Bush, Alex Casino, Ryan Stark
ECE 445 Spring 2017

## Slide 2
Motivation:
  HVAC systems account for up to 50% of building energy consumption
  Outdoor climate can improve indoor temperature
  Manual window movement is tedious and can be inefficient
Solution:
  Use real time climate data to automatically control window position
  Control wirelessly for convenient use and scalability
Introduction

## Slide 3
Automatically close windows
  When it is raining
  If it is too hot or cold
Automatically open windows
  If outdoor weather can positively impact indoor temperature
Control from a smartphone
  Set comfortable temperature range. Get updates about window position, temperature, and rain status.
Goals

## Slide 4
Window Design
Window: Inside View
IR Sensor
Ultrasonic Sensor
Motor
Motor Driver PCB
Window Unit
AC/DC Converter
Limit Switches
Window: Outside View
Rain Sensor
Temperature Sensor

## Slide 5
Block Diagram - Complete

## Slide 6
Block Diagram – Window Unit
Motor
Sensors
Window Microcontroller
Wi-Fi Module
Window
Power Management System
AC/DC Converter
Buck Converter
120 VAC
12 VDC
12 VDC
5 VDC
Linear Regulator
5 VDC
3.3 VDC
IR Proximity
Moisture
Temperature
Motor Driver
Ultrasonic Sensor
Motor
Limit Switches
Legend
Power
Digital Data
Wireless Data
Analog

## Slide 7
Block Diagram - Hub Unit
Temperature Sensor
Sensors
Window Microcontroller
Wi-Fi Module
Central Hub
Power Management System
AC/DC Converter
120 VAC
5 VDC
Linear Regulator
5 VDC
3.3 VDC
Legend
Power
Digital Data
Wireless Data
Analog

## Slide 8
System Control Flow

## Slide 9
Motor Driver
Window Unit
Hub Unit
PCB Designs

## Slide 10
TI DRV8886 Stepper Driver
Step/Direction
5 inputs from MCU
1 output to MCU
4 outputs to motor
Motor Driver PCB

## Slide 11
Motor Driver PCB

## Slide 12
Motor Control Flow
How the window opens

## Slide 13
ATMega328 MCU
TI LM22676 Buck Converter
TI LM2937 LDO
Powered by 12V and had nets of 5V and 3.3V
Inputs and outputs to sensors, motor driver, and Wi-Fi module
Window Unit

## Slide 14
Window Unit
Schematic
Notes: Imin = .1A, F = 500*10^3 Hz Vin = 12V Vout = 5V

## Slide 15
Window Unit PCB

## Slide 16
ATMega328 MCU
TI LM2937 LDO
TI LM35DMX Temperature Sensor
Receives and transmits data to Wi-Fi module and smartphone
Powered by 5V and has nets of 5V and 3.3V
Hub Unit

## Slide 17
Hub Schematic

## Slide 18
If indoor temperature is out of user preference
  Open window if outside is improvement
  Close window if outside is worse
If indoor temperature is within user preference
  Do nothing
Climate Control Flow

## Slide 19
Ex. Indoor Temperature = 80
Outdoor Temperature = 70
User preference = 70 to 75
Action = Open Window
Climate Control Flow Example

## Slide 20
Power System
Motor
Sensors
Communication
Block Descriptions

## Slide 21
Power Management
Output voltages must be within ±2% at expected load current
Load testing using DC Electronic Load
All power supplies passed the load testing
Converter | I_L (A) | Min Allowed V_out (V) | Max Allowed V_out (V) | Measured V_out (V)
AC-DC 120-5V | 1 | 4.90 | 5.10 | 4.96
AC-DC 120-12V | 2 | 11.76 | 12.24 | 11.91
DC-DC 12-5V | 1 | 4.90 | 5.10 | 4.91
DC-DC 5-3.3V | 0.3 | 3.23 | 3.37 | 3.30

## Slide 22
Nema 17 Stepper Motor
27/1 Planetary Gearbox
3 Nm torque
7.2 rpm
Stepper Motor

## Slide 23
Used to detect whether the window is fully open or fully closed
Limit Switches
Schematic

## Slide 24
Uxcell rain sensor
Analog and digital outputs
Potentiometer to determine sensitivity
Rain Sensor

## Slide 25
TI LM35DMX/NOPB
0.5º C ensured accuracy
Range of -55º C to 150º C
Temperature Sensor

## Slide 26
Calibrates to ambient IR levels
Digital output for change in IR detected
Proximity IR Sensor

## Slide 27
Ultrasonic Sensor - Overview
Used to detect the distance that the window has moved
Detects jammed or stalled window

## Slide 28
Ultrasonic Sensor - Calculations
v = speed of sound (m/s)
T = temperature (°C)
t = round trip time (μs)
d = distance (in)

## Slide 29
Ultrasonic Sensor – Test Setup
Range of 2-10.5 inches
100 measurements taken at every .5 inch increment

## Slide 30
Ultrasonic Sensor – Test Results

## Slide 31
Example: Closing Window
Ultrasonic Sensor - Window Position
Distance (inches) | Delta (inches)
4.89 | 
5.16 | .27
5.34 | .18
5.64 | .30
5.88 | .24
Takes average of 5 distance measurements every .25 inches (10 seconds of motion)
Delta must be between .15 and .35 inches

## Slide 32
ESP-01 Wi-Fi modules
Wired communication with MCUs using UART
One module acts as an access point (with WPA security)
Wireless communication via http requests
Wi-Fi Communication
Window Module
(Client)
Hub Module
(Access Point)
Smartphone
(Client)

## Slide 33
App Interface
User preference range
Auto Control
Position Status
Rain Status

## Slide 34
Window open/closed successfully
Control flow implemented
Successful communication between phone, hub, and window
Conclusion

## Slide 35
More advanced user options
Integration into an existing home safety and climate system
Research into using a quieter motor
Implement using a casement window for improved safety and visual appeal
Future Developments

## Slide 36
Glen Hedin
Kexin Hui
Special Thanks!

## Slide 37
Thank You