## Slide 1: 16 Step Analog/Digital Synthesizer
Team #1
Justin Sconza and Kyle Vondrak
TA: Eric Clark
Sponsor: Skot Wiedmann

## Slide 3: Introduction
Low cost, easy to play instrument
Combines both a synthesizer and a step sequencer into an easy to use package
Intended for hobbyists, or those just becoming interested in music synthesis

## Slide 4: Objectives
User control of tempo via keypad
Easily adjustable voltage control for synthesizer
Ability to be used in any location that standard wall outlets are available

## Slide 5: Block Diagram

## Slide 6: VCO - Control and Octave/Volt
Aiming for one octave/volt
Coarse and fine tuning adjustable trimpots
Octave/volt adjustable trimpot for fine tuning
1% resistors used for best accuracy

## Slide 7: VCO - Exponentiator
Dual Pair must be perfectly matched

## Slide 8: VCO - Oscillator
Fast comparator to make reset time as small as possible
Ultra-high impedance integrator
JFET has high pinch-off and low on resistance

## Slide 9: Waveshaper - Sawtooth
Amplifies Raw Sawtooth to 20 Vp-p

## Slide 10: Waveshaper - Square
Slams Raw Sawtooth to +10 V or -10 V

## Slide 11: Waveshaper - Triangle
Diodes add together Sawtooth and Inverted Sawtooth
Inverts and amplifies output to 20 Vp-p

## Slide 12: Verification
Reset time of sawtooth less than 1% of total period.
Trapezoidal Component of Square less than 1% of total period
Sawtooth Reset Time
Square Trapezoidal Time

## Slide 13: Verification - Waveshaper
Peak to Peak is within 10% of 20 V
Frequency = 60 Hz * 2Control Volts

## Slide 14: Verification - Waveshaper
Peak to Peak is within 10% of 20 V
Frequency = 60 Hz * 2Control Volts

## Slide 15: Verification - Waveshaper
Peak to Peak is within 10% of 20 V
Frequency = 60 Hz * 2Control Volts

## Slide 16: Block Diagram - TTL Stage

## Slide 17: TTL Stage
Counter driven by PWM output from MCU stage
Control Voltage set by potentiometers

## Slide 18: TTL - Priority Encoders

## Slide 19: Verifications
Pushbuttons perform task in less than 50 ms
Voltage range of sliders is 0.005 to 5.01 V
0.1% error on the lower limit
0.2% error on the upper limit

## Slide 20: Block Diagram - MCU Stage

## Slide 21: MCU Stage

## Slide 22: Software

## Slide 23: Verifications
Keypad works and correctly displays BPM value
Goal was to keep output BPM within 1% of input value

## Slide 24: Block Diagram - Power Supply

## Slide 25: Power Supply - Analog Supply
VCO Power Inputs
Bipolar Voltage for Electric Switch

## Slide 26: Power Supply - Digital Supply

## Slide 27: Fixing the Current Problem
Large current when LED display was switching caused sharktooth dips in MCU voltage
Fixed by switching to DC-DC converters for better isolation
  Eliminated the voltage sag

## Slide 28: Verifications
+10 V Regulator measured at +10.01 V
-10 V Regulator measured at -10.00 V
+5 V DC-DC Step-down converter measured at +5.01 V
+3.3 V DC-DC Step-down converter measured at +3.300 V

## Slide 29: Block Diagram - Output and UI

## Slide 30: Output Stage

## Slide 31: User Interface
First version of UI board was found to contain errors
Two 8 step UI boards were then designed and chained together to form 16 steps

## Slide 32: User Interface - Uncertainties
Buttons found to be broken on final board
Caused by desoldering from previous version of UI board

## Slide 33: Future Work
Create visually appealing enclosure, and to reduce the number of wires (Ribbon cables)
Adding extra features such as voltage controlled filters (VCF) and additional waveshapes
Using CPLDs to replace the TTL logic ICs

## Slide 34: Conclusion
Successful in achieving all design goals
  BPM tempo can be easily input and a corresponding PWM wave is generated
  Control Voltage levels, offset and range easily adjustable on the UI board
  User is able to skip, hold and start over via pushbuttons
  Three distinct waveshapes were successfully generated
  Power supply is robust and portable

## Slide 35: Questions?

## Slide 36: Thank You!