## Slide 1
Team 55: Head Impact Telemetry Data Logging System
Matt Hebard, Matt Schafer, & Evan Qi

## Slide 2
Introduction
Concussions are a major factor in most high impact sports
No accurate system in market that gives good data for concussion correlation
Millions of dollars have been poured into developing a system…

## Slide 3
Create a system that can provide valuable and accurate data to researchers
A wearable design that any athlete can wear in a high impact sport
Answer the question: Is it feasible for an ECE 445 group to build this design under certain constraints?
Objective

## Slide 4
Design
Takes accelerometer and heart rate data
Time stamp this data to microSD to be used for further use
Design system under constraints:
  Power: System runs at 3.3v
  PCB Size: 10cm x 9cm x 2cm
  Wearability: Fit on any athletes body

## Slide 5
Device will be attached to athletes body
Durable and can adjust to athlete
Weight < 400g
Design (cont.)

## Slide 6
Block Diagram

## Slide 7
Small enough to attach to athletes head
Uses the ADXL375 3-axis accelerometer
Own power supply: 3.3v Coin Cell
Communicates via SPI: 4 MHz
Accelerometer PCB
3.2cm
7.5cm
ADXL375
Battery Holder
Notes: How does the speed relate to our overall design?
Research states in order to collect useful data for analyzing concussive blows, need a Bandwidth of at least 600Hz
Our output data rate we set to 1600Hz to achieve bandwidth of 800Hz
Need high speed communication to ensure no missed samples of data

## Slide 8
Sampling rate: 1600 Hz
BW: 800 Hz
Data from Accelerometer
Force (Gs)
X Axis of Accel
Z Axis of Accel
Y Axis of Accel
Time (ms)
Notes: High sampling rate ensures the correct detection and magnitude of hit in high impact sports
Football hits last roughly 10ms

## Slide 9
Sampling rate: 100 Hz
BW: 50 Hz
Data From Acceleromter (cont.)
Z Axis of Accel
Y Axis of Accel
X Axis of Accel
Force (Gs)
Time (ms)
Notes: We can miss the entire magnitude of the impact due to low sampling rates (100Hz)

## Slide 10
Need to understand noise characteristics for research use
Noise Analysis
Force (Gs)
Time (ms)
Avg. 1g output
Actual Signal

## Slide 11
As bandwidth changes based on the desired constraints, noise increases by 5mg/
Noise Analysis (Cont.)
SNR at 800 Hz =
= 18dB

## Slide 12
Two AA Energizer Alkaline batteries
LTC3402 Boost Converter
Outputs 3.3v with max 1A draw
Specifically for MCU and microSD
Power
8cm
8.8cm
AA Battery Holder
LTC3402
Output

## Slide 13
MCU PCB
ATmega328P
3.3V input | Max current draw of 250 mA
Communicates via SPI
7.1cm
10cm
ATmega328P
Breakout Board

## Slide 14
10-bit Analog/Digital Converter
Adaptive response to variance in inputs
BPM Calc
Heart Rate Sensor
BPM Graph

## Slide 15
Real-time digital filtering
Heart Rate Sensor (cont.)
Digital Filter

## Slide 16
5v -> 3.3v conversion
Interface through microSD breakout board
Datalog format at 1600 Hz
  “hh:mm:ss.sss - ±xxx.xx ±yyy.yy ±zzz.zz H hhh.h”
  Easy access and readability for graphing and analysis
MicroSD

## Slide 17
Power
  Battery System did not output correctly
  Communication
Challenges
Notes: We need a final statement telling us of our findings
What worked/ What didn’t?
How could we improve on the design?
What did we learn? Key takeaways

## Slide 18
Accelerometer Logged Data
Results
HR Sensor Logged Data

## Slide 19
Testing on Human subject for wearability and accuracy during activity
Making number of Accelerometers scalable
Looking Forward

## Slide 20
Questions?
Thank You!