## Slide 1: Requirements and Verification
ECE445

## Slide 2: What is RV table?
A two-column table with requirements on the left, and verification on the right
A checklist for both modular goals and modular debugging
If all requirements have been verified by your verification for every module, you should have a fully functioning project.

## Slide 3: Requirements
A technical definition of what each and every module in your system block diagram must be able to do
Quantitative (tolerance range)
Thorough and detailed
Driven by project goals
Design requirements ≠ purchase requirements

## Slide 4: Verification
A set of procedures that you will use to verify that a requirement has been met
Equipment
Test procedures
Presentation of results
Explicit

## Slide 5: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.

## Slide 6: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
What is battery voltage?

## Slide 7: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
Do I fail if the output is 3.25V?

## Slide 8: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
Do we miss any requirements? e.g, current draw?

## Slide 9: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
How to measure?

## Slide 10: Good RV Example
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0 -300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.

## Slide 11: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Quantitative measurable ranges
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 12: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Very detailed and thorough
requirements
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 13: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Step-by-step procedure
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 14: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Equipment
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 15: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Explicit set-up/configuration
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 16
If you have any questions, contact your TA!