## Slide 1: ECE 476 Power System Analysis
Lecture 1:Introduction
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
overbye@illinois.edu

## Slide 2: About Prof. Tom Overbye
Professional
  Received BSEE, MSEE, and Ph.D. all from University of Wisconsin at Madison (83, 88, 91)
  Worked for eight years as engineer for an electric utility (Madison Gas & Electric)
  Have been at UI since 1991, doing teaching and doing research in the area of electric power systems
  Developed commercial power system analysis package, known now as PowerWorld Simulator. This package has been sold to about 600 different corporate entities worldwide
  DOE investigator for 8/14/2003 blackout

## Slide 3: About Prof. Tom Overbye
Nonprofessional
  Married to Jo
  Have three children
    Tim age 21
    Hannah age 19
    Amanda age 17
  Live in country by Homer on the Salt Fork River
  We’ve homeschooled our kids all the way through, with Tim now starting his fourth year at UIUC in ME and Hannah her second year in psychology

## Slide 4: About Iyke Idehen
3rd year graduate student
  BSc (ECE, University of Benin, Nigeria)
  MSc (EE, Tuskegee University, Alabama)
  Research Area
    Power Systems and Control
    Data visualization
  Advisor: Prof. Tom Overbye
  Hobbies & Interests: Soccer, Music, Travel
Hollywood, 2014
Soccer field by FAR/PAR (2014)
Courtesy: Won Jang

## Slide 5: Simple Power System
Every power system has three major components
  generation: source of power, ideally with a specified voltage and frequency
  load: consumes power; ideally with a constant resistive value
  transmission system: transmits power; ideally as a perfect conductor

## Slide 6: Complications
No ideal voltage sources exist
Loads are seldom constant
Transmission system has resistance, inductance, capacitance and flow limitations
Simple system has no redundancy so power system will not work if any component fails

## Slide 7: Notation - Power
Power: Instantaneous consumption of energy
Power Units
Watts = voltage x current for dc (W)
kW – 1 x 103 Watt
MW – 1 x 106 Watt
GW – 1 x 109 Watt
Installed U.S. generation capacity is about 1000 GW ( about 3 kW per person)
Maximum load of Champaign/Urbana about 300 MW

## Slide 8: Notation - Energy
Energy: Integration of power over time; energy is what people really want from a power system
Energy Units
  Joule = 1 Watt-second (J)
  kWh = Kilowatthour (3.6 x 106 J)
  Btu = 1055 J; 1 MBtu=0.292 MWh
  One gallon of gas has about 0.125 MBtu (36.5 kWh);
U.S. electric energy consumption is about 3600 billion kWh (about 13,333 kWh per person, which means on average we each use 1.5 kW of power continuously)

## Slide 9: Power System Examples
Electric utility: can range from quite small, such as an island, to one covering half the continent
  there are four major interconnected ac power systems in North American, each operating at 60 Hz ac; 50 Hz is used in some other countries.
Airplanes and Spaceships: reduction in weight is primary consideration; frequency is 400 Hz.
Ships and submarines
Automobiles: dc with 12 volts standard
Battery operated portable systems

## Slide 10: North America Interconnections

## Slide 11: Electric Systems in Energy Context
Class focuses on electric power systems, but we first need to put the electric system in context of the total energy delivery system
Electricity is used primarily as a means for energy transportation
  Use other sources of energy to create it, and it is usually converted into another form of energy when used
About 40% of US energy is transported in electric form
Concerns about need to reduce CO2 emissions and fossil fuel depletion are becoming main drivers for change in world energy infrastructure

## Slide 12: Looking at the 2015 Energy Pie: Where the USA Got Its Energy
About 40% of our energy is consumed in the form of electricity, a percentage that is gradually increasing. The vast majority on the non-fossil fuel energy is electric!
About 81% Fossil Fuels (86% in 1990 and 2000)
In 2015 we got about 1.9% of our energy from wind and 0.6% from solar (PV and solar thermal), 0.2% from geothermal
Source: EIA Monthly Energy Review, July 2016
Total of 97.5 Quad; 1 Quad = 293 billion kWh (actual), 1 Quad = 98 billion kWh (used, taking into account efficiency)

## Slide 13: US Historical Energy Usage
Source: EIA Monthly Energy Review, July 2016

## Slide 14: Renewable Energy Consumption
Source: EIA Monthly Energy Review, July 2016

## Slide 15: Growth in US Wind Power Capacity
Source: AWEA Wind Power Outlook 2 Qtr, 2016
The quick development time for wind of 6 months to a year means that changes in federal tax incentives can have an almost immediate impact on construction

## Slide 16: Wind Capacity Installations by State
Source: AWEA Wind Power Outlook 2 Qtr, 2016

## Slide 17: The World
Source: EIA, International Energy Outlook 2016

## Slide 18: Energy Economics
Electric generating technologies involve a tradeoff between fixed costs (costs to build them) and operating costs
  Nuclear and solar high fixed costs, but low operating costs (though cost of solar has decreased substantially recently)
  Natural gas/oil have low fixed costs but can have higher operating costs (dependent upon fuel prices)
  Coal, wind, hydro are in between
Also the units capacity factor is important to determining ultimate cost of electricity

## Slide 19: Ball park Energy Costs
Source: Steve Chu and Arun Majumdar, “Opportunities and challenges for a sustainable energy future,” Nature, August 2012, Figure 6
Energy costs depend upon the capacity factor for the generator. The capacity factor is the ratio of the electricity actually produced, divided by its maximum potential output. It is usually expressed on an annual basis.

## Slide 20: Natural Gas Prices 1997 to 2015
Marginal cost for natural gas fired electricity price
in $/MWh is about 7-10 times gas price
Source: http://www.eia.gov/dnav/ng/hist/rngwhhdW.htm

## Slide 21: Coal Prices have Fallen Substantially from Five Years Ago
BTU content per pound varies between about 8000 and 15,000 Btu/lb, giving costs of around $1 to 2/Mbtu
July 2016 prices per ton range from $8.70 to $43.35
Source: eia.gov/coal

## Slide 22: Solar PV Prices
Image: http://cleantechnica.com/2015/08/13/us-solar-pv-cost-fell-50-5-years-government-report/screen-shot-2015-08-12-at-12-33-53-pm/

## Slide 23: Course Syllabus
Introduction and review of phasors & three phase
Transmission line modeling
Per unit analysis and change of base
Models for transformers, generators, and loads
Power flow analysis and control
Economic system operation/restructuring
Short circuit analysis
Transient stability
System protection
Distribution systems

## Slide 24: Brief History of Electric Power
First real practical uses of electricity began with the telegraph (1860's) and then arc lighting in the 1870’s
Early 1880’s – Edison introduced Pearl Street dc system in Manhattan supplying 59 customers
1884 – Sprague produces practical dc motor
1885 – invention of transformer
Mid 1880’s – Westinghouse/Tesla introduce rival ac system
Late 1880’s – Tesla invents ac induction motor
1893 – Three-phase transmission line at 2.3 kV

## Slide 25: History, cont’d
1896 – ac lines deliver electricity from hydro generation at Niagara Falls to Buffalo, 20 miles away; also 30kV line in Germany
Early 1900’s – Private utilities supply all customers in area (city); recognized as a natural monopoly; states step in to begin regulation
By 1920’s – Large interstate holding companies control most electricity systems

## Slide 26: History, cont’d
1935 – Congress passes Public Utility Holding Company Act to establish national regulation, breaking up large interstate utilities (repealed 2005)
    This gave rise to electric utilities that only operated in one state
1935/6 – Rural Electrification Act brought electricity to rural areas
1930’s – Electric utilities established as vertical monopolies
Frequency standardized in the 1930’s

## Slide 27: Vertical Monopolies
Within a particular geographic market, the electric utility had an exclusive franchise
Generation
Transmission
Distribution
Customer Service
In return for this exclusive
franchise, the utility had the
obligation to serve all
existing and future customers
at rates determined jointly
by utility and regulators
It was a “cost plus” business

## Slide 28: Vertical Monopolies
Within its service territory each utility was the only game in town
Neighboring utilities functioned more as colleagues than competitors
Utilities gradually interconnected their systems so by 1970 transmission lines crisscrossed North America, with voltages up to 765 kV
Economies of scale keep resulted in decreasing rates, so most every one was happy

## Slide 29: History, cont’d -- 1970’s
1970’s brought inflation, increased fossil-fuel prices, calls for conservation and growing environmental concerns
Increasing rates replaced decreasing ones
As a result, U.S. Congress passed Public Utilities Regulator Policies Act (PURPA) in 1978, which mandated utilities must purchase power from independent generators located in their service territory (modified 2005)
PURPA introduced some competition

## Slide 30: PURPA and Renewables
PURPA, through favorable contracts, caused the growth of a large amount of renewable energy in the 1980’s (about 12,000 MW of wind, geothermal, small scale hydro, biomass, and solar thermal)
  These were known as “qualifying facilities” (QFs)
  California added about 6000 MW of QF capacity during the 1980’s, including 1600 MW of wind, 2700 MW of geothermal, and 1200 MW of biomass
  By the 1990’s the ten-year QFs contracts written at rates of $60/MWh in 1980’s, and they were no longer profitable at the $30/MWh 1990 values so many sites were retired or abandoned

## Slide 31: Abandoned Wind Farm Need South Point in Hawaii
Source: Prof. Sanders