## Slide 1: ECE 476 Renewable Energy Systems
Lecture 2: Power Industry History, Review of Phasors
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
overbye@illinois.edu

## Slide 2: Announcements
Please read Chapters 1 and 2
HW 1 is 2.7, 16, 24, 33, 47; due Thursday 9/1
  Do the regular problems (not multiple choice)
  HW 1 will be turned in (for other homework we may have an in-class quiz)
  For Problem 2.33 you need to use the PowerWorld Software. You can download the software and cases at the below link; get Version 19 (August 11, 2016) www.powerworld.com/gloveroverbyesarma

## Slide 3: History, cont’d – 1990’s & 2000’s
Major opening of industry to competition occurred as a result of National Energy Policy Act of 1992
This act mandated that utilities provide “nondiscriminatory” access to the high voltage transmission
Goal was to set up true competition in generation
Result over the last few years has been a dramatic restructuring of electric utility industry (for better or worse!)
Energy Bill 2005 repealed PUHCA; modified PURPA

## Slide 4: Electricity Prices, 1960-2010
Sources: EIA, Annual Energy Review, 2010, Figure 8.10; 2015, Fig 9

## Slide 5: Utility Restructuring
Driven by significant regional variations in electric rates
Goal of competition is to reduce rates through the introduction of competition
Eventual goal is to allow consumers to choose their electricity supplier

## Slide 6: State Variation in Electric Rates

## Slide 7: The Goal: Customer Choice

## Slide 8: The Result for California in 2000/1
OFF
OFF

## Slide 9: The California-Enron Effect
Source : http://www.eia.doe.gov/cneaf/electricity/chg_str/regmap.html
RI
AK
electricity
restructuring
delayed
restructuring
no activity
suspended
restructuring
WA
OR
NV
CA
ID
MT
WY
UT
AZ
CO
NM
TX
OK
KS
NE
SD
ND
MN
IA
WI
MO
IL
IN
OH
KY
TN
MS
LA
AL
GA
FL
SC
NC
W
VA
VA
PA
NY
VT
ME
MI
NH
MA
CT
NJ
DE
MD
AR
HI
DC

## Slide 10: The Rise of Natural Gas
Source: US EIA, 2011

## Slide 11: August 14th, 2003 Blackout

## Slide 12: My Favorite Blackout Hoax Photo

## Slide 13: My Favorite 8/14/2003 Blackout Cartoon!

## Slide 14: The Smart Grid
The term “Smart Grid” dates officially to the 2007 “Energy Independence and Security Act”, Title 13 (“Smart Grid”)
  Use of digital information and control techniques
  Dynamic grid optimization with cyber-security
  Deployment of distributed resources including
  Customer participation and smart appliances
  Integration of storage including PHEVs
  Development of interoperability standards

## Slide 15: Smart Grid Perceptions (Some of Us Like the Term “Smarter”)

## Slide 16: Renewable Portfolio Standards (September 2012)
Source: http://www.dsireusa.org/

## Slide 17: In the News: First US Offshore Wind is Complete
US wind has grown rapidly, but none has been offshore
First offshore wind, Block Island Wind Farm, is now complete and should be generating in October 2016
  It has five 6 MW GE direct drive wind turbines (30 MW total)
  Located three miles southeast of Block Island, Rhode Island
  Connected to grid by underwater 34.5 kV three-phase cables
Image source: New York Times, Aug 22, 2016

## Slide 18: North America Electric Load and Generation

## Slide 19: Power System Modeling and Time Frames
Much of class covers power system models. An important quote to keep in mind is
  “Essentially, all models are wrong, but some are useful. However, the approximate nature of the model must always be borne in mind.” G.E.P. Box, N.R. Draper, Empirical Model-Building and Response Surfaces, Wiley, 1987, p. 424.
Power systems covers many different time frames, with essentially no models valid for all of them
Image: Sauer, P.W., M. A. Pai, Power System Dynamics and Stability, Stripes Publishing, 2007

## Slide 20: Review of Phasors
Goal of phasor analysis is to simplify the analysis of constant frequency ac systems
v(t) = Vmax cos(wt + qv)
i(t) = Imax cos(wt + qI)
Root Mean Square (RMS) voltage of sinusoid

## Slide 21: Phasor Representation

## Slide 22: Phasor Representation, cont’d
(Note: Some texts use “boldface” type for complex numbers, or “bars on the top”)

## Slide 23: Advantages of Phasor Analysis
(Note: Z is a complex number but not a phasor)

## Slide 24: RL Circuit Example

## Slide 25: Complex Power

## Slide 26: Complex Power, cont’d

## Slide 27: Complex Power
(Note: S is a complex number but not a phasor)

## Slide 28: Complex Power, cont’d

## Slide 29: Conservation of Power
At every node (bus) in the system
  Sum of real power into node must equal zero
  Sum of reactive power into node must equal zero
This is a direct consequence of Kirchhoff’s current law, which states that the total current into each node must equal zero.
  Conservation of power follows since S = VI*

## Slide 30: Conversation of Power Example
Earlier we found
I = 20-6.9 amps