## Slide 1: Phys 102 – Lecture 14
Faraday’s law of induction

## Slide 2: Today we will...
Continue our discussion of electromagnetic induction unifying electricity & magnetism
  Last time: Lenz’ law for EMF direction
  Today: Faraday’s law for EMF magnitude
Apply these concepts
  Lenz’ & Faraday’s law are basis for electrical generators & transformers, and much more
Power plant
Credit card reader
Guitar pickup

## Slide 3: Faraday’s law of induction
Direction
Lenz’ law: EMF ε opposes change in flux 
Rate of change of flux 
Induced EMF ε
Magnitude
Induced EMF ε = rate of change of flux 
Change in flux  through a loop induces an EMF ε

## Slide 4: ACT: moving loops
Three loops are moving at the same speed v in a region containing a uniform B field. The field is zero everywhere outside.
In which loop is |ε| greatest at the instant shown?
Loop A B. Loop B C. Loop C
A
v
B
v
C
v
Bext

## Slide 5: Faraday’s Law of Induction
“Induced EMF” = rate of change of magnetic flux
    Area of loop covered by flux
    Magnetic field B
    Angle φ between normal and B
Since , 3 things can change F
Notes: http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=1142 (Helmholtz & credit card)
http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=371 (Helmholtz & magnet)

## Slide 6: Calculation: changing area
A bar slides with speed v on a conducting track in a uniform B field
Bext
L
v
x
and only x is changing
What is the magnitude of the EMF induced in the circuit?
Notes: http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=1329

## Slide 7: Moving loops revisited
Three loops are moving at the same speed v in a region containing a uniform B field. The field is zero everywhere outside.
A
v
B
v
C
v
L
w
Bext

## Slide 8: ACT: Moving loop
A loop moves through a region with a uniform B field at a constant speed v. The field is zero outside.
v
Which diagram best represents the EMF ε in the loop vs. time?
ε
ε
ε
t
t
t
B. C.

## Slide 9: Calculation: solenoid cannon
A loop of radius rloop = 11 cm is placed around a long solenoid. The solenoid has a radius rsol = 4.8 cm and n = 10,000 turns/m of wire. The current I through solenoid increases at a rate of 1.5 A/s.
I
Side view
Top view
Bsol
Bsol
EXAM 2, FA13
What is the EMF |ε| in the loop?
B field is changing, area is constant
rloop
rsol

## Slide 10: ACT: time-varying B field
5
10
15
20
t (sec)
B(t) (T)
+1.0
-1.0
0
+0.5
-0.5
0
From EX2, SP11
t = 5 s
t = 12 s
t = 20 s
A circular loop is placed in a uniform B field that varies in time according to the plot on the right.
At which time is the EMF magnitude |ε| in the loop largest?

## Slide 11: Changing φ
–AB
AB

t
EMF can be induced by changing angle φ between loop normal and B field
Rotating loop: Angle φ increases at a rate ω (in rad/s)
B
normal
φ
φ = 30° (CheckPoint 1.1)
Notes: DEMO 109

## Slide 12: Calculation: EMF from changing φ
–AB
AB

t
–εmax
εmax
ε
t
What is the EMF induced by changing angle φ between loop normal and B field?
Δ/Δt represents rate of change or slope of  vs. t at that particular time
EMF is a sine wave!
φ = 30° (CheckPoint 1.2-1.3)

## Slide 13: ACT: Rotating loop
The loop below rotates in a uniform B field. Which of the following factors can increase the EMF in the loop?
Increasing the rotation rate ω
Wrapping more turns of wire around the loop
Increasing the B field
All of the above
B
normal
DEMO
Notes: http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=109

## Slide 14: Application: generators
Electrical generators use external energy source (gas, steam, water, wind, nuclear, etc) to spin loop in B field
Why electrical current from outlets is alternating current (AC)
In US, current oscillates at a frequency of 60 Hz (cycles/s)
U of I coal power plant

## Slide 15: Calculation: CheckPoint 2
A generator produces 1.2 Giga Watts of power, which it transmits to a town through power lines with total resistance 0.01 Ω.
Power delivered by generator through lines:
How much power is lost in the lines if it is transmitted at 120 V?
Power lost in lines:
εgen = 120 V
R = 0.01 Ω
Pgen = 1.2 GW
I
Plost = ?
Notes: Try this example for motivating power lines. Resistivity=10^-8 Ohm Meters. 1 inch square copper wire has about 0.1 ohm resistance in 7 km.

## Slide 16: Electrical power distribution
500,000 V
Low current
240 / 120 V
High current
Transformers make it possible to distribute electrical power at high voltage and “step-down” to low voltage at your house.
Notes: http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=407 (power line model)

## Slide 17: Transformers
Key to modern electrical system
Transform between high and low voltages
Very efficient
Transformers are made of two coils wound around a common iron core
Notes: http://demo.physics.uiuc.edu/LectDemo/scripts/demo_descript.idc?DemoID=255 (transformer)

## Slide 18: Principles of transformers
“Primary” coil
with Np turns
“Secondary” coil
with Ns turns
“Step-up” transformer: Ns > Np
Transformers work by Faraday’s law. Changing current in “primary” creates changing flux in primary and “secondary”
Energy is conserved
Core ensures B field of primary passes through secondary

## Slide 19: ACT: CheckPoint 3.1
You are going on a trip to France where the outlets are 240 V. You remember from PHYS 102 that you need a transformer, so you wrap 100 turns of a primary.
A. 50 B. 100 C. 200
How many turns should you wrap around the secondary to get 120 V out to run your hair dryer?

## Slide 20: ACT: Transformers
A. Vs = 0 V B. Vs = 6 V C. Vs = 12 V D. Vs = 24 V
A 12 V battery is connected to a transformer that has a 100 turn primary coil and 200 turn secondary coil.
What is the voltage across the secondary after the battery has been connected for a long time?
+
12 V

## Slide 21: Summary of today’s lecture
    Magnetic field B
Since , 3 things can change F
Faraday’s law: “Induced EMF” = rate of change of magnetic flux
    Area of loop
    Angle φ
v
10
20
t
B(t)
+1.0
-1.0
0
+0.5
-0.5
0
B
n
ω