## Slide 1: Phys 102 – Lecture 9
RC circuits

## Slide 2: Recall from last time...
We solved various circuits with resistors and batteries (also capacitors and batteries)
+
R3
R1
R2
ε
What about circuits that combine all three...
+
R3
ε2
ε1
+
R1
?
...RC circuits
+
R2
R1
ε
C

## Slide 3: RC circuits
Circuits that store and release energy controllably...
Camera flash
Defibrillator
Nerve cells

## Slide 4: Today we will...
Learn about RC circuits
  Charge on capacitors cannot change instantly,
  so behavior of RC circuit depends on time
Analyze RC circuits under different situations
  Charging capacitors at short/long times
  Discharging capacitors at short/long times
  Time dependence
Apply these concepts
  Nerve cells and nerve impulses (action potential)

## Slide 5: Charging capacitor
+
ε
I
R
S1
C
S2
Initially the capacitor is uncharged (Q0 = 0)
At t = 0 we close switch S1.
Immediately after:
Current I0 flows around loop, through C No charge on C (Q0 = 0)
After a long time (t = ):
Charge on C builds until VC = ε. Current decreases to zero (I = 0)
+Q
–Q

## Slide 6: ACT: CheckPoint 1.1
+
ε
2R
C
R
Both switches are initially open and the capacitor is uncharged. What is the current through light bulb 1 right after switch S1 is closed?
S1
S2
Ib = 0
Ib = ε/3R
Ib = ε/2R
Ib = ε/R
DEMO
1
2

## Slide 7: ACT: charging
+
ε
2R
C
R
Both switches are initially open and the capacitor is uncharged. What is the voltage across the capacitor a long time after switch S1 is closed?
S1
S2
VC = 0
VC = ε/2
VC = ε
VC = 2ε
DEMO
1
2

## Slide 8: Discharging capacitor
+
ε
R
S1
C
Initially the capacitor is fully charged (Q0 = Cε)
At t = 0 we close switch S2.
Immediately after:
Current I0 driven around loop, through C Charge on C from before (Q0 = Cε)
After a long time (t = ):
Charge on C dissipates until VC = 0. Current decreases to zero (I = 0)
S2

## Slide 9: ACT: CheckPoint 1.5
+
ε
2R
C
R
After S1 has been closed for a long time, it is opened and S2 is closed. What is the current through light bulb 2 right after S2 is closed?
S1
Ib = 0
Ib = ε/3R
Ib = ε/2R
Ib = ε/R
DEMO
1
2
S2

## Slide 10: ACT: RC circuit practice
+
ε
2R
C
R
Now both S1 and S2 are closed. What is the current through light bulb 2 a long time after both switches are closed?
S1
Ib = 0
Ib = ε/3R
Ib = ε/2R
Ib = ε/R
DEMO
1
2
S2

## Slide 11: Summary: charging & discharging
Charge (and therefore voltage, since VC = Q/C) on capacitors cannot change instantly
Short term behavior of capacitor:
  If the capacitor is charging, current I drives charge onto it, and Q increases (acts like a wire)
  If the capacitor is discharging, current I drives charge off of it, and Q decreases (acts like a battery)
Long term behavior of capacitor:
  If the capacitor is fully charged, I = 0 and Q is maximum (acts like an open circuit)
  If the capacitor is fully discharged, I = 0 and Q is minimum (acts like an open circuit)

## Slide 12: Nerve cell equivalent circuit
RCl
ICl
+
εCl
Vout
Vin
Neurons have ion channels (K+,Na+, and Cl–) that pump current into and out of cell (it is polarized). Cell membrane also has capacitance
Vout
Vin
Cm
RNa
+
εK
INa
IK
RK
+
εNa
S

## Slide 13: Action potential
At rest, Na+ channels in cell are closed. When stimulated, the cell’s voltage increases (depolarization). If a threshold is exceeded, the Na+ channels open & trigger a nerve impulse (action potential)
Cm
RNa
+
εK
INa
IK
RK
+
εNa
S

## Slide 14: ACT: Resting state of neuron
Cm
RNa
+
εK
RK
+
εNa
S
Vout
Vin
The neuron has been in resting state for a long time. What is the voltage across the membrane capacitance?
εK = 70 mV, εNa = 60 mV,
RK = 2 MΩ, RNa = 0.4 MΩ, Cm = 300 pF
VC > εK
VC = εK
VC < εK
+Q
–Q

## Slide 15: Calculation: action potential I
RNa
+
εK
RK
+
εNa
S
εK = 70 mV, εNa = 60 mV,
RK = 2 MΩ, RNa = 0.4 MΩ, Cm = 300 pF
Some time ago, the cell was stimulated and depolarized to –60 mV, less than threshold to open Na+ channels. What happens next?
Vout
Vin = –60 mV
Cm
Immediately after:
No current through Na+ channel
Current IK driven by K+ channel
Charge Q0 on Cm from VC = 60 mV
After a long time:
Current IK decays to 0
Charge on Cm returns to rest value
Vin = –70 mV

## Slide 16: RC circuit time dependence
+
ε
R
C
+Q
–Q
Q
I0
I0
Q0
Charging:
Discharging:
t
t
DEMO
Charge builds up:
Current decays:
Charge decays:
Q, I
Q, I
Current decays:
I
Note that RC has units of time!
R×C = [V]/[I] × [Q]/[V] = [Q]/[I] = [t]

## Slide 17: Myelinated nerve cells
Many neurodegenerative diseases (ex: MS) cause progressive de-myelination.
Action potentials propagate down nerve cell at rate determined by the cell’s RC time constant.
With very few exceptions (ex: C fibres) human neuron fibres are myelinated. Myelin reduces C, decreasing time constant & increasing propagation speed.
Notes: C fibres are not myelinated. They are called “pain fibres” and associated with “slow pain” response

## Slide 18: Calculation: action potential I
How long does the cell take to return to 90% of its resting voltage?
–60
–70
t (ms)
V (mV)
Take natural log of both sides:
0
“Failed initiation”
Stimulus
Resting state
Cell voltage Vin – Vout = –VC = –Q/C:

## Slide 19: Calculation: action potential II
RNa
+
εK
IK
RK
+
εNa
Vout
Cm
S
Now, the cell was stimulated and depolarized to –50 mV, over the threshold to open Na+ channels. What happens next?
Immediately after:
Current INa through Na+ channel
Current IK driven by K+ channel
Charge Q0 on Cm from before
Vin = –50 mV
εK = 70 mV, εNa = 60 mV,
RK = 2 MΩ, RNa = 0.4 MΩ, Cm = 300 pF
INa

## Slide 20: ACT: action potential II
All currents are 0
The currents IK = INa ≠ 0
Voltage across Cm is 0
A long time after stimulating the cell, which statement below holds TRUE?
RNa
+
εK
RK
+
εNa
Vout
Cm
S
Vin
εK = 70 mV, εNa = 60 mV,
RK = 2 MΩ, RNa = 0.4 MΩ, Cm = 300 pF

## Slide 21: Action potential summary
–55
–70
+40
0
t (ms)
V (mV)
Resting state
Threshold
“Failed initiation”
Action potential
If the stimulus exceeds –55 mV, the Na+ channels open, depolarize the cell & trigger an action potential.
Once a +40 mV potential is reached, the Na+ channels close again & the cell repolarizes to its resting potential.

## Slide 22: Summary of today’s lecture
Next week magnetism!
RC circuits depend on time
  Charge on capacitors cannot change instantly
Short/long times & charging/discharging
  t = 0: I flows Q onto/off of C, Q increases/decreases (charging/discharging)
  t = : I through C decays to 0, Q reaches maximum/minimum (charging/discharging)
  τ = RC: provides time to charge/discharge