## Slide 1: Accelerometers
LSM9DS1 9-axis accelerometer
Ritika, Juliana, Sneh, Brock

## Slide 2: Omg, what are these, 9 axes??
3-axis accelerometer
  Where’s gravity??
3-axis magnetometer
  B-field to find magnetic north
3-axis gyroscope
  Twist and spin detection
Wow! Now we get 9 degrees of freedom (plus temperature)

## Slide 3: How it works: Accelerometer
Measures “proper acceleration”
  Acceleration in its own rest frame
  Inertial frame guaranteed
Accelerometer on Earth’s surface measures 9.81 m/s^2 up
3D digital linear acceleration sensor
  Acceleration scale of ±2g/±4g/±8/±16 g

## Slide 4: How it works: Magnetometer
Measures magnetic fields, includes Earth’s
Can operate at 8 different refresh rates of: 0.625, 1.25, 2.5, 5, 10, 20, 40, or 80 Hz
Stores an internal 16-bit offset for each axis to compensate for effects from auxiliary magnetic fields
Can come from nearby metal objects and even parts of the accelerometer
Offers different calibration procedures to correct for this

## Slide 5: How it works: Gyroscope
3 axes
Measures spin & twist
±245/±500/±2000 dps ranges
Large range of sensitivity
Uses “Zero Rate Level” to calibrate and find deviations if no acceleration
  Want the lowest value possible

## Slide 6: Applications
Measuring orientation, movement
3D motion capture
Inverted pendulum devices
  Segway / Humans
Inertial guidance systems

## Slide 8: References
https://learn.adafruit.com/adafruit-lsm9ds1-accelerometer-plus-gyro-plus-magnetometer-9-dof-breakout
https://www.parallax.com/sites/default/files/downloads/28065-LSM9DS1-9-axis-IMU-Guide-v1.0.pdf